## Slide 1: JVET-R0233: AHG16: Line buffer problem of CC-ALF for 4:2:2 and 4:4:4 sequences
Nan Hu, Vadim Seregin, Marta Karczewicz

## Slide 2: ALF virtual boundary in VTM8
4 lines Luma and 2 line of chroma samples

## Slide 3: CCALF in VTM8
4:2:0
4:2:2/4:4:4

## Slide 4: CCALF in VTM8
Blue/red chroma samples:
  DB, SAO and ALF are done, ready for CC-ALF
Blue/red co-located luma samples:
  DB, SAO and ALF are pending on samples from lower CTB
Problem:
  Chroma samples wait for luma samples
  Store blue and red chroma samples as additional line buffers
4:2:2/4:4:4

## Slide 5: Method 1
Clip luma samples to the closest one above an ALF VB
4:4:4/4:2:2 | Y | U | V | EncT | DecT
AI | 0.00% | 0.00% | 0.01% | 100% | 100%
RA | 0.01% | -0.03% | 0.02% | 100% | 100%
LDB | 0.01% | -0.06% | 0.01% | 100% | 100%
LDP | -0.02% | -0.02% | -0.04% | 100% | 100%

## Slide 6: Method 2
When CC-ALF is applied to a chroma sample above a VB and its co-located luma sample is below the VB, CC-ALF is not applied to this chroma sample.
Skip
4:4:4/4:2:2 | Y | U | V | EncT | DecT
AI | 0.00% | 0.02% | 0.06% | 100% | 99%
RA | 0.02% | 0.04% | 0.11% | 100% | 100%
LDB | 0.00% | 0.03% | 0.08% | 100% | 100%
LDP | -0.06% | 0.00% | 0.04% | 100% | 99%
Thank Bytedance for crosschecking

## Slide 7: Method 3
For 4:2:2 and 4:4:4 sequences, the position of an ALF VB is changed into 4 chroma lines above a CTU boundary. Compared to VVC draft 8, line buffer increases by 2 lines of chroma samples for each chroma component.
Line buffer increases by 2 chroma lines in each chroma component
4:4:4/4:2:2 | Y | U | V | EncT | DecT
AI | 0.00% | -0.01% | -0.02% | 100% | 99%
RA | 0.00% | -0.06% | -0.03% | 100% | 101%
LDB | 0.01% | -0.07% | -0.05% | 100% | 101%
LDP | -0.02% | -0.04% | -0.13% | 100% | 101%
Thank Bytedance for crosschecking