## Slide 1: 4:4:4 vs. 4:2:0 Bit-rate in VTM
JVET-R0243
Advanced Technology Team
European Professional Engineering
Sony Europe
Steve Keating
Sony Corp.

## Slide 2: Introduction
In Annex A, Table A3 of the specification, the values of CpbVclFactor and CpbNalFactor for the Main 4:4:4 10 profile are defined to be x2.5 those of the Main 10 profile.
This contribution compares bit-rates to check if this ratio is reasonable.
Various 4:4:4 sequences were trial encoded with VTM8.0 and the (RA) bit-rates compared with their 4:2:0 versions (obtained using the HDR Tools functions):

## Slide 3: Bit-rates
 | Level | 420 kbps |  | 444 kbps |  | bitrate ratio |  |  | Level | 420 kbps |  | 444 kbps |  | bitrate ratio
Traffic_QP22 | 5 | 11807 |  | 22108 |  | 1.9 |  | Pool_QP22 | 4 | 17839 |  | 27142 |  | 1.5
Traffic_QP27 |  | 4716 |  | 7392 |  | 1.6 |  | Pool_QP27 |  | 7212 |  | 9688 |  | 1.3
Traffic_QP32 |  | 2273 |  | 3021 |  | 1.3 |  | Pool_QP32 |  | 2899 |  | 3545 |  | 1.2
Traffic_QP37 |  | 1164 |  | 1378 |  | 1.2 |  | Pool_QP37 |  | 1044 |  | 1201 |  | 1.2
BirdsInCage_QP22 | 4.1 | 3223 |  | 20728 |  | 6.4 |  | VenueVu_QP22 | 4 | 4841 |  | 5840 |  | 1.2
BirdsInCage_QP27 |  | 738 |  | 2697 |  | 3.7 |  | VenueVu_QP27 |  | 2382 |  | 2751 |  | 1.2
BirdsInCage_QP32 |  | 315 |  | 469 |  | 1.5 |  | VenueVu_QP32 |  | 1262 |  | 1396 |  | 1.1
BirdsInCage_QP37 |  | 166 |  | 199 |  | 1.2 |  | VenueVu_QP37 |  | 661 |  | 707 |  | 1.1
CrowdRun_QP22 | 4.1 | 45468 |  | 67343 |  | 1.5 |  | View_QP22 | 4 | 3473 |  | 12383 |  | 3.6
CrowdRun_QP27 |  | 19145 |  | 23703 |  | 1.2 |  | View_QP27 |  | 1070 |  | 2264 |  | 2.1
CrowdRun_QP32 |  | 8989 |  | 10306 |  | 1.1 |  | View_QP32 |  | 521 |  | 627 |  | 1.2
CrowdRun_QP37 |  | 4154 |  | 4591 |  | 1.1 |  | View_QP37 |  | 261 |  | 294 |  | 1.1
EBULupoCandlelight_QP22 | 4.1 | 3195 |  | 3486 |  | 1.1 |  | DucksAndLegs_QP22 | 4.1 | 34445 |  | 146278 |  | 4.2
EBULupoCandlelight_QP27 |  | 1437 |  | 1458 |  | 1.0 |  | DucksAndLegs_QP27 |  | 9857 |  | 26310 |  | 2.7
EBULupoCandlelight_QP32 |  | 733 |  | 725 |  | 1.0 |  | DucksAndLegs_QP32 |  | 4036 |  | 6679 |  | 1.7
EBULupoCandlelight_QP37 |  | 377 |  | 366 |  | 1.0 |  | DucksAndLegs_QP37 |  | 1946 |  | 2343 |  | 1.2
EBURainFruits_QP22 | 4.1 | 7647 |  | 8171 |  | 1.1 |  | OldTownCross_QP22 | 4.1 | 21846 |  | 65907 |  | 3.0
EBURainFruits_QP27 |  | 3625 |  | 3705 |  | 1.0 |  | OldTownCross_QP27 |  | 4231 |  | 10018 |  | 2.4
EBURainFruits_QP32 |  | 1820 |  | 1847 |  | 1.0 |  | OldTownCross_QP32 |  | 1279 |  | 1534 |  | 1.2
EBURainFruits_QP37 |  | 917 |  | 926 |  | 1.0 |  | OldTownCross_QP37 |  | 645 |  | 706 |  | 1.1
Ferns_QP22 | 4 | 7024 |  | 8876 |  | 1.3 |  | ParkScene_QP22 | 4 | 7445 |  | 16000 |  | 2.1
Ferns_QP27 |  | 2958 |  | 3244 |  | 1.1 |  | ParkScene_QP27 |  | 3067 |  | 4434 |  | 1.4
Ferns_QP32 |  | 1561 |  | 1626 |  | 1.0 |  | ParkScene_QP32 |  | 1358 |  | 1687 |  | 1.2
Ferns_QP37 |  | 859 |  | 852 |  | 1.0 |  | ParkScene_QP37 |  | 604 |  | 695 |  | 1.2
Genesis_QP22 | 4 | 3497 |  | 9131 |  | 2.6 |  | Seeking_QP22 | 4.1 | 30794 |  | 57520 |  | 1.9
Genesis_QP27 |  | 1354 |  | 2097 |  | 1.5 |  | Seeking_QP27 |  | 10270 |  | 14385 |  | 1.4
Genesis_QP32 |  | 696 |  | 791 |  | 1.1 |  | Seeking_QP32 |  | 4443 |  | 5250 |  | 1.2
Genesis_QP37 |  | 372 |  | 413 |  | 1.1 |  | Seeking_QP37 |  | 2052 |  | 2261 |  | 1.1
Kimono_QP22 | 4 | 5369 |  | 12519 |  | 2.3 |  |  |  |  |  |  |  | 
Kimono_QP27 |  | 2168 |  | 3346 |  | 1.5 |  |  |  |  |  |  |  | 
Kimono_QP32 |  | 1059 |  | 1258 |  | 1.2 |  |  |  |  |  |  |  | 
Kimono_QP37 |  | 516 |  | 579 |  | 1.1 |  |  |  |  |  |  |  | 

## Slide 4: Bit-rates
Some 4:4:4 sequences require significantly more than 2x bit-rate
This is generally at the lower QPs
Further investigation of these sequences showed that they had a lot of high frequency energy in the U channel
So the variance of the Y, U and V channels was calculated and compared:

## Slide 5: Bit-rates and Variance
 | 444 variance |  |  | bitrate ratio | U:Y var ratio | 
 | Y | U | V |  |  | QP
Traffic | 55 | 30 | 5 | 1.9 | 0.5 | 22
BirdsInCage | 27 | 72 | 16 | 6.4 | 2.7 | 22
CrowdRun | 350 | 72 | 54 | 1.5 | 0.2 | 22
EBULupoCandlelight | 44 | 4 | 2 | 1.1 | 0.1 | 22
EBURainFruits | 95 | 4 | 3 | 1.1 | 0.0 | 22
Ferns | 164 | 12 | 16 | 1.3 | 0.1 | 22
Genesis | 22 | 48 | 18 | 2.6 | 2.1 | 22
Kimono | 14 | 32 | 10 | 2.3 | 2.4 | 22
Pool | 74 | 35 | 40 | 1.5 | 0.5 | 22
VenueVu | 72 | 8 | 21 | 1.2 | 0.1 | 22
View | 32 | 59 | 26 | 3.6 | 1.8 | 22
DucksAndLegs | 85 | 266 | 72 | 4.2 | 3.1 | 22
OldTownCross | 112 | 111 | 59 | 3.0 | 1.0 | 22
ParkScene | 66 | 42 | 28 | 2.1 | 0.6 | 22
Seeking | 143 | 64 | 54 | 1.9 | 0.4 | 22
Chart: 444:420 bitrate ratio vs. U:Y variance ratio
| 0.54908424908424913 | 2.7152516904583019 | 0.20692806351200843 | 8.6068395685104424E-2 | 3.7711272414046655E-2 | 7.378089716203845E-2 | 2.1365461847389557 | 2.3723038678072674 | 0.46791957568869402 | 0.11754851319279631 | 1.8390399200973813 | 3.1317216981132074 | 0.98924288526937532 | 0.64067694167422173 | 0.44913064730116603
QP22 | 1.8724 | 6.431 | 1.4811 | 1.0911 | 1.0686 | 1.2637 | 2.6112 | 2.3315 | 1.5215 | 1.2064 | 3.5657 | 4.2467 | 3.0169 | 2.1492 | 1.8679
Examining U:Y variance ratio of the pictures shows a correlation with bitrate ratio.
  And the U:Y variance ratios seem to be higher than expected.

## Slide 6: Chroma Noise
RGB
Y
U
V

## Slide 7: Chroma Noise
Applying a horizontal 1,2,1 low-pass filter to the chroma reduces this noise
Brings the 4:4:4 bit-rate closer to 2x the 4:2:0 bit-rate
Chart: 444UfiltH:420 bitrate ratio vs. U:Y variance ratio
| 0.54908424908424913 | 2.7152516904583019 | 0.20692806351200843 | 8.6068395685104424E-2 | 3.7711272414046655E-2 | 7.378089716203845E-2 | 2.1365461847389557 | 2.3723038678072674 | 0.46791957568869402 | 0.11754851319279631 | 1.8390399200973813 | 3.1317216981132074 | 0.98924288526937532 | 0.64067694167422173 | 0.44913064730116603
QP22 | 1.6413 | 2.7926 | 1.3185 | 1.0613 | 1.0542 | 1.1935 | 1.7935 | 1.8961 | 1.4564 | 1.1878 | 2.3193 | 2.4838 | 1.9852 | 1.7757 | 1.5448
 | 444 variance |  |  | bitrate ratio | U:Y var ratio | 
 | Y | U | V |  |  | QP
Traffic | 55 | 30 | 5 | 1.6 | 0.5 | 22
BirdsInCage | 27 | 72 | 16 | 2.8 | 2.7 | 22
CrowdRun | 350 | 72 | 54 | 1.3 | 0.2 | 22
EBULupoCandlelight | 44 | 4 | 2 | 1.1 | 0.1 | 22
EBURainFruits | 95 | 4 | 3 | 1.1 | 0.0 | 22
Ferns | 164 | 12 | 16 | 1.2 | 0.1 | 22
Genesis | 22 | 48 | 18 | 1.8 | 2.1 | 22
Kimono | 14 | 32 | 10 | 1.9 | 2.4 | 22
Pool | 74 | 35 | 40 | 1.5 | 0.5 | 22
VenueVu | 72 | 8 | 21 | 1.2 | 0.1 | 22
View | 32 | 59 | 26 | 2.3 | 1.8 | 22
DucksAndLegs | 85 | 266 | 72 | 2.5 | 3.1 | 22
OldTownCross | 112 | 111 | 59 | 2.0 | 1.0 | 22
ParkScene | 66 | 42 | 28 | 1.8 | 0.6 | 22
Seeking | 143 | 64 | 54 | 1.5 | 0.4 | 22

## Slide 8: Conclusion
Main 4:4:4 10 profile can work with twice the bit-rate of Main 10 profile
  Provided that chroma noise is limited at the lower QPs
Note that contribution JVET-R0244 proposes changes to CpbVclFactor and MinCrScaleFactor for Main 4:4:4 10 profile.