## Slide 1: Level Coding in VVC
JVET-R0245
Advanced Technology Team
European Professional Engineering
Sony Europe
Steve Keating
Sony Corp.

## Slide 2: Background
In the current specification various levels are defined from 1 to 6.2 with the highest possible level being 8.5; the level is coded in 8 bits as Level*30, hence level 8.5 being coded as 255. There is also the condition:
  Decoders conforming to the *** profile at a specific level of a specific tier shall be capable of decoding all bitstreams for which all of the following conditions apply:
  …
  The bitstream is indicated to conform to a level that is not level 8.5 and is lower than or equal to the specified level.

## Slide 3: Background
This has some issues:
  It’s not possible to go beyond 120fps: only way is to use a level with a larger picture size
  The maximum level is 8.5, implying a maximum picture size of 32K
And
  The space that was added in HEVC (due to *30 factor) over AVC (which had a *10 factor) was not required, and much of that space in the mapping cannot be used.
 | JVET-Q2001-vE Table A.1 |  |  | JVET-Q2001-vE Table A.2 | 
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size |  | Max luma sample rate MaxLumaSr (samples/sec) | Max frame rate of max size MaxLumaSr/MaxLumaPs (frames/sec)
1 | 36,864 |  |  | 552,960 | 
2 | 122,880 |  |  | 3,686,400 | 
2.1 | 245,760 |  |  | 7,372,800 | 
3 | 552,960 |  |  | 16,588,800 | 
3.1 | 983,040 |  |  | 33,177,600 | 
4 | 2,228,224 | 2048x1088 |  | 66,846,720 | 30
4.1 | 2,228,224 | 2048x1088 |  | 133,693,440 | 60
5 | 8,912,896 | 4096x2176 |  | 267,386,880 | 30
5.1 | 8,912,896 | 4096x2176 |  | 534,773,760 | 60
5.2 | 8,912,896 | 4096x2176 |  | 1,069,547,520 | 120
6 | 35,651,584 | 8192x4352 |  | 1,069,547,520 | 30
6.1 | 35,651,584 | 8192x4352 |  | 2,139,095,040 | 60
6.2 | 35,651,584 | 8192x4352 |  | 4,278,190,080 | 120

## Slide 4: Proposal
Code the level in 8 bits as Major*16+Minor
  E.g. level 4.1 is coded as 65
  Maximum level is now 15.15
Modify constraint of decoding of levels:
  Decoders conforming to the *** profile at a specific level, D.d of a specific tier shall be capable of decoding all bitstreams for which all of the following conditions apply:
  …
  The bitstream is indicated to conform to a level S.s that is not level 15.15 and S is lower than or equal to D and S*2+s is lower than or equal to D*2+d..
  Allows higher frame rates without using a higher Major level (longer line buffers etc.)

## Slide 5: Example
A level 5.3 stream would be decodable by a level 6.1 decoder (5 is lower than or equal to 6 and 5*2+3 is lower than or equal to 6*2+1)
 | JVET-Q2001-vE Table A.1 |  |  | JVET-Q2001-vE Table A.2 | 
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size |  | Max luma sample rate MaxLumaSr (samples/sec) | Max frame rate of max size MaxLumaSr/MaxLumaPs (frames/sec)
1 | 36,864 |  |  | 552,960 | 
2 | 122,880 |  |  | 3,686,400 | 
2.1 | 245,760 |  |  | 7,372,800 | 
3 | 552,960 |  |  | 16,588,800 | 
3.1 | 983,040 |  |  | 33,177,600 | 
4 | 2,228,224 | 2048x1088 |  | 66,846,720 | 30
4.1 | 2,228,224 | 2048x1088 |  | 133,693,440 | 60
5 | 8,912,896 | 4096x2176 |  | 267,386,880 | 30
5.1 | 8,912,896 | 4096x2176 |  | 534,773,760 | 60
5.2 | 8,912,896 | 4096x2176 |  | 1,069,547,520 | 120
5.3 | 8,912,896 | 4096x2176 |  | 2,139,095,040 | 240
6 | 35,651,584 | 8192x4352 |  | 1,069,547,520 | 30
6.1 | 35,651,584 | 8192x4352 |  | 2,139,095,040 | 60
6.2 | 35,651,584 | 8192x4352 |  | 4,278,190,080 | 120

## Slide 6: Conclusion
New coding method increases maximum level from 8.5 to 15.15
Allows higher frame rates to be added without requiring all higher level decoders to be able to decode the increased sample rate