## Slide 1: Max. Luma Picture Size in VVC
JVET-R0246
Advanced Technology Team
European Professional Engineering
Sony Europe
Steve Keating
Sony Corp.

## Slide 2: Introduction
In Annex A, Table A1 specifies the maximum luma picture size for each level
These values are taken from HEVC which has a maximum block size of 64x64, but VVC has a maximum block size of 128x128

## Slide 3: Issue
Table A1
    Highlighted cells show picture sizes which are not multiples of 128x128
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size
1 | 36,864 | 192x192
2 | 122,880 | 384x320
2.1 | 245,760 | 640x384
3 | 552,960 | 960x576
3.1 | 983,040 | 1280x768
4 | 2,228,224 | 2048x1088
4.1 | 2,228,224 | 2048x1088
5 | 8,912,896 | 4096x2176
5.1 | 8,912,896 | 4096x2176
5.2 | 8,912,896 | 4096x2176
6 | 35,651,584 | 8192x4352
6.1 | 35,651,584 | 8192x4352
6.2 | 35,651,584 | 8192x4352

## Slide 4: Issue
It may be desirable for hardware design to be always able to process a complete CTU.
Even with VDPU it may be needed, as functions such as prediction or loop filtering will need to access data outside the VDPU, i.e. the pipeline might be a CTU pipeline (128x128) rather than a VDPU pipeline (64x64).

## Slide 5: Proposed Changes: option 1
Do nothing
  It’s not considered a problem

## Slide 6: Proposed Changes: option 2
Revise the Max Picture Sizes
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size
1 | 65,536 | 256x256
2 | 147,456 | 384x384
2.1 | 245,760 | 640x384
3 | 614,400 | 960x640
3.1 | 983,040 | 1280x768
4 | 2,359,296 | 2048x1152
4.1 | 2,359,296 | 2048x1152
5 | 8,912,896 | 4096x2176
5.1 | 8,912,896 | 4096x2176
5.2 | 8,912,896 | 4096x2176
6 | 35,651,584 | 8192x4352
6.1 | 35,651,584 | 8192x4352
6.2 | 35,651,584 | 8192x4352
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size
1 | 36,864 | 192x192
2 | 122,880 | 384x320
2.1 | 245,760 | 640x384
3 | 552,960 | 960x576
3.1 | 983,040 | 1280x768
4 | 2,228,224 | 2048x1088
4.1 | 2,228,224 | 2048x1088
5 | 8,912,896 | 4096x2176
5.1 | 8,912,896 | 4096x2176
5.2 | 8,912,896 | 4096x2176
6 | 35,651,584 | 8192x4352
6.1 | 35,651,584 | 8192x4352
6.2 | 35,651,584 | 8192x4352

## Slide 7: Proposed Changes: option 3
Restrict the Max Block Size
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size
1 | 36,864 | 192x192
2 | 122,880 | 384x320
2.1 | 245,760 | 640x384
3 | 552,960 | 960x576
3.1 | 983,040 | 1280x768
4 | 2,228,224 | 2048x1088
4.1 | 2,228,224 | 2048x1088
5 | 8,912,896 | 4096x2176
5.1 | 8,912,896 | 4096x2176
5.2 | 8,912,896 | 4096x2176
6 | 35,651,584 | 8192x4352
6.1 | 35,651,584 | 8192x4352
6.2 | 35,651,584 | 8192x4352
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size | Max CTU size
1 | 36,864 | 192x192 | 64x64
2 | 122,880 | 384x320 | 64x64
2.1 | 245,760 | 640x384 | 64x64
3 | 552,960 | 960x576 | 64x64
3.1 | 983,040 | 1280x768 | 64x64
4 | 2,228,224 | 2048x1088 | 64x64
4.1 | 2,228,224 | 2048x1088 | 64x64
5 | 8,912,896 | 4096x2176 | 128x128
5.1 | 8,912,896 | 4096x2176 | 128x128
5.2 | 8,912,896 | 4096x2176 | 128x128
6 | 35,651,584 | 8192x4352 | 128x128
6.1 | 35,651,584 | 8192x4352 | 128x128
6.2 | 35,651,584 | 8192x4352 | 128x128

## Slide 8: Proposed Changes: option 3
Restrict the Max Block Size
  This has some loss:
    Especially for larger image sizes
 | Over VTM8.0-Benchmark-VTM-JVET-M1010 |  |  |  |  | 
 | Y | U | V | YUV | EncT | DecT
Class A1 | 0.44% | 1.41% | 1.70% | 0.56% | 97% | 132%
Class A2 | 0.59% | 0.96% | 0.27% | 0.44% | 97% | 134%
Class B | 0.39% | 0.15% | 0.77% | 0.39% | 96% | 107%
Class C | 0.31% | 0.25% | 0.59% | 0.32% | 99% | 107%
Class E | 0.41% | 0.01% | 1.50% | 0.45% | 99% | 106%
Overall | 0.42% | 0.50% | 0.92% | 0.42% | 97% | 115%
Class D | 0.11% | 0.23% | 0.75% | 0.16% | 98% | 101%
Class F | -1.07% | -1.46% | -1.12% | -1.15% | 83% | 106%
Class TGM | -0.42% | -0.57% | -0.58% | -0.47% | 89% | 110%

## Slide 9: Proposed Changes: option 4
Combination
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size
1 | 36,864 | 192x192
2 | 122,880 | 384x320
2.1 | 245,760 | 640x384
3 | 552,960 | 960x576
3.1 | 983,040 | 1280x768
4 | 2,228,224 | 2048x1088
4.1 | 2,228,224 | 2048x1088
5 | 8,912,896 | 4096x2176
5.1 | 8,912,896 | 4096x2176
5.2 | 8,912,896 | 4096x2176
6 | 35,651,584 | 8192x4352
6.1 | 35,651,584 | 8192x4352
6.2 | 35,651,584 | 8192x4352
Level | Max luma picture size MaxLumaPs (samples) | Example max luma size | Max CTU size
1 | 36,864 | 192x192 | 64x64
2 | 122,880 | 384x320 | 64x64
2.1 | 245,760 | 640x384 | 128x128
3 | 614,400 | 960x640 | 128x128
3.1 | 983,040 | 1280x768 | 128x128
4 | 2,359,296 | 2048x1152 | 128x128
4.1 | 2,359,296 | 2048x1152 | 128x128
5 | 8,912,896 | 4096x2176 | 128x128
5.1 | 8,912,896 | 4096x2176 | 128x128
5.2 | 8,912,896 | 4096x2176 | 128x128
6 | 35,651,584 | 8192x4352 | 128x128
6.1 | 35,651,584 | 8192x4352 | 128x128
6.2 | 35,651,584 | 8192x4352 | 128x128

## Slide 10: Conclusion
If the maximum luma picture size is made to be an integer number of maximum sized blocks then this may be achieved by either:
  increasing the maximum picture size, or
  restricting the maximum block size for some levels, or
  a combination of these methods.