## Slide 1: AHG16: Cleanup MIP flag signaling (JVET-R0281)
Jin Heo, Hyeongmun Jang, Jangwon Choi, Jaehyun Lim, and Seung Hwan Kim

## Slide 2: Summary
Introduction
  MIP context model in VVC draft 8,
    Four contexts are used for MIP flag, depending on information and block shape from neighboring blocks (left and above)
Proposed method
  Remove unnecessary dependency from neighboring blocks for MIP flag context
  It could also remove line buffer storage for MIP flag
Syntax element | binIdx |  |  |  |  | 
 | 0 | 1 | 2 | 3 | 4 | >= 5
intra_mip_flag[ ][ ] | (Abs( Log2(cbWidth) − Log2(cbHeight) ) > 1) ? 3 : ( 0,1,2 ) | na | na | na | na | na
Syntax element | condL (Left check) | condA (Above check) | ctxSetIdx
intra_mip_flag[ x0 ][ y0 ] | intra_mip_flag[ xNbL ][ yNbL ] | intra_mip_flag[ xNbA ][ yNbA ] | 0

## Slide 3: Proposed methods
Method 1
  Not to consider the upper blocks, when the current CU is at the upper boundary of each CTU
Method 2
  Consider only the left blocks
Method 3
  Consider NO neighboring block

## Slide 4: Experimental Results
Method 1 AI and RA
Method 2 AI and RA

## Slide 5: Experimental Results
Method 3 AI and RA

## Slide 6: Conclusion
It is proposed to cleanup MIP flag signaling
  Remove unnecessary dependency from neighboring blocks for MIP flag context
  It could also remove line buffer storage for MIP flag