## Slide 1: JVET-R0292 Fixes for 4-tap interpolation filtering
K. Andersson, R. Ruoyang, Z. Zhang, J. Ström
Ericsson

## Slide 2: Summary
It is asserted that the current 4-tap interpolation filters which are used both for intra angular prediction and chroma motion compensation have significant phase misalignments compared to the ideal phases of the interpolation filters.
For ten of the interpolation filters the phase misalignments are as large as the expected phase differences between two interpolation filters of adjacent fractional positions.
This contribution proposes 4-tap interpolation filters that fixes the phase misalignments of the current 4-tap interpolation filters.

## Slide 3: VVC 4-tap filters

## Slide 4: Proposed 4-tap filters

## Slide 5: Individual filter responses 4-tap filters (1/32)

## Slide 6: Individual filter responses 4-tap filters (2/32)

## Slide 7: Individual filter responses 4-tap filters (3/32)

## Slide 8: Individual filter responses 4-tap filters (4/32)

## Slide 9: Individual filter responses 4-tap filters (5/32)

## Slide 10: Individual filter responses 4-tap filters (6/32)

## Slide 11: Individual filter responses 4-tap filters (7/32)

## Slide 12: Individual filter responses 4-tap filters (8/32)

## Slide 13: Individual filter responses 4-tap filters (9/32)

## Slide 14: Individual filter responses 4-tap filters (10/32)

## Slide 15: Individual filter responses 4-tap filters (11/32)

## Slide 16: Individual filter responses 4-tap filters (12/32)

## Slide 17: Individual filter responses 4-tap filters (13/32)

## Slide 18: Individual filter responses 4-tap filters (14/32)

## Slide 19: Individual filter responses 4-tap filters (15/32)

## Slide 20: Individual filter responses 4-tap filters (16/32)

## Slide 21: Further analysis of vvc and proposed filters
subpel | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16
VVC Mean energy | 0.97 | 0.94 | 0.89 | 0.85 | 0.83 | 0.82 | 0.80 | 0.78 | 0.77 | 0.77 | 0.74 | 0.72 | 0.69 | 0.66 | 0.65 | 0.64
Proposed Mean energy | 0.91 | 0.92 | 0.86 | 0.85 | 0.80 | 0.80 | 0.76 | 0.73 | 0.74 | 0.71 | 0.69 | 0.71 | 0.66 | 0.65 | 0.64 | 0.68
Average of mean energy for all filters is similar for proposal and VVC:
  Average of mean energy VVC: 0.78
  Average of mean energy Proposal: 0.76
Variation of mean energy is less for proposal than for VVC:
  Variation in mean energy = max mean energy - min mean energy
  Variation in mean energy VVC: 0.97-0.64=0.33
  Variation in mean energy Proposed: 0.92-0.64=0.28

## Slide 22: Objective performance
 | All intra Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,01% | 0,07% | -0,02% | 106% | 103%
Class A2 | -0,03% | -0,01% | -0,04% | 109% | 100%
Class B | -0,04% | -0,02% | 0,03% | 105% | 100%
Class C | -0,05% | -0,06% | -0,10% | 101% | 98%
Class E | -0,14% | -0,12% | -0,23% | 97% | 98%
Overall | -0,05% | -0,03% | -0,06% | 103% | 100%
Class D | -0,06% | -0,14% | -0,07% | 96% | 99%
Class F | -0,01% | -0,01% | -0,09% | 102% | 100%
 | Random access Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,00% | -0,07% | -0,11% | 113% | 102%
Class A2 | -0,01% | 0,05% | -0,08% | 112% | 102%
Class B | -0,02% | -0,09% | -0,06% | 102% | 100%
Class C | -0,06% | -0,08% | -0,35% | 93% | 102%
Class E |  |  |  |  | 
Overall | -0,02% | -0,05% | -0,15% | 103% | 101%
Class D | 0,02% | 0,10% | -0,06% | 92% | 99%
Class F | 0,02% | -0,23% | -0,12% | 97% | 98%
 | Low-delay B Over VTM-8.0 |  |  |  | 
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,03% | -0,05% | -0,26% | 115% | 100%
Class C | -0,12% | -0,45% | -0,30% | 110% | 100%
Class E | -0,22% | -0,29% | -0,36% | 103% | 101%
Overall | -0,11% | -0,24% | -0,30% | 110% | 100%
Class D | 0,04% | -1,04% | -0,30% | 92% | 101%
Class F | -0,02% | -0,31% | -0,65% | 105% | 100%
 | Random access Over VTM-8.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0,00% | -0,11% | -0,06% | 111% | 101%
Class A2 | -0,05% | 0,05% | 0,10% | 113% | 100%
Class B | -0,04% | -0,07% | 0,08% | 101% | 99%
Class C | -0,05% | -0,01% | -0,22% | 94% | 97%
Class E |  |  |  |  | 
Overall | -0,04% | -0,04% | -0,02% | 103% | 99%
Class D | 0,02% | -0,09% | -0,24% | 92% | 104%
Class F | 0,06% | -0,17% | -0,10% | 97% | 101%
 | Low-delay B Over VTM-8.0 |  |  |  | 
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,02% | 0,19% | -0,37% | 114% | 100%
Class C | -0,09% | -0,07% | 0,12% | 110% | 100%
Class E | -0,10% | -0,18% | 0,11% | 103% | 101%
Overall | -0,06% | 0,01% | -0,09% | 110% | 100%
Class D | -0,05% | -0,33% | -0,13% | 92% | 98%
Class F | -0,03% | 0,10% | -0,37% | 103% | 100%
Intra only
Both intra and inter

## Slide 23: Proposed modifications to VVC
Fractional sample position p | fC interpolation filter coefficients |  |  |  | fG interpolation filter coefficients |  |  | 
 | fC[ p ][ 0 ] | fC[ p ][ 1 ] | fC[ p ][ 2 ] | fC[ p ][ 3 ] | fG[ p ][ 0 ] | fG[ p ][ 1 ] | fG[ p ][ 2 ] | fG[ p ][ 3 ]
0 | 0 | 64 | 0 | 0 | 16 | 32 | 16 | 0
1 | 0 | 61 | 4 | -1 | 16 | 32 | 16 | 0
2 | -1 | 61 | 5 | -1 | 15 | 31 | 17 | 1
3 | -1 | 59 | 7 | -1 | 15 | 31 | 17 | 1
4 | −2 | 58 | 10 | −2 | 14 | 30 | 18 | 2
5 | -2 | 56 | 12 | -2 | 14 | 30 | 18 | 2
6 | -3 | 55 | 15 | -3 | 13 | 29 | 19 | 3
7 | -3 | 53 | 17 | -3 | 13 | 29 | 19 | 3
8 | -3 | 51 | 19 | -3 | 12 | 28 | 20 | 4
9 | -4 | 50 | 22 | -4 | 12 | 28 | 20 | 4
10 | -4 | 48 | 24 | -4 | 11 | 27 | 21 | 5
11 | -4 | 46 | 26 | -4 | 11 | 27 | 21 | 5
12 | -5 | 45 | 29 | -5 | 10 | 26 | 22 | 6
13 | -4 | 42 | 30 | -4 | 10 | 26 | 22 | 6
14 | -4 | 40 | 32 | -4 | 9 | 25 | 23 | 7
15 | -4 | 38 | 34 | -4 | 9 | 25 | 23 | 7
16 | -5 | 37 | 37 | -5 | 8 | 24 | 24 | 8
17 | -4 | 34 | 38 | -4 | 8 | 24 | 24 | 8
18 | -4 | 32 | 40 | -4 | 7 | 23 | 25 | 9
19 | -4 | 30 | 42 | -4 | 7 | 23 | 25 | 9
20 | -5 | 29 | 45 | -5 | 6 | 22 | 26 | 10
21 | -4 | 26 | 46 | -4 | 6 | 22 | 26 | 10
22 | -4 | 24 | 48 | -4 | 5 | 21 | 27 | 11
23 | -4 | 22 | 50 | -4 | 5 | 21 | 27 | 11
24 | -3 | 19 | 51 | -3 | 4 | 20 | 28 | 12
25 | -3 | 17 | 53 | -3 | 4 | 20 | 28 | 12
26 | -3 | 15 | 55 | -3 | 3 | 19 | 29 | 13
27 | -2 | 12 | 56 | -2 | 3 | 19 | 29 | 13
28 | −2 | 10 | 58 | −2 | 2 | 18 | 30 | 14
29 | -1 | 7 | 59 | -1 | 2 | 18 | 30 | 14
30 | -1 | 5 | 61 | -1 | 1 | 17 | 31 | 15
31 | -1 | 4 | 61 | 0 | 1 | 17 | 31 | 15
Table 25 – Specification of interpolation filter
coefficients fC and fG
Fractional sample position p | interpolation filter coefficients |  |  | 
 | fC[ p ][ 0 ] | fC[ p ][ 1 ] | fC[ p ][ 2 ] | fC[ p ][ 3 ]
1 | 0 | 61 | 4 | -1
2 | -1 | 61 | 5 | -1
3 | -1 | 59 | 7 | -1
4 | -2 | 58 | 10 | -2
5 | -2 | 56 | 12 | -2
6 | -3 | 55 | 15 | -3
7 | -3 | 53 | 17 | -3
8 | -3 | 51 | 19 | -3
9 | -4 | 50 | 22 | -4
10 | -4 | 48 | 24 | -4
11 | -4 | 46 | 26 | -4
12 | -5 | 45 | 29 | -5
13 | -4 | 42 | 30 | -4
14 | -4 | 40 | 32 | -4
15 | -4 | 38 | 34 | -4
16 | -5 | 37 | 37 | -5
17 | -4 | 34 | 38 | -4
18 | -4 | 32 | 40 | -4
19 | -4 | 30 | 42 | -4
20 | -5 | 29 | 45 | -5
21 | -4 | 26 | 46 | -4
22 | -4 | 24 | 48 | -4
23 | -4 | 22 | 50 | -4
24 | -3 | 19 | 51 | -3
25 | -3 | 17 | 53 | -3
26 | -3 | 15 | 55 | -3
27 | -2 | 12 | 56 | -2
28 | -2 | 10 | 58 | -2
29 | -1 | 7 | 59 | -1
30 | -1 | 5 | 61 | -1
31 | -1 | 4 | 61 | 0
Table 33 – Specification of the chroma interpolation
filter coefficients fC[ p ] for each 1/32 fractional sample
position p

## Slide 24: Conclusions
It has been shown that the phase delay responses of the current 4-tap interpolation filters have significant deviations from the ideal phase delay responses and that some of the filters also have the same phase delay at low frequency which is clearly incorrect.
We propose to adopt the fixes of filter coefficients for the 4-tap interpolation filters used for intra angular prediction and chroma motion compensation to VVC specification and software such that VVC has 4-tap interpolation filters with proper interpolation properties.
Thanks to HHI for cross-checking