## Slide 1
JVET-R0331 Cleanup of LFNST signaling
Xiaoyu Xiu, Yi-Wen Chen, Tsung-chuan Ma, Hong-Jheng Jhu, Xianglin Wang

## Slide 2: Introduction
In VVC draft 8, LFNST is only applied to luma in single-tree
  The presence of LFNST is conditioned on luma and chroma transform_skip_flag.
  Both luma and chroma coefficients are checked for LfnstDcOnly and LfnstZeroOutSigCoeffFlag.
  Leading to redundant LFNST signaling in single-tree
  LFNST is signaled at the end of CU
  Inverse transform cannot be invoked until the transform coefficients are parsed.
  Causing undesirable decoding latency

## Slide 3: Proposal
Method One
  For single-tree, only check luma coefficients when determining LfnstDcOnly, i.e., whether there is only DC coefficient for LFNST signaling
  Removing LFNST index signaling in single-tree

## Slide 4: Proposal
Method Two
  For single-tree, only check luma transform_skip_flag for LFNST index signaling.
  For single-tree, only check luma coefficients for determining LfnstDcOnly and LfnstZeroOutSigCoeffFlag.
  Move LFNST/MTS index signaling to the last LFNST TB
    For single-tree and luma dual-tree, the LFNST/MTS index is signaled after the luma TB; for the ISP mode, the indices are signaled after the last luma TB.
    For chroma dual-tree, the LFNST index is signaled after Cr TB.

## Slide 5: Proposal
Method Three
  Disable chroma LFNST in both single-tree and chroma dual-tree
  Move LFNST/MTS index signaling to the luma TB ; for the ISP mode, the indices are signaled after the last luma TB