## Slide 1: JVET-R0345: Unified primary transform kernel for ISP mode
Junyan Huo, Wenhan Qiao, Haixin Wang,
Yanzhuo Ma, Shuai Wan, Fuzheng Yang,
Yuanfang Yu, Yang Liu,
April. 2020

## Slide 2: Primary transform kernel for ISP mode
In VVC Draft
The primary transform kernels selection of ISP mode:
  When lfnst_idx == 0, the primary transform kernels may be DCT-2 or DST-7 which are selected according to width and height.
  When lfnst_idx == 1 or 2, the primary transform kernels are DCT-2.
Proposed method
Primary transform kernels of ISP mode are unified to DCT-2 whether LFNST is used or not

## Slide 3: Experimental results
 |  |  | All Intra |  | 
 |  |  | Over VTM-8.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01% | 0.09% | -0.09% | 99% | 101%
Class A2 | 0.05% | 0.06% | 0.10% | 100% | 101%
Class B | 0.06% | 0.15% | 0.18% | 99% | 100%
Class C | 0.05% | 0.12% | 0.05% | 99% | 99%
Class E | 0.15% | 0.24% | 0.32% | 99% | 98%
Overall | 0.06% | 0.13% | 0.12% | 99% | 100%
Class D | 0.04% | 0.09% | 0.05% | 99% | 99%
Class F | -0.04% | 0.06% | 0.00% | 101% | 102%
 |  |  | Random Access |  | 
 |  |  | Over VTM-8.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02% | 0.01% | -0.03% | 100% | 99%
Class A2 | 0.01% | 0.05% | 0.22% | 98% | 100%
Class B | 0.04% | 0.02% | 0.07% | 100% | 100%
Class C | 0.02% | 0.02% | 0.09% | 99% | 99%
Class E |  |  |  |  | 
Overall | 0.02% | 0.02% | 0.08% | 99% | 99%
Class D | 0.08% | 0.12% | 0.19% | 100% | 101%
Class F | 0.04% | 0.00% | 0.04% | 100% | 101%

## Slide 4: Spec text changes

## Slide 5: Conclusion
Proposed to use a unified primary transform kernel for ISP mode.
  DCT-2
Coding performance:
AI: 0.06% 0.13% 0.12%, 99% 100%
    RA: 0.02% 0.02% 0.08%, 99% 99%
  Complexity reduction of encoder and decoder with little loss.
Recommend to adopt into VVC.
Thanks crosschecking by Tencent.

## Slide 6
Thank you