## Slide 1: JVET-R350: MIP for all channels in the case of 4:4:4-chroma format and of single tree
Fraunhofer HHI

## Slide 2: OVERVIEW OF PROPOSAL
Proposed method:
  For 4:4:4-content and single tree, if luma component uses MIP mode and chroma-intra mode is DM-mode, also other two components use this MIP mode.
  No change for non-4:4:4 or non-single-tree case.
  No change in encoder search.
Relation to ACT:
  ACT works best for strong correlation between channels.
  If ACT is enabled on a block, chroma-intra mode has to be the DM-mode.
  Experimental results show gain of -1.81% / -1.28% for RGB-camera-content, AI/RA. RGB-camera-captured is intersection of MIP/ACT - relevant cases.
2

## Slide 3: ExperIMEntal results for Camera Capured Content
All Intra
Random Access
2
 | Y/G | U/B | V/R | enc time | dec time
YUV 4:4:4 | -0.25% | -0.23% | -0.22% | 100% | 102%
RGB 4:4:4 | -1.81% | -0.61% | -1.00% | 97% | 101%
 | Y/G | U/B | V/R | enc time | dec time
YUV 4:4:4 | -0.15% | -0.13% | -0.07% | 101% | 102%
RGB 4:4:4 | -1.28% | -0.38% | -0.55% | 100% | 103%

## Slide 4: ExperIMEntal results for Screen content, RGB
All Intra
Random Access
2
 | G | B | R | enc time | dec time
TGM 1080 | -0.05% | -0.05% | -0.03% | 100% | 101%
TGM 720 | -0.49% | -0.35% | -0.31% | 101% | 96%
Animation | -0.77% | -0.59% | -0.62% | 95% | 100%
Mixed | -0.81% | -0.74% | -0.65% | 99% | 99%
 | G | B | R | enc time | dec time
TGM 1080 | -0.03% | -0.01% | -0.03% | 99% | 93%
TGM 720 | -0.30% | -0.22% | -0.29% | 97% | 97%
Animation | -0.41% | -0.35% | -0.37% | 99% | 100%
Mixed | -0.81% | -0.63% | -0.59% | 99% | 101%

## Slide 5: ExperIMEntal results for Screen content, YUV
All Intra
Random Access
2
 | Y | U | V | enc time | dec time
TGM 1080 | -0.01% | -0.02% | -0.02% | 101% | 99%
TGM 720 | -0.08% | 0.01% | -0.04% | 101% | 100%
Animation | -0.19% | -0.09% | -0.19% | 99% | 100%
Mixed | -0.10% | -0.17% | -0.19% | 99% | 101%
 | Y | U | V | enc time | dec time
TGM 1080 | 0,04% | 0,03% | -0,01% | 101% | 104%
TGM 720 | -0,05% | 0,04% | -0,03% | 100% | 100%
Animation | -0,07% | -0,15% | -0,16% | 101% | 103%
Mixed | -0,14% | -0,15% | -0,26% | 101% | 97%