## Slide 1: High bit depths
JVET-R0351
Advanced Technology Team
European Professional Engineering
Sony Europe
Adrian Browne
Sony Corp.

## Slide 2: Introduction
This contribution presents VTM 8.0 performance at multiple bit depths
  8, 10, 12, 14 and 16 bits
Study aims:
  Test the correctness of VVC under currently defined profiles
    Does VVC achieve expected PSNR at very low / negative QP?
  Identify problems to be solved for potential future higher bit profiles
    Are changes similar to those in HEVC Range Extensions applicable to VVC?
      Extended precision flag
      High precision forward transform
    What other tools can benefit from higher precision?
      i.e. improve PSNR for 12, 14 and 16 bit depths

## Slide 3: Background – HEVC Range Extensions
HEVC Range Extensions introduced flag for higher numerical accuracy
  extended_precision_processing_flag in SPS
  Increases numerical accuracy from transform onwards
  If disabled, MAX_TR_DYNAMIC_RANGE = 15 bits + sign bit
  If enabled, MAX_TR_DYNAMIC_RANGE = max(15, bitDepth + 6) bits + sign bit
Higher precision forward transforms in HM
  14 bit rather than standard 6 bit
  Non-normative as inverse transform in decoder is unchanged
  Achieved PSNR gains at QP’=4 over HM with standard 6 bit transforms
    1.03dB at 10 bit, 8.77dB at 12 bit, 19.74dB at 14 bit

## Slide 4: Background – HM16.21
Without extended precision,
16 bit processing overflows at
lowest QPs
With extended precision,16 bit
processing no longer overflows at
lowest QPs but does not perform
any better than 12 bit
With high precision forward transforms,
12, 14 and 16 bit achieve higher PSNRs

## Slide 5: Implementation – VTM 8.0
VTM 8.0 has inherited the following from HM (not in VVC spec)
  RExt__HIGH_BIT_DEPTH_SUPPORT pre-processor directive
    Enables different data types for high bit depth processing
    When enabled VTM 8.0 will not compile (Patch ready for merge request)
  RExt__HIGH_BIT_PRECISION_FORWARD_TRANSFORM directive
    Data structure for different forward and inverse transforms exists
      In VTM8.0 both forward and inverse transforms are identical and 6 bit
      Introduced 14 bit forward transforms in encoder, 6 bit inverse transform unchanged
        DCT2, DCT8 and DST7
  Extended precision flag in SPS
    When enabled problems in multiple tools identified
      ALF, BCW, BIO (Patch ready for merge request)

## Slide 6: Results – VTM 8.0
Without extended precision,
16 bit processing overflows at
lowest QPs in VTM 8.0, and never
exceeds 14 bit PSNR.
With extended precision enabled,
16 bit processing no longer
overflows at lowest QPs but does
not perform any better than 14 bit
With high precision forward transforms,
12, 14 and 16 bit achieve higher PSNRs.
All bit depths achieve theoretical maximum
Indicating encoding is approaching lossless.

## Slide 7: Proposals
The extended precision flag is kept in VTM
  Currently contained in SPS within RExt structure
  At risk as RExt structure in PPS removed from VTM 8.0
  Allows investigation of tools and techniques beyond version 1 profiles
The bug fixes reported in the submission are adopted
  A merge request will be made when required
  None of the changes requires a specification change
If / when work commences on version 2 of VVC
  Higher bit depths up to 16 bit are studied
    Application areas include
      medical images (16 bits)
      camera capture (12/14 bit)
    Increasing the reach of VVC