## Slide 1: JVET-R0380 Scaling list for adaptive colour transform
NHK and InterDigital

## Slide 2
Overview of discussion
There is the general opinion that such a mechanism would be useful, as the charcteristics of RGB and YCgCo in the spatial domain are probably different.
Solution 3 seems to be more appropriate, as the characteristics of LFNST and ACT are probably different, and the additional flag would only be relevant in a 4:4:4 profile.
It is asked if it is more appropriate to switch off the scaling matrices for RGB coded blocks rather than YCgCo?
Would it be better to design the scaling matrices for the YCgCo and disable for the RGB coded blocks?
Revisit: Numbers of frequency of usage, then decide which of the two solutions (enabling or disabling) would be better.
 Have checked the frequency of the usage of ACT for 4:4:4 RGB sequences
This contribution originally proposed to disable scaling matrix for the blocks coded with ACT
Meeting note d8:

## Slide 3
Pixel usage of ACT for 444 RGB sequences
Test sequence | QP | RGB vs YCC | 
S01 Traffic | 22 | 67% | 33%
 | 27 | 41% | 59%
 | 32 | 18% | 82%
 | 37 | 11% | 89%
S02 Kimono1 | 22 | 94% | 6%
 | 27 | 32% | 68%
 | 32 | 11% | 89%
 | 37 | 8% | 92%
S03 EBULupoCandlelight | 22 | 58% | 42%
 | 27 | 15% | 85%
 | 32 | 7% | 93%
 | 37 | 9% | 91%
S04 EBURainFruits | 22 | 3% | 97%
 | 27 | 2% | 98%
 | 32 | 4% | 96%
 | 37 | 7% | 93%
Test sequence | QP | RGB vs YCC | 
S05 VenueVu | 22 | 13% | 87%
 | 27 | 12% | 88%
 | 32 | 14% | 86%
 | 37 | 18% | 82%
S06 DucksAndLegs | 22 | 96% | 4%
 | 27 | 76% | 24%
 | 32 | 29% | 71%
 | 37 | 12% | 88%
S07 OldTownCross | 22 | 98% | 2%
 | 27 | 81% | 19%
 | 32 | 30% | 70%
 | 37 | 16% | 84%
S08 ParkScene | 22 | 93% | 7%
 | 27 | 44% | 56%
 | 32 | 17% | 83%
 | 37 | 12% | 88%
RandomAccess, R0468 bitstream (VTM-8.0 with MR1488,MR1492, DualITree=0)

## Slide 4
Solution 3-1 (originally Solution #3)
cu_act_enabled ?
sps_scaling_matrix_
for_act_disable_flag
Apply user defined scaling list
Apply flat quant matrix (=16)
seq_parameter_set_rbsp( ) { | Descriptor
... | 
sps_explicit_scaling_list_enabled_flag | u(1)
sps_act_enabled_flag | u(1)
if ( sps_act_enabled_flag && sps_explicit_scaling_list_enabled_flag ) | 
sps_scaling_matrix_for_act_disabled_flag | u(1)
Yes
Yes
No
No

## Slide 5
Solution 3-1
sps_scaling_matrix_for_act_disabled_flag equal to 1 specifies that scaling matrices are not applied to blocks coded with ACT. sps_scaling_matrix_for_act_disabled_flag equal to 0 specifies that the scaling matrices may be applied to the blocks coded with ACT. When not present, the value of scaling_matrix_for_act_disabled_flag is inferred to be equal to 1.
The intermediate scaling factor m[ x ][ y ] is derived as follows:
  If one or more of the following conditions are true, m[ x ][ y ] is set equal to 16:
    slice_explicit_scaling_list_used_flag is equal to 0.
    transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 1.
    scaling_matrix_for_lfnst_disabled_flag is equal to 1 and ApplyLfnstFlag is equal to 1.
    sps_scaling_matrix_for_act_disabled_flag is equal to 1 and cu_act_enabled_flag[ xTbY ][ yTbY ] is equal to 1.
Semantics change
Decoding process change

## Slide 6
Solution 3-2
cu_act_enabled ?
Apply flat quant matrix (=16)
Apply user defined scaling list
seq_parameter_set_rbsp( ) { | Descriptor
... | 
sps_explicit_scaling_list_enabled_flag | u(1)
sps_act_enabled_flag | u(1)
if ( sps_act_enabled_flag && sps_explicit_scaling_list_enabled_flag ) | 
sps_scaling_matrix_for_non_act_disabled_flag | u(1)
Yes
Yes
No
sps_scaling_matrix_
for_non_act_disabled_flag
No

## Slide 7
Solution 3-2
sps_scaling_matrix_for_non_act_disabled_flag equal to 1 specifies that scaling matrices are not applied to blocks coded without ACT. sps_scaling_matrix_for_non_act_disabled_flag equal to 0 specifies that the scaling matrices may be applied to the blocks coded without ACT. When not present, the value of scaling_matrix_for_act_disabled_flag is inferred to be equal to 1.
The intermediate scaling factor m[ x ][ y ] is derived as follows:
  If one or more of the following conditions are true, m[ x ][ y ] is set equal to 16:
    slice_explicit_scaling_list_used_flag is equal to 0.
    transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 1.
    scaling_matrix_for_lfnst_disabled_flag is equal to 1 and ApplyLfnstFlag is equal to 1.
    sps_scaling_matrix_for_non_act_disabled_flag is equal to 1 and cu_act_enabled_flag[ xTbY ][ yTbY ] is equal to 0.
Semantics change
Decoding process change

## Slide 8
Solution 3-3
sps_scaling_matrix_for_alternative_
colour_space_disabled_flag
Apply flat quant matrix (=16)
Apply user defined scaling list
seq_parameter_set_rbsp( ) { | Descriptor
... | 
sps_explicit_scaling_list_enabled_flag | u(1)
sps_act_enabled_flag | u(1)
if ( sps_act_enabled_flag && sps_explicit_scaling_list_enabled_flag ) | 
sps_scaling_matrix_for_alternative_colour_space_disabled_flag | u(1)
if ( sps_scaling_matrix_for_alternative_colour_space_disabled_flag ) | )
sps_scaling_matrix_designate_rgb_flag | u(1)
No
Yes
sps_scaling_list_designate_rgb_flag
== cu_act_enabled_flag
Yes
No
Scaling list | ACT on (YCC) | ACT off (RGB)
Designed for RGB | X | O
Designed for YCC | O | X

## Slide 9
Solution 3-3
sps_scaling_matrix_for_alternative_colour_space_disabled_flag equal to 1 specifies that scaling matrices are not applied to blocks when the colour space of the blocks is not equal to the designated colour space of scaling matrix. sps_scaling_matrix_for_alternative_colour_space_disabled_flag equal to 0 specifies that scaling matrices are applied to the blocks whether or not the colour space of the blocks is equal to the designated colour space of scaling matrix. When not present, the value of sps_scaling_matrix_for_alternative_colour_space_disabled_flag is inferred to be equal to 0.
sps_scaling_list_designate_rgb_flag equal to 1 specifies that the designated colour space of scaling matrices is RGB. sps_scaling_list_designate_rgb_flag equal to 0 specifies that the designated colour space of scaling matrices is YCgCo. When not present, the value of sps_scaling_list_designate_rgb_flag is inferred to be equal to 1.
The intermediate scaling factor m[ x ][ y ] is derived as follows:
  If one or more of the following conditions are true, m[ x ][ y ] is set equal to 16:
    slice_explicit_scaling_list_used_flag is equal to 0.
    transform_skip_flag[ xTbY ][ yTbY ][ cIdx ] is equal to 1.
    scaling_matrix_for_lfnst_disabled_flag is equal to 1 and ApplyLfnstFlag is equal to 1.
    sps_scaling_matrix_for_alternative_colour_space_disabled_flag is equal to 1 and sps_scaling_list_designe_rgb_flag is equal to cu_act_enabled_flag[ xTbY ][ yTbY ].
Decoding process change

## Slide 11
Pixel usage of ACT for 444 RGB sequences
Test sequence | QP | No-residual | RGB | YCC | RGB vs YCC | 
S01 Traffic | 22 | 24% | 51% | 25% | 67% | 33%
 | 27 | 78% | 9% | 13% | 41% | 59%
 | 32 | 90% | 2% | 8% | 18% | 82%
 | 37 | 94% | 1% | 5% | 11% | 89%
S02 Kimono1 | 22 | 13% | 82% | 6% | 94% | 6%
 | 27 | 61% | 12% | 26% | 32% | 68%
 | 32 | 76% | 3% | 22% | 11% | 89%
 | 37 | 84% | 1% | 15% | 8% | 92%
S03 EBULupoCandlelight | 22 | 55% | 26% | 19% | 58% | 42%
 | 27 | 85% | 2% | 13% | 15% | 85%
 | 32 | 91% | 1% | 9% | 7% | 93%
 | 37 | 93% | 1% | 6% | 9% | 91%
S04 EBURainFruits | 22 | 46% | 1% | 53% | 3% | 97%
 | 27 | 70% | 1% | 29% | 2% | 98%
 | 32 | 86% | 1% | 13% | 4% | 96%
 | 37 | 92% | 1% | 7% | 7% | 93%
Test sequence | QP | No-residual | RGB | YCC | RGB vs YCC | 
S05 VenueVu | 22 | 57% | 6% | 37% | 13% | 87%
 | 27 | 68% | 4% | 28% | 12% | 88%
 | 32 | 75% | 3% | 22% | 14% | 86%
 | 37 | 80% | 4% | 16% | 18% | 82%
S06 DucksAndLegs | 22 | 3% | 93% | 4% | 96% | 4%
 | 27 | 32% | 52% | 16% | 76% | 24%
 | 32 | 66% | 10% | 24% | 29% | 71%
 | 37 | 76% | 3% | 21% | 12% | 88%
S07 OldTownCross | 22 | 3% | 95% | 2% | 98% | 2%
 | 27 | 62% | 31% | 7% | 81% | 19%
 | 32 | 93% | 2% | 5% | 30% | 70%
 | 37 | 96% | 1% | 3% | 16% | 84%
S08 ParkScene | 22 | 12% | 81% | 6% | 93% | 7%
 | 27 | 78% | 10% | 12% | 44% | 56%
 | 32 | 90% | 2% | 9% | 17% | 83%
 | 37 | 93% | 1% | 6% | 12% | 88%
RandomAccess, R0468 bitstream (VTM-8.0 with MR1488,MR1492, DualITree=0)