## Slide 1
JVET-R0483
AHG9: Combination of JVET-R0049 and JVET-R0271
2020/4/21

## Slide 2
Combination 1: method 1 of R0049 + variation 2 of R0271
seq_parameter_set_rbsp( ) { | Descriptor
sps_seq_parameter_set_id | u(4)
sps_video_parameter_set_id | u(4)
….. | 
sps_transform_skip_enabled_flag | u(1)
if( sps_transform_skip_enabled_flag ) { | 
log2_transform_skip_max_size_minus2 | ue(v)
sps_bdpcm_enabled_flag | u(1)
sps_ts_residual_coding_disabled_slice_present_flag | u(1)
} | 
…. | 
} | 
slice_header( ) { | Descriptor
… | 
if (sps_ts_residual_coding_disabled_slice_present_flag ) | 
slice_ts_residual_coding_disabled_flag | u(1)
if( sps_dep_quant_enabled_flag && !slice_ts_residual_coding_disabled_flag ) | 
slice_dep_quant_enabled_flag | u(1)
if( sps_sign_data_hiding_enabled_flag && !slice_dep_quant_enabled_flag && !slice_ts_residual_coding_disabled_flag ) | 
slice_sign_data_hiding_enabled_flag | u(1)
if( ph_lmcs_enabled_flag ) | 
slice_lmcs_enabled_flag | u(1)
if( ph_explicit_scaling_list_enabled_flag ) | 
slice_explicit_scaling_list_used_flag | u(1)
… | 
} | 
Use case | sps_TS_enabled | sps_tsrc_disable_present | sh_tsrc_disable_flag | ( sh_SDH ¦¦ sh_DQ ) | Number of SH bits
TS disabled | 0 | x (0 inferred) | x (0 inferred) | 0/1 | 1
Lossy in CLVS | 1 | 0 | x (0 inferred) | 0/1 | 1*
lossless in CLVS** | 1 | 1 | 1 | x (0 inferred) | 1
Mixed LL lossy Slices | 1 | 1 | 0 | 0/1 | 2
Mixed LL lossless Slices | 1 | 1 | 1 | x (0 inferred) | 1
RRC only | 1 | 1 | 1 | x (0 inferred) | 1
** is lossless CTC
* some experts disagreed.

## Slide 3
Combination 2: method 1 of R0049 + variation 3 of R0271
seq_parameter_set_rbsp( ) { | Descriptor
sps_seq_parameter_set_id | u(4)
sps_video_parameter_set_id | u(4)
….. | 
sps_transform_skip_enabled_flag | u(1)
if( sps_transform_skip_enabled_flag ) { | 
log2_transform_skip_max_size_minus2 | ue(v)
sps_bdpcm_enabled_flag | u(1)
sps_ts_residual_coding_disabled_slice_present_flag | u(1)
} | 
…. | 
} | 
slice_header( ) { | Descriptor
… | 
if( sps_dep_quant_enabled_flag ) | 
slice_dep_quant_enabled_flag | u(1)
if( sps_sign_data_hiding_enabled_flag && !slice_dep_quant_enabled_flag ) | 
slice_sign_data_hiding_enabled_flag | u(1)
if( sps_ts_residual_coding_disabled_slice_present_flag && !slice_dep_quant_enabled_flag && ! slice_sign_data_hiding_enabled_flag ) | 
slice_ts_residual_coding_disabled_flag | u(1)
if( ph_lmcs_enabled_flag ) | 
slice_lmcs_enabled_flag | u(1)
if( ph_explicit_scaling_list_enabled_flag ) | 
slice_explicit_scaling_list_used_flag | u(1)
if( NumEntryPoints > 0 ) { | 
… | 
} | 
Use case | sps_TS_enabled | sps_tsrc_disable_present | ( sh_SDH ¦¦ sh_DQ ) | sh_tsrc_disable_flag | Number of SH bits
TS disabled | 0 | x (0 inferred) | 0/1 | x (0 inferred) | 1
Lossy in CLVS | 1 | 0 | 0/1 | x (0 inferred) | 1
lossless in CLVS** | 1 | 1 | x (0 inferred) | 1 | 1
Mixed LL lossy Slices | 1 | 1 | 1 | x (0 inferred) | 1
Mixed LL lossless Slices | 1 | 1 | 0 | 1 | 2
RRC only | 1 | 1 | x (0 inferred) | 1 | 1
** is lossless CTC

## Slide 4
Combination 3: method 3 of R0049 + variation 2 of R0271
slice_header( ) { | Descriptor
… | 
if (sps_transform_skip_enabled_flag ) | 
slice_ts_residual_coding_disabled_flag | u(1)
if( sps_dep_quant_enabled_flag && !slice_ts_residual_coding_disabled_flag ) | 
slice_dep_quant_enabled_flag | u(1)
if( sps_sign_data_hiding_enabled_flag && !slice_dep_quant_enabled_flag && !slice_ts_residual_coding_disabled_flag ) | 
slice_sign_data_hiding_enabled_flag | u(1)
if( ph_lmcs_enabled_flag ) | 
slice_lmcs_enabled_flag | u(1)
if( ph_explicit_scaling_list_enabled_flag ) | 
slice_explicit_scaling_list_used_flag | u(1)
… | 
} | 
Use case | sps_TS_enabled | sh_tsrc_disable_flag | ( sh_SDH ¦¦ sh_DQ ) | Number of SH bits
TS disabled | 0 | x (0 inferred)) | 0/1 | 1
Lossy in CLVS | 1 | 0 | 0/1 | 2
lossless in CLVS** | 1 | 1 | x (0 inferred)) | 1
Mixed LL lossy Slices | 1 | 0 | 0/1 | 2
Mixed LL lossless Slices | 1 | 1 | x (0 inferred)) | 1
RRC only | 1 | 1 | x (0 inferred)) | 1
** is lossless CTC

## Slide 5
Combination 4: method 3 of R0049 + variation 3 of R0271
slice_header( ) { | Descriptor
… | 
if( sps_dep_quant_enabled_flag ) | 
slice_dep_quant_enabled_flag | u(1)
if( sps_sign_data_hiding_enabled_flag && !slice_dep_quant_enabled_flag ) | 
slice_sign_data_hiding_enabled_flag | u(1)
if(sps_transform_skip_enabled_flag && !slice_dep_quant_enabled_flag && ! slice_sign_data_hiding_enabled_flag ) | 
slice_ts_residual_coding_disabled_flag | u(1)
if( ph_lmcs_enabled_flag ) | 
slice_lmcs_enabled_flag | u(1)
if( ph_explicit_scaling_list_enabled_flag ) | 
slice_explicit_scaling_list_used_flag | u(1)
if( NumEntryPoints > 0 ) { | 
… | 
} | 
 | sps_TS_enabled | ( sh_SDH ¦¦ sh_DQ ) | sh_tsrc_disable_flag | Number of SH bits
TS disabled | 0 | 0/1 | x (0 inferred) | 1
Lossy in CLVS | 1 | 0/1 | 0/x (0 inferred) | 1*
lossless in CLVS** | 1 | x (0 inferred) | 1 | 1
Mixed LL lossy Slices | 1 | 1 | x (0 inferred) | 1
Mixed LL lossless Slices | 1 | 0 | 1 | 2
RRC only | 1 | x (0 inferred) | 1 | 1
** is lossless CTC
* some experts disagreed.

## Slide 6
 | Number of bits in SH |  |  | 
 | Combination 1: Method 1 + variation 2 | Combination 2: Method 1 + variation 3 | Combination 3: Method 3 + variation 2 | Combination 4: Method 3 + variation 3
TS disabled | 1 | 1 | 1 | 1
Lossy in CLVS | 1* | 1 | 2 | 1*
lossless in CLVS | 1 | 1 | 1 | 1
Mixed LL lossy Slices | 2 | 1 | 2 | 1
Mixed LL lossless Slices | 1 | 2 | 1 | 2
RRC only | 1 | 1 | 1 | 1
*some experts disagreed.
Combination 1 and combination 2 require additional sps flag.
For SCC combinations 1 and 2 have 1 SH saving for lossless.