## Slide 1: EE1.1: A Comparison of Depthwise Separable Convolution and Regular Convolution with the JVET-T0057 Neural Network-based In-loop Filter
Cheung Auyeung, Wei Wang, Wei Jiang, Xiang Li, Shan Liu
Jan 6, 2021
JVET-U0060

## Slide 2: Regular Convolution in Pytorch

## Slide 3: Depthwise Separable Convolution in Pytorch
Depthwise Convolution
Pointwise Convolution

## Slide 4: DRNLF from JVET-T0057
Pre-Processing
Post-Processing
Deblocked
Picture
in YUV420
Format
QP Map
QP Map Quantizer
Filtered
Picture
in YUV420
Format
Take a patch from inputs until all inputs are processed
Process each patch by DRNLF kernel
Reassemble output patches as output picture
Picture
in YUV444
Format
Picture
in YUV444
Format
Main Processing

## Slide 5: DRNLF Kernel in JVET-T0057
CONV 3x3xM
CONV 3x3xM
DSC 3x3xM
ReLU
DSC 3x3xM
Conv 1x1xM
DSC 3x3xM
ReLU
DSC 3x3xM
Conv 1x1xM
DSC 3x3xM
ReLU
DSC 3x3xM
Conv 1x1xM
DSC 3x3xM
ReLU
DSC 3x3xM
…
NxDRU
QP Map Patch
*
+
*
-
*
1/1023
YUV444 Patch
DIV2K
Mean
1/51
1023
DIV2K
Mean
A DRU with DSC
DSC to be replaced by RC

## Slide 6: Network Information in Training State for DSC and RC
Network Information in Training Stage |  | 
Mandatory | GPU Type | Nvidia DGX station (2x Intel Xeon E5-2698 v4 2.2 GHz x 20, 256GB RAM and 4x 32GB Tesla V100)
 | Framework: | PyTorch v0.4.1
 | Number of GPUs per Task | 2x Tesla V100 was used for training
 | Epoch: | 300
 | Batch size: | 16
 | Training time: | 24h
 | Training data information: | DIV2K(compressed images and corresponding uncompressed images)
 | Training configurations for generating compressed training data (if different to VTM CTC): | QP = 22, 27, 32, 37
Optional |  | 
 | Number of iterations | 
 | Patch size | 64x64
 | Learning rate: | 2.00E-05
 | Optimizer: | ADAM
 | Loss function: | L1
 | Preprocessing: | randomly cropped and rotated
 | Other information: | 

## Slide 7: Network Information in Inference Stage
Network Information in Inference Stage |  | 
Mandatory | HW environment: | 
 | GPU Type | Intel(R) Xeon(R) CPU E5-2620 v3 (CPU only)
 | Framework: | Pytorch 1.2.0
 | Number of GPUs per Task | 0
 | Total Parameter Number | 22371
 | Parameter Precision (Bits) F | 32
 | Memory Parameter (MB) | 0.085338593
 | MAC (Giga) | 186.64 G per 3840x2160 pixels
Optional |  | 
 | Total Conv. Layers | 13
 | Total FC Layers | 0
 | Total Memory (MB) | 
 | Batch size: | 1
 | Patch size | 
 | Changes to network configuration or weights required to generate rate points | (e.g. )
 | Peak Memory Usage | 
 | Other information: | 
Network Information in Inference Stage |  | 
Mandatory | HW environment: | 
 | GPU Type | Intel(R) Xeon(R) CPU E5-2620 v3 (CPU only)
 | Framework: | Pytorch 1.2.0
 | Number of GPUs per Task | 0
 | Total Parameter Number | 77443
 | Parameter Precision (Bits) F | 32
 | Memory Parameter (MB) | 0.2954216
 | MAC (Giga) | 643.43 G per 3840x2160 pixels
Optional |  | 
 | Total Conv. Layers | 13
 | Total FC Layers | 0
 | Total Memory (MB) | 
 | Batch size: | 1
 | Patch size | 
 | Changes to network configuration or weights required to generate rate points | (e.g. )
 | Peak Memory Usage | 
 | Other information: | 
DSC
RC

## Slide 8: Results

## Slide 9: Results
DecT
Y-BDR