## Slide 1
JVET-U0063
A constraint of max transform size for high bit depth
Kenji Kondo, Masaru Ikeda (Sony)

## Slide 2: Summary
Introduce an issue
  A large transformation increases a cost of hardware.
Proposed solution
  A constraint to restrict max transform size to 32.
Experiment
  Log2MaxTbSize : 5
Conclusion
  Small impact BD-rate
  Propose the above constraint

## Slide 3: Issue: Storage cost for large transform and high bit depth
Need buffers corresponding to max size of transform.
  For high bit depth, the memory size more increases.
Related topics
  Low QPs for high bit depth coding
    To keep high quality for HBD content, low QPs are used as a HBD CTC.
    At low QPs range, small coding loss is expected even without large transform.
  64-point transform
    Max size of transform in VVC
    A technique, zero-out is used.
Dequantization
Vertical Transform
Horizontal Transform
CABAC
Mem.
3
Mem.
2
Reconstruct
1
32x64
64x64
32x32

## Slide 4: Complexity analysis (memory 2)
Cases
  VVC v1
    10-bit input
      32 x 64 x 16 bit (+0%)
  VVC v2
    16-bit input
      32 x 64 x 23 bit (+43%) Additional cost to use 64-point transform and HBD.
    12-bit input
      32 x 64 x 16 bit (+0%)
  VVC v2 + constraint (sps_max_luma_transform_size_64_flag = 0)
    16-bit input
      32 x 32 x 23 bit (-28%)
    12-bit input
      32 x 32 x 16 bit (-50%)
HEVC spec:
extended_precision_processing_flag equal to 1 specifies that an extended dynamic range is used for transform coefficients and transform processing. extended_precision_processing_flag equal to 0 specifies that the extended dynamic range is not used. When not present, the value of extended_precision_processing_flag is inferred to be equal to 0.
The variables CoeffMinY, CoeffMinC, CoeffMaxY and CoeffMaxC are derived as follows:
CoeffMinY = −( 1 << ( extended_precision_processing_flag ? Max( 15, BitDepthY + 6 ) : 15 ) ) (7-27)
CoeffMinC = −( 1 << ( extended_precision_processing_flag ? Max( 15, BitDepthC + 6 ) : 15 ) ) (7-28)
CoeffMaxY = ( 1 << ( extended_precision_processing_flag ? Max( 15, BitDepthY + 6 ) : 15 ) ) − 1 (7-29)
CoeffMaxC = ( 1 << ( extended_precision_processing_flag ? Max( 15, BitDepthC + 6 ) : 15 ) ) − 1 (7-30)
Note: If the chip supports both v1 and v2, the storage size becomes the same as v1.

## Slide 5: Complexity analysis (memory 3)
Cases
  VVC v1
    10-bit input
      64 x 64 x 11 bit (+0%)
  VVC v2
    16-bit input
      64 x 64 x 17 bit (+54%) Additional cost to use 64-point transform and HBD.
    12-bit input
      64 x 64 x 13 bit (+18%) Additional cost to use 64-point transform and HBD.
  VVC v2 + constraint (sps_max_luma_transform_size_64_flag = 0)
    16-bit input
      32 x 32 x 17 bit (-61%)
    12-bit input
      32 x 32 x 13 bit (-70%)
Note: If the chip supports both v1 and v2, the storage size becomes the same as v1.

## Slide 6: Proposed solution
Propose a constraint
  To save hardware cost, restrict max transform size to 32.
  For high bit depth coding,
    sps_max_luma_transform_size_64_flag sets equal to 0.
Experiment
  Anchor
    Follow HBD CTC
  Test
    Log2MaxTbSize : 5

## Slide 7: Experimental results
HDR PQ | AI |  |  |  |  |  |  | 
 | Over VTM11.0 |  |  |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.01% | 0.04% | 0.05% | 0.01% | 0.04% | 0.04% | 99% | 100%
PQ422 | 0.02% | 0.11% | 0.14% | 0.02% | 0.09% | 0.11% | 100% | 101%
Overall | 0.02% | 0.08% | 0.09% | 0.01% | 0.06% | 0.07% | 99% | 101%
 | LDB |  |  |  |  |  |  | 
 | Over VTM11.0 |  |  |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.01% | 0.02% | -0.01% | 0.01% | 0.01% | -0.01% | 102% | 100%
PQ422 | 0.01% | 0.01% | 0.03% | 0.01% | 0.01% | 0.03% | 101% | 100%
Overall | 0.01% | 0.01% | 0.01% | 0.01% | 0.01% | 0.01% | 102% | 100%
 | RA |  |  |  |  |  |  | 
 | Over VTM11.0 |  |  |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
PQ444 | 0.00% | 0.01% | -0.01% | 0.00% | 0.01% | -0.01% | 101% | 100%
PQ422 | 0.01% | 0.02% | 0.01% | 0.00% | 0.01% | 0.01% | 100% | 100%
Overall | 0.01% | 0.02% | 0.00% | 0.00% | 0.01% | 0.00% | 101% | 100%
Overall PQ | 0.01% | 0.04% | 0.03% | 0.01% | 0.03% | 0.03% | 101% | 100%
HDR HLG |  |  | AI |  | 
 | Over VTM11.0 |  |  |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | 0.07% | -0.06% | 0.02% | 101% | 101%
HLG422 | 0.03% | -0.01% | 0.04% | 99% | 100%
Overall | 0.05% | -0.03% | 0.03% | 100% | 101%
 |  |  | LDB |  | 
 | Over VTM11.0 |  |  |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | -0.04% | 0.04% | 0.05% | 101% | 101%
HLG422 | -0.02% | 0.05% | 0.01% | 102% | 100%
Overall | -0.03% | 0.04% | 0.03% | 102% | 100%
 |  |  | RA |  | 
 | Over VTM11.0 |  |  |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
HLG444 | -0.04% | 0.07% | 0.07% | 101% | 100%
HLG422 | -0.01% | 0.04% | 0.01% | 101% | 101%
Overall | -0.02% | 0.06% | 0.04% | 101% | 101%
Overall HLG | 0.00% | 0.02% | 0.03% | 101% | 100%

## Slide 8: Experimental results
SVT RGB |  |  | AI |  | 
 |  |  | Over VTM11.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.00% | 0.00% | 0.00% | 100% | 100%
SVT12 | 0.00% | 0.00% | 0.00% | 100% | 99%
Overall | 0.00% | 0.00% | 0.00% | 100% | 100%
 |  |  | LDB |  | 
 |  |  | Over VTM11.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.00% | 0.00% | 0.00% | 100% | 100%
SVT12 | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | 0.00% | 0.00% | 0.00% | 100% | 100%
 |  |  | RA |  | 
 |  |  | Over VTM11.0 |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.00% | 0.00% | 0.00% | 100% | 100%
SVT12 | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall RGB | 0.00% | 0.00% | 0.00% | 100% | 100%
For RGB contents, an anchor sets “Log2MaxTbSize : 5”.
Test results become the same as anchor.

## Slide 9: Additional experiment for RGB contents (ACT: 0)
Test condition is modified over HBD CTC.
Anchor:
  “Log2MaxTbSize : 6” and “ACT : 0”.
Test:
  “Log2MaxTbSize : 5” and “ACT : 0”.
SVT RGB |  |  | AI |  | 
 | Over VTM11.0, ACT:0 Log2MaxTbSize:6 |  |  |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.00% | 0.00% | 0.00% | 101% | 100%
SVT12 | 0.00% | 0.00% | 0.00% | 100% | 100%
Overall | 0.00% | 0.00% | 0.00% | 100% | 100%
 |  |  | LDB |  | 
 | Over VTM11.0, ACT:0 Log2MaxTbSize:6 |  |  |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | -0.01% | -0.01% | -0.01% | 105% | 101%
SVT12 | 0.00% | 0.00% | 0.00% | 103% | 100%
Overall | 0.00% | 0.00% | 0.00% | 104% | 100%
 |  |  | RA |  | 
 | Over VTM11.0, ACT:0 Log2MaxTbSize:6 |  |  |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
SVT16 | 0.00% | -0.01% | -0.01% | 105% | 100%
SVT12 | 0.00% | 0.00% | 0.00% | 104% | 100%
Overall | 0.00% | 0.00% | 0.00% | 104% | 100%
Overall RGB | 0.00% | 0.00% | 0.00% | 103% | 100%

## Slide 10: Conclusion
Introduced an issue of this contribution
  A large transform Increases memory size and cost.
Proposed a constraint for high bit depth
  sps_max_luma_transform_size_64_flag sets equal to 0.
Showed experimental results
  Tested “Log2MaxTbSize : 5”
  Negligible loss
HDR PQ | AI |  |  |  |  |  |  | 
 | Over VTM11.0 |  |  |  |  |  |  | 
 | wPsnrY | wPsnrU | wPsnrV | psnrY | psnrU | psnrV | EncT | DecT
Overall PQ | 0.01% | 0.04% | 0.03% | 0.01% | 0.03% | 0.03% | 101% | 100%
HDR HLG |  |  | AI |  | 
 | Over VTM11.0 |  |  |  | 
 | psnrY | psnrU | psnrV | EncT | DecT
Overall HLG | 0.00% | 0.02% | 0.03% | 101% | 100%
SVT RGB |  |  | AI |  | 
 | Over VTM11.0, ACT:0 Log2MaxTbSize:6 |  |  |  | 
 | psnrG | psnrB | psnrR | EncT | DecT
Overall RGB | 0.00% | 0.00% | 0.00% | 103% | 100%