## Slide 1
JVET-U0067
AHG8: On ALF clipping of high bit-depth coding
2021/1/7

## Slide 2
Problem statement
The coding gain of ALF is reduced if the coding bit-depth/bit-rate is increased.
At the very high bit-rate, the reconstructed frame consists of lot of details and high frequency components. Applying ALF may remove the details/high frequencies which ultimately impact the coding performance.
In order to reduce the over-filtering of high bit-depth and high bit-rate operating range, in the proposed method, the effect of over filtering process is reduced by adjusting the clipping values.

## Slide 3
Proposed method
The clipShift is derived as follows:

## Slide 4
Proposed method

## Slide 5
Simulation results: Anchor VTM-11.0
Proposed method
 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | -0.04% | -0.17% | -0.26% | 100% | 102% | -0.01% | 0.02% | 0.00% | 100% | 102% | 0.00% | 0.00% | 0.00% | 100% | 104%
LDB | -0.29% | -1.17% | -1.07% | 101% | 103% | -0.04% | -0.03% | -0.13% | 101% | 102% | -0.01% | 0.00% | 0.00% | 101% | 104%
RA | -0.26% | -1.18% | -1.09% | 101% | 102% | -0.02% | -0.04% | -0.21% | 99% | 100% | 0.00% | 0.00% | 0.00% | 101% | 104%
Overall | -0.20% | -0.84% | -0.81% | 101% | 102% | -0.02% | -0.02% | -0.11% | 100% | 101% | 0.00% | 0.00% | 0.00% | 101% | 104%
 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | 0.02% | 0.17% | 0.26% | 100% | 99% | 0.06% | 0.27% | 0.30% | 100% | 99% | 0.00% | 0.00% | 0.00% | 100% | 100%
LDB | 0.38% | 0.99% | 0.96% | 100% | 99% | 0.44% | 0.65% | 0.58% | 99% | 99% | 0.00% | 0.00% | 0.00% | 100% | 99%
RA | 0.32% | 0.99% | 1.02% | 100% | 99% | 0.41% | 0.67% | 0.61% | 98% | 98% | 0.00% | 0.00% | 0.00% | 100% | 99%
Overall | 0.24% | 0.72% | 0.75% | 100% | 99% | 0.30% | 0.53% | 0.50% | 99% | 99% | 0.00% | 0.00% | 0.00% | 100% | 99%
Tool OFF test: Disable ALF clipping
 | HDR PQ |  |  |  |  | HDR HLG |  |  |  |  | SVT RGB |  |  |  | 
 | wY | wU | wV | Enc | Dec | Y | U | V | Enc | Dec | G | B | R | Enc | Dec
AI | 0.14% | 0.41% | 0.76% | 99% | 91% | 0.24% | 1.21% | 1.63% | 99% | 91% | 0.00% | 0.00% | 0.00% | 100% | 99%
LDB | 1.54% | 2.92% | 3.52% | 99% | 84% | 2.21% | 5.18% | 6.14% | 100% | 82% | 0.01% | 0.00% | 0.00% | 100% | 99%
RA | 1.22% | 2.69% | 3.14% | 100% | 84% | 2.27% | 5.38% | 6.47% | 99% | 81% | 0.01% | 0.00% | 0.00% | 100% | 99%
Overall | 0.97% | 2.01% | 2.48% | 99% | 86% | 1.57% | 3.92% | 4.75% | 99% | 85% | 0.01% | 0.00% | 0.00% | 100% | 99%
Tool OFF test: Disable ALF_CCALF

## Slide 6
Conclusions
Proposed to adjust ALF clipping values at high-bit depth
Following results are reported:
  PQ sequence Y : -0.04% (AI), -0.29% (LDB), -0.26% (RA)
  HLG sequence Y: -0.01% (AI), -0.04% (LDB), -0.02% (RA)
  SVT sequence G: -0.00% (AI), 0.01% (LDB), 0.00% (RA)

## Slide 7
Thanks Qualcomm for cross-checking.