## Slide 1
JVET-U0099 AHG11: Neural Network-based Super Resolution
A. M. Kotra, K. Reuzé , J. Chen, H. Wang, M. Karczewicz, J. Li (Qualcomm)

## Slide 2: Neural Network-based Super Resolution
JVET-U0053 and JVET-T0092
  Showed that some of the Class A sequences exhibit BD-Rate gains when whole sequence is downsampled before encoding using RPR scheme.
  JVET-T0092 showed BD-Rate gains on top of VTM-10.0
    Only uses the VTM up-sampling filter
  JVET-U0053 showed BD-Rate gains on top of VTM-11.0
    Uses CNN based up-sampling filter
  In both contributions Anchor QPs used were 32, 37, 42 and 47 (very low-bitrate scenarios)
Current contribution
  Studied performance of using a CNN based up-sampling filter for “Sequence based” super resolution.
  Results are mainly shown using the Neural Network CTC QPs (22, 27, 32, 37, 42) for the VTM-11.0 Anchor
Motivation of the proposal
2x
Encode Frame
Original sequence
bitstream
Decode Frame
2x
Output pictures
VTM-11.0 Encoder
VTM-11.0 Decoder

## Slide 3: CNN based up-sampling filter
*EDSR architecture was used for the super-resolution upsampling filter
Number of residual blocks =16
Number of feature maps in each layer = 64
Parameter number per model = ~1.3 Million
Two models were trained to serve different QP ranges
Total parameter number = ~2.6 Million
Model selection during inference uses “Sequence QP”
* Lim et al, Enhanced Deep Residual Networks for Single Image Super-Resolution,“ 2017 (CVPRW)

## Slide 4: Training details
BVC-DVI is used as the training dataset.
Each sample is a tuple of (decoded , Original (2x upsampled ))
Two versions of training were tried
  “Training 1”: Uses the BVI-DVC encoded with VTM directly as input
  “Training 2”: Uses the BVI_DVC data downsampled by 2x using VTM downsampling filter and then encoded by VTM
Preprocessing during training and inference
  YUV 4:2:0 is converted to YUV 4:4:4 before feeding to network
  Chroma upsampling is done by repeating in vertical direction and averaging in horizontal direction
  Output from network is converted from YUV 4:4:4 to YUV 4:2:0 by averaging in both horizontal and vertical direction
Loss function
  Weighted L1 loss 8:1:1 (Y:U:V)

## Slide 5: Learning curve for “Training 1”
QP22-QP27 model
QP32-QP37 model

## Slide 6: Learning curve for “Training 2”
QP20-QP25 model
QP30-QP35 model

## Slide 7: Results of applying VTM-upsampling filter
Results of applying super resolution scheme using existing VTM up-sampling filter
 |  | Random access Main10 |  |  |  | 
 |  | Over VTM-11.0 (QP 22,27,32,37,42) |  |  |  | 
 |  | Y | U | V | EncT | DecT
Cass A1 4K | Tango2 | -4.41% | 0.19% | 10.52% | 50% | 33%
 | FoodMarket4 | -0.57% | 10.37% | 9.06% |  | 
 | Campfire | -2.56% | 95.98% | 35.38% |  | 
Class A2 4K | CatRobot1 | 24.07% | 44.74% | 68.09% | 40% | 30%
 | DaylightRoad2 | 42.46% | 18.66% | 41.19% |  | 
 | ParkRunning3 | -0.06% | 297.20% | 146.30% |  | 
 |  | All Intra Main10 |  |  |  | 
 |  | Over VTM-11.0 (QP 22,27,32,37,42) |  |  |  | 
 |  | Y | U | V | EncT | DecT
Cass A1 4K | Tango2 | -2.73% | -4.22% | 4.95% | 68% | 36%
 | FoodMarket4 | 1.41% | 6.63% | 7.16% |  | 
 | Campfire | 8.75% | 784.57% | 46.39% |  | 
Class A2 4K | CatRobot1 | 7.16% | 23.13% | 36.15% | 54% | 38%
 | DaylightRoad2 | 19.26% | -1.14% | 17.41% |  | 
 | ParkRunning3 | -2.45% | 147.69% | 78.17% |  | 

## Slide 8: Results of applying CNN based upsampling filter
Super resolution scheme using Neural-Network based up-sampling filter using“Training 1” (trained for *300* Epochs)
 |  | Random access Main10 |  |  |  | 
 |  | Over VTM-11.0 (QP 22,27,32,37,42) |  |  |  | 
 |  | Y | U | V | EncT | DecT
Cass A1 4K | Tango2 | -7.48% | -11.02% | -1.39% | 92% | 32%
 | FoodMarket4 | -4.03% | 7.27% | 5.77% |  | 
 | Campfire | -12.68% | 79.71% | -3.04% |  | 
Class A2 4K | CatRobot1 | 11.86% | 21.67% | 32.83% | 99% | 37%
 | DaylightRoad2 | 25.36% | 5.73% | 21.00% |  | 
 | ParkRunning3 | -4.87% | 194.75% | 89.13% |  | 
 |  | All Intra Main10 |  |  |  | 
 |  | Over VTM-11.0 (QP 22,27,32,37,42) |  |  |  | 
 |  | Y | U | V | EncT | DecT
Cass A1 4K | Tango2 | -6.49% | -9.62% | -7.78% | 147% | 36%
 | FoodMarket4 | -3.35% | 4.74% | 3.14% |  | 
 | Campfire | -3.63% | 293.00% | -3.72% |  | 
Class A2 4K | CatRobot1 | -2.59% | 6.64% | 11.29% | 99% | 37%
 | DaylightRoad2 | 5.47% | -10.53% | 0.18% |  | 
 | ParkRunning3 | -7.39% | 100.34% | 46.43% |  | 

## Slide 9: Results of applying CNN based upsampling filter
 |  | Random access Main10 |  |  |  | 
 |  | Over VTM-11.0 (QP 22,27,32,37,42) |  |  |  | 
 |  | Y | U | V | EncT | DecT
Cass A1 4K | Tango2 | -7.71% | -9.67% | 4.70% | 90% | 31%
 | FoodMarket4 | -5.20% | 4.88% | 4.81% |  | 
 | Campfire | -13.44% | 85.12% | 6.07% |  | 
Class A2 4K | CatRobot1 | 7.85% | 23.33% | 40.51% | 74% | 31%
 | DaylightRoad2 | 21.33% | 5.31% | 23.25 |  | 
 | ParkRunning3 | -7.44% | 197.45% | 93.99% |  | 
 |  | All Intra Main10 |  |  |  | 
 |  | Over VTM-11.0 (QP 22,27,32,37,42) |  |  |  | 
 |  | Y | U | V | EncT | DecT
Cass A1 4K | Tango2 | -6.74% | -10.56% | -0.37% | 148% | 36%
 | FoodMarket4 | -3.96% | 3.00% | 3.20% |  | 
 | Campfire | -6.53% | 302.39% | 3.27% |  | 
Class A2 4K | CatRobot1 | -4.22% | 7.44% | 16.21% | 92% | 37%
 | DaylightRoad2 | 2.83% | -11.59% | 0.74% |  | 
 | ParkRunning3 | -10.69% | 97.93% | 48.40% |  | 
Super resolution scheme using Neural-Network based up-sampling filter using “Training 2” (trained for *128* Epochs)

## Slide 10: Results over VTM-upsampling (using “Training2”)

## Slide 11: Conclusion & Future work
Performance of CNN based upsampling filter for “Sequence based” super resolution was studied
  Neural Network CTC QPs are used for the VTM-11.0 Anchor (MCTF ON, GOP size 32, fixed intra period)
Average Luma BD-Rate gains mainly observed for Class A1 sequences
  5.74% for All Intra and 8.79% for RA configuration
BD-Rate gain mainly seems content dependent
For sequences with “more high frequency content”, the upsampling filter fails to recover the “high frequencies” lost during downsampling
Future work
  The decision to code a “picture” or CTU at a downsampled resolution is chosen by comparing its RD cost with the RD cost of encoding at normal resolution
  It is asserted this method may provide further BD-Rate benefit for other sequences including low resolution sequences (Class B etc.)

## Slide 12: Thank you