## Slide 1: JVET-V0xxx AHG8: a combination of JVET-V0059 option 2 and JVET-V0122 for high bit depth and high bit rate extensions Fan Wang Z. Xie, Y. Yu, H. Yu, D. Wang

## Slide 2: Introduction
In JVET-V0059, a method of using CABAC bypass alignment and a bypass coding of sb_coded_flag is proposed as option 2 to improve the throughput.
    alignment is needed only once after the limit of the context coded bins has been reached for the TB
In JVET-V0122, a full-bypass mode in residual coding is proposed to improve the throughput and software encoding/decoding speed.
  the coefficient or residual levels are only coded through bypass mode without using any context-coded bin
  over 15% reduction in average encoding and decoding time from the 16-bit SVT sequences
This contribution proposes a combination of JVET-V0059 option 2 and JVET-V0122.
  all the syntax elements in residual coding, except for last significant coefficient position in RRC, are coded through bypass mode
  alignment is needed only once after the last significant coefficient position in RRC and at the very beginning of a TB in TSRC

## Slide 3: Proposed method (1/3)
A SPS level syntax element sps_high_throughput_flag is used to enable/disable the proposed method. If sps_high_throughput_flag is equal to 1, the following aspects are changed:
  The initial value of remBinsPass1 in RRC and RemCcbs in TSRC are set to 0
    the maximum number of context coded bins is set to 0
    As a result the coefficient or residual levels at all positions are coded only in the bypass mode
  The alignment happens before going into sub-block
    after last_sig_coeff_x_prefix, last_sig_coeff_y_prefix, last_sig_coeff_x_suffix and last_sig_coeff_y_suffix if any of residual_coding in RRC
    at the very beginning of residual_ts_coding in TSRC
  The sb_coded_flag is always coded in bypass mode.

## Slide 4: Proposed method (2/3)
In case of regular residual coding:
For last significant coefficient position
  context_coding of last_sig_coeff_x_prefix, last_sig_coeff_y_prefix, last_sig_coeff_x_suffix and last_sig_coeff_y_suffix
For remBinsPass1 and alignment
  if (sps_high_throughput_flag == 0)
    remBinsPass1 = ( ( 1 << ( log2TbWidth + log2TbHeight ) ) * 7 ) >> 2
  Else
    remBinsPass1 = 0
    CABAC bypass alignment (i.e.set ivlCurrRange to 256)
For each coefficient group
  if (sps_high_throughput_flag == 0)
    context_coding of sb_coded_flag
  else
    bypass_coding of sb_coded_flag
  if (sb_coded_flag ==1)
    if (remBinsPass1 >= 4)
      Pass 1:
        sig_coeff_flag; remBinsPass1--;
        abs_level_gtx_flag[ ][ 0 ] ; remBinsPass1--;
        par_level_flag; remBinsPass1--;
        abs_level_gtx_flag[ ][ 1 ] ; remBinsPass1--;
        set firstPosMode1
    Pass 2:
      if (n > firstPosMode1 && abs_level_gtx_flag[ ][ 1 ] == 1) abs_remainder
      if (n <= firstPosMode1) dec_abs_level
    Pass 3: coeff_sign_flag
In case of transform-skip residual coding:
For RemCcbs and alignment
  if (sps_high_throughput_flag == 0)
    RemCcbs = ( ( 1 << ( log2TbWidth + log2TbHeight ) ) * 7 ) >> 2
  else
    RemCcbs = 0
    CABAC bypass alignment (i.e.set ivlCurrRange to 256)
For each coefficient group
  if (sps_high_throughput_flag == 0)
    context_coding of sb_coded_flag
  else
    bypass_coding of sb_coded_flag
  if (sb_coded_flag ==1)
    if (RemCcbs >= 4)
      Pass 1:
        sig_coeff_flag; RemCcbs--;
        coeff_sign_flag; RemCcbs--;
        abs_level_gtx_flag[ ][ 0 ] ; RemCcbs--;
        par_level_flag; RemCcbs--;
    if (RemCcbs >= 4)
      Pass 2:
        abs_level_gtx_flag [ ][ 1 ]; RemCcbs--;
        abs_level_gtx_flag [ ][ 2 ] ; RemCcbs--;
        abs_level_gtx_flag [ ][ 3] ; RemCcbs--;
        abs_level_gtx_flag [ ][ 4 ] ; RemCcbs--;
    Pass 3: abs_remainder, coeff_sign_flag

## Slide 5: Proposed method (3/3)
Example of proposed method in RRC

## Slide 6: Proposed method (3/3)
Example of proposed method in TSRC

## Slide 7: Simulation results
The CTC specified for high bit depth and high bit rate video coding in [1] were used in the simulations;
The “anchor” is produced by the CE base software [2];
The “test” is produced by the proposed method implemented in the CE base software.
[1] A. Browne, T. Ikai, D. Rusanovskyy, M. Sarwer, X. Xiu “Common test conditions for high bit depth and high bit rate video coding”, JVET-U2018
[2] A. Browne, T. Hashimoto, H.-J. Jhu, D. Rusanovskyy, K. Kawamura, T. Zhou “CE on entropy coding for high bit depth and high bit rate coding”, JVET-U2022

## Slide 8: Simulation results
Low QP:

## Slide 9: Simulation results
Lossless:

## Slide 10: Conclusion
This contribution proposes a combination of JVET-V0059 option 2 and JVET-V0122
It is suggested to apply the proposed method in 16 bit high throughput configuration
  enable decoding of all the coefficients in a TB simply by using a shift register and multiple coded bins can be decoded in parallel
  Over 15% time reduction in encoding and decoding time
It is recommended to conduct core experiment on this method