## Slide 1
AHG11: Deep neural network for inter bi-prediction
Young-Ju Choi, Young-Woon Lee, Byung-Gyu Kim, Jongho Kim, Se Yoon Jeong
JVET-X0102

## Slide 2
Overview
In VVC, the bi-prediction block is generated from two different prediction blocks by utilizing several regular bi-prediction modes.
The regular bi-prediction modes consist of averaging, weighted averaging called BCW (bi-prediction with CU-level weight), and averaging with bi-directional optical flow (BDOF)-based refinement.
In this contribution, a neural network-based inter bi-prediction scheme is proposed as a replacement of regular bi-prediction modes on some of the block types.
The proposed method is applied only on the luma component, and regular averaging is applied on chroma components.

## Slide 3
Network Architecture
Figure 1. The architecture of the proposed attention-based bi-prediction neural network.
and : two prediction blocks
: final bi-prediction block
Kernel size for all the CNN layers : 3x3
Number of feature maps : 64 (last layer : 1)
Activation function : LeakyReLU
Number of Residual Blocks (wherein no batch normalization units) : 10
The attention map between two features can be obtained by using the dot product and the sigmoid activation function.

## Slide 4
Inference
Inference information |  | 
Mandatory | GPU Type | Quadro RTX 8000-48GB
 | CPU Type | Intel(R) Xeon(R) Gold 6256 CPU @ 3.60GHz
 | Framework: | Standalone C++, PyTorch 1.7.1
 | Number of GPUs per Task | 1
 | Total Parameter Number | 1295k
 | Parameter Precision (Bits) | 32 (F)
Optional | Total Conv. Layers | 32
 | Total FC Layers | 0
 | Batch size: | 1 block at a time
 | Patch size | Depending on the block (128x128, 64x64, 32x32)
Table 1. Inference information.
In inference stage, PyTorch 1.7.1 is used for performing the proposed neural network-based bi-prediction mode in VTM-11.0.
The proposed method is applied to three block types (128x128, 64x64, and 32x32).

## Slide 5
Training
Dataset
  The BVI-DVC dataset is used.
  Two prediction blocks are derived from the VTM-11.0 decoder with RA configuration.
  Ground truth is the original block.
  The dataset contains about 9M pair of blocks.
Training information |  | 
Mandatory | GPU Type | GeForce RTX 2080 Ti-11GB
 | CPU Type | Intel(R) Xeon(R) CPU E5-2620 v4 @ 2.10GHz
 | Framework: | PyTorch 1.4.0
 | Number of GPUs per Task: | 1
 | Number of Iterations: | 600k
 | Batch size: | 64
 | Total Parameter Number: | 1295k
 | Parameter Precision (Bits): | 32 (F)
 | Training data information: | BVI-DVC
 | Training configurations for generating compressed training data (if different to VTM CTC): | VTM-11.0, QP {22, 27, 32, 37, 42}
Optional | Patch size | 32x32x2, 64x64x2, 128x128x2
 | Learning rate: | 4e-4
 | Optimizer: | ADAM
 | Loss function: | Charbonnier penalty function
 | Preprocessing: | Augmentation : Random horizontal and vertical flips, 90° rotation
Table 2. Training information.

## Slide 6
Training
In training stage, PyTorch 1.4.0 is used for training the proposed neural network.
For different block types (128x128, 64x64, and 32x32) and QPs (22, 27, 32, 37, and 42), the proposed network is trained independently.
Training information |  | 
Mandatory | GPU Type | GeForce RTX 2080 Ti-11GB
 | CPU Type | Intel(R) Xeon(R) CPU E5-2620 v4 @ 2.10GHz
 | Framework: | PyTorch 1.4.0
 | Number of GPUs per Task: | 1
 | Number of Iterations: | 600k
 | Batch size: | 64
 | Total Parameter Number: | 1295k
 | Parameter Precision (Bits): | 32 (F)
 | Training data information: | BVI-DVC
 | Training configurations for generating compressed training data (if different to VTM CTC): | VTM-11.0, QP {22, 27, 32, 37, 42}
Optional | Patch size | 32x32x2, 64x64x2, 128x128x2
 | Learning rate: | 4e-4
 | Optimizer: | ADAM
 | Loss function: | Charbonnier penalty function
 | Preprocessing: | Augmentation : Random horizontal and vertical flips, 90° rotation
Table 2. Training information.

## Slide 7
Experimental Results
For all sequences in class B, a subset of frames equivalent to 1 second is used.
It is observed that averagely 0.98%, 0.96%, and 2.08% BD-rate reductions with five QPs are achieved for Y component on B, C, and D classes under RA configurations, respectively.
 | Random access Main10 |  |  |  | 
 | Over VTM-11.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.98% | 0.25% | 0.19% | 6494% | 660%
Class C | -0.96% | 0.06% | 0.11% | 3634% | 715%
Class D | -2.08% | -0.31% | -0.41% | 3029% | 1012%
Overall | -1.32% | 0.02% | -0.02% | 4296% | 771%
Table 3. Experimental results on VTM-11.0 (class B: 1 sec, class C/D: 10 sec, GPU time).

## Slide 8
Thank You