## Slide 1: JVET-X0152: AHG12: Edge classifier for Cross-component Sample Adaptive Offset (CCSAO)
A. M. Kotra, N. Hu, V. Seregin, M. Karczewicz (Qualcomm) C. –W. Kuo, X. Xiu, Y. –W. Chen, H. –J. Jhu, W. Chen, N. Yan, X. Wang (Kwai)

## Slide 2: SAO and CCSAO in ECM-2.0
SAO
Band Classifier
Edge Classifier
CCSAO
Band Classifier
Edge based Classifier is proposed
  A Classifier based on the edge information is proposed
  Similar to SAO, classification is performed based on Edge Information
  Main differences with SAO Edge classifier:
    Sample differences are compared with a threshold value for classification
    For Chroma components co-located luma samples are used to derive the Edge information

## Slide 3: Edge based classifier for CCSAO
Similar to SAO, one among the 4 1-D patterns (H, V, 135° diagonal and 45° diagonal) is used to compute the sample differences
Based on sample differences classifier variables “Ea” and “Eb” are computed
  Ea=(a-c<0)?(a-c<(-Th)?0:1):(a-c<(Th)?2:3) – (1)
  Eb=(b-c<0)?(b-c<(-Th)?0:1):(b-c<(Th)?2:3) – (2)
  Variable “Th” is the threshold value which is pre-defined
Final classification index is derived as follows:
  class_idx = band * 16 + Ea * 4 + Eb – (3)
  Variable “band” in Eq. 3 above is derived based on the sample value of either the Luma or Chroma sample.
Each CTU can either select the new “Edge based” classifier or “Band” classifier.

## Slide 4: “Edge based” classifier applied only to Chroma components
 | All Intra Main10 |  |  |  | 
 | Over ECM-2.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.09% | -1.25% | -0.87% | 102% | 101%
Class A2 | 0.05% | -1.29% | -4.66% | 99% | 102%
Class B | 0.08% | -2.25% | -0.24% | 101% | 103%
Class C | 0.04% | 0.28% | 0.20% | 100% | 101%
Class E | 0.04% | -0.93% | 0.37% | 101% | 102%
Overall | 0.06% | -1.14% | -0.88% | 101% | 102%
Class D | 0.01% | -0.04% | 0.01% | 100% | 100%
Class F | 0.04% | -1.29% | -0.78% | 100% | 102%
Class TGM | 0.05% | -1.77% | -1.54% | 100% | 100%
Random Access Main 10 |  |  |  | 
Over ECM-2.0 |  |  |  | 
Y | U | V | EncT | DecT
0.03% | -0.39% | -0.04% | 100% | 99%
0.03% | -1.23% | -3.16% | 97% | 99%
0.06% | -1.62% | -0.14% | 99% | 99%
0.03% | -0.07% | 0.05% | 99% | 99%
0.04% | -0.88% | -0.67% | 99% | 99%
0.01% | -0.14% | -0.07% | 100% | 100%
0.01% | -0.65% | -0.50% | 102% | 101%
0.00% | -0.82% | -0.63% | 101% | 100%
Low delay B Main10 |  |  |  | 
Over ECM-2.0 |  |  |  | 
Y | U | V | EncT | DecT
0.03% | -1.29% | -0.61% | 101% | 101%
-0.06% | -0.24% | 0.06% | 95% | 96%
-0.06% | -1.23% | -1.18% | 98% | 97%
-0.02% | -0.93% | -0.53% | 98% | 98%
0.05% | -0.32% | 0.19% | 98% | 99%
-0.08% | -0.53% | -0.59% | 98% | 97%
0.07% | -0.65% | -0.46% | 100% | 99%
“Edge based” classifier applied to both Luma and Chroma components
Random Access Main 10 |  |  |  | 
Over ECM-2.0 |  |  |  | 
Y | U | V | EncT | DecT
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
-0.24% | -1.36% | 0.06% | 101% | 100%
-0.03% | 0.15% | 0.28% | 99% | 99%
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
-0.01% | -0.13% | -0.03% | 99% | 97%
-0.19% | -0.30% | -0.19% | 102% | 100%
-0.44% | -0.62% | -0.59% | 101% | 100%
Low delay B Main10 |  |  |  | 
Over ECM-2.0 |  |  |  | 
Y | U | V | EncT | DecT
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
-0.19% | 0.05% | 0.33% | 100% | 101%
-0.42% | -0.55% | 0.14% | 104% | 100%
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
-0.07% | -0.99% | -0.12% | 100% | 99%
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
#VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | All Intra Main10 |  |  |  | 
 | Over ECM-2.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -1.14% | -0.83% | 102% | 102%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | 0.02% | -2.13% | -0.13% | 101% | 103%
Class C | 0.02% | 0.42% | 0.30% | 100% | 100%
Class E | -0.07% | -0.77% | 0.39% | 102% | 102%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | 0.01% | -0.04% | 0.01% | 101% | 101%
Class F | -0.12% | -1.06% | -0.60% | 101% | 103%
Class TGM | -0.29% | -1.70% | -1.45% | 100% | 101%

## Slide 5: Conclusion
“Edge” based classifier for CCSAO is proposed
When applied only to Chroma components, BD-Rate changes in RA condition are as follows (Y/U/V): 0.04%, -0.88%, -0.67% without substantial EncT and DecT increase
When applied to both Luma and Chroma components, BD-Rate changes in RA condition are as follows (Y/U/V): ??%, ??%, ??% without substantial EncT and DecT increase
Suggested to further study the “Edge” based classifier in next round of EE.
We would like to thank Alibaba for cross checking JVET-X0191