## Slide 1
JVET-X0152
AHG12: CCSAO classification with edge information
Che-Wei Kuo, Xiaoyu Xiu, Yi-Wen Chen, Hong-Jheng Jhu, Wei Chen, Ning Yan, and Xianglin Wang

## Slide 2: Introduction
In ECM-2.0, the CCSAO classifier only uses band information of all three components to classify the current sample
In this contribution, one new classifier considering both edge and band information is proposed

## Slide 3: Proposal
Combine luma EO and BO to classify the current luma/chroma sample
  EO: one of 4 directions, classify (c-a) and (c-b) into 4*4 categories
  BO: luma bandNum

## Slide 4: Proposal
The original three component band classifier and the proposed edge classifier are switched at CTB level
Parameters for the proposed classifier (i.e., , , and offsets) are signaled in frame level (same as original CCSAO BO classifier)
only contains power-of-2 values to reduce hardware complexity

## Slide 5: Simulation Results
Without SIMD

## Slide 6: Conclusion
One new classifier considering both edge and band information is proposed
Coding gains with low complexity classification-based sample operation
Suggest to study in EE
Thank Alibaba for crosscheck