## Slide 1: JVET-Y0048 AHG10: study of layer bitrate allocation for spatial scalability in VTM
P. de Lagrange, F. Urban, G. Marquant
InterDigital R&D France
January 2021

## Slide 2: Context
JVET-Y0047 = HD+UHD scalability visual test report with equal EL and BL bitrate
  Exploring other allocation welcome, since it has a strong impact on performance, in favor of more bitrate on BL
  Could lead to recommendations for further visual tests (refined verification test plan)
Brazil TV3.0 “enhancement” codec, competition with LCEVC
  TV3.0 test conditions, PSNR-Y BD-rate vs simulcast: VVC = -14% ; LCEVC = about +200%
  LCEVC was selected, with no obvious technical reason
    Challenged on complexity, and deployment readiness
    What about VVC ?
  LCEVC nominally uses a very thin enhancement layer : look like a valid choice
    Is coding performance relevant for a very low bitrate layer ?
  LCEVC is said to bring gain vs single layer
    MPEG requirements: “when enhancing an n-th generation MPEG codec (e.g., AVC), the compression efficiency for the aggregate stream is appreciably higher than that of the n-th generation MPEG codec used at full resolution”
  What about VVC ? Can dual-layer coding be considered as a coding tool ?
    See also: adaptive resolution, JVET-Y0068, and work related to super-resolution

## Slide 3: EL/BL rate balance: exploration method
Single reference with fixed rate points
  eg QP(SL)= [28, 32, 36, 40, 44]
Enhancement layer: keep the same fixed QPs as single layer
  Should get similar quality
Base layer: for each QP(EL), sweep QP(BL)
Add QP(EL)=63, with very wide QP(BL) sweep
  mimic « RPR » (downscaled coding + pure upscale), similar to JVET-Y0068 but always 2x scale
May add 1 or 2 lower bitrate points to show scalability benefit

## Slide 4: EL/BL exploration: illustration (1)

## Slide 5: EL/BL exploration: illustration (2)

## Slide 6: EL/BL exploration: illustration (3)

## Slide 7: BD-rates with optimal allocation
Name | QPBL | QPEL = QPSL | BD-rate vs single layer (PSNR_Y) | BD-rate vs single layer (SSIM_Y) | BD-rate vs single layer (VMAF) | Enc. time | Dec. time
Procession | 22, 28, 34, 40 | 28, 34, 40, 46 | +0.4% | -4.5% | -3.4% | 95% | 101%
RiverBoat | 23, 29, 34, 40 | 29, 35, 41, 47 | +0.0% | -6.4% | -5.1% | 101% | 111%
Marathon2 | 23, 27, 32, 35, 37 | 29, 33, 38, 41, 45 | +5.6% | +2.7% | +3.1% | 75% | 99%
MountainBay2 | 24, 27, 30, 33, 37 | 30, 33, 36, 39, 43 | +9.7% | +3.9% | +11.6% | 124% | 93%
TallBuildings2 | 25, 30, 35, 34, 38 | 28, 32, 36, 40, 44 | +16.6% | +9.7% | +9.3% | 173% | 112%
CorsaireJoy | 23, 26, 30, 34, 38 | 28, 32, 36, 40, 44 | -0.9% | -6.2% | -3.8% | 105% | 105%
TwoBirdsInDawn | 23, 26, 30, 34, 38 | 28, 32, 36, 40, 44 | +4.0% | -1.4% | +0.8% | 150% | 101%
AngelInSunrise | 23, 27, 30, 34, 38 | 28, 32, 36, 40, 44 | +10.2% | +6.3% | +11.7% | 163% | 105%
Average |  |  | +5.7% | +0.5% | +3.0% | 123% | 103%
Highly dependent on bitrate: gains at low bitrates, losses at high bitrates

## Slide 8: BD-rates with optimal allocation
Name | QPBL | QPEL = QPSL | BD-rate vs single layer (PSNR_Y) | BD-rate vs single layer (SSIM_Y) | BD-rate vs single layer (VMAF) | Enc. time | Dec. time
Procession | 26, 33, 39, 44 | 28, 34, 40, 46 | +17.9% | +18.3% | +18.1% | 136% | 115%
RiverBoat | 27, 33, 39, 45 | 29, 35, 41, 47 | +13.5% | +11.7% | +13.% | 143% | 119%
Marathon2 | 27, 31, 36, 39, 43 | 29, 33, 38, 41, 45 | +18.8% | +17.6% | +15.4% | 131% | 118%
MountainBay2 | 28, 31, 34, 37, 42 | 30, 33, 36, 39, 43 | +12.3% | +10.4% | +14.5% | 162% | 118%
TallBuildings2 | 23, 28, 33, 38, 42 | 28, 32, 36, 40, 44 | +19.4% | +15.6% | +13.9% | 175% | 112%
CorsaireJoy | 27, 31, 35, 39, 43 | 28, 32, 36, 40, 44 | +18.0% | +18.8% | +18.2% | 145% | 117%
TwoBirdsInDawn | 26, 30, 44, 38, 42 | 28, 32, 36, 40, 44 | +27.3% | +27.7% | +24.5% | 164% | 108%
AngelInSunrise | 26, 31, 35, 39, 43 | 28, 32, 36, 40, 44 | +20.1% | +20.8% | +19.8% | 168% | 112%
Average |  |  | +18.4% | +17.6% | +17.3% | 153% | 115%
Highly dependent on bitrate: gains at low bitrates, losses at high bitrates

## Slide 9: Crops
QP 38/44

## Slide 10
SL : QP 44

## Slide 11
QP 43/44

## Slide 12: Encoding time illustration