## Slide 1
JVET-Y0095
Non-EE2: RPR with luma-only re-scaling
Philippe Bordes, Franck Galpin, Edouard François

## Slide 2
RPR drops in chroma ?
  RPR benefits for UHD content:
    reduces blocking artefacts at low bit rate
    encoding/decoding times (complexity) decreases significantly
  But previous meetings raised RPR had BD-rate gains in luma but loss in chroma:
    RPR performs an additional down-scaling filtering on samples that were already filtered from the original canonical 4:4:4 content to create the 4:2:0 format
* Combination of full size and quarter size coding (RPR) adaptively per sequences and target rate (RPR is used at low bit rate if it improves anchors). RPR streams QPs =QPCTC - 5 = {17, 22, 27, 32, 37}
1 1 frame in AI, 17 frames in RA, {BodeMuseum, NeptuneFountain2, NeptuneFountain3, OberbaumSpree, QuadrigaTree, SubwayTree, TiergartenParkway}.

## Slide 3
Proposal
  Proposal:
    increase the flexibility of RPR by allowing down-scaling luma only
    the codec may switch dynamically resolution and/or chroma format which is signaled in PPS
    still benefit from the CC tools (intra prediction, CC-SAO, CC-ALF)
    RPR luma-only feature is limited to down-scaling by 2 both horizontally and vertically, so that the chroma format of the reconstructed pictures may be 4:2:0 (no-RPR or regular RPR) or 4:4:4 (luma-only RPR)
  Tests:
    Chroma qp-offset = +5 to align with the CTC chroma qp anchors

## Slide 4
luma-only RPR: Chroma qp-offset adjustment

## Slide 5
Chroma qp-offset adjustment
Luma-only RPR
Regular RPR

## Slide 6
Conclusion
RPR improves the coding efficiency for low bit-rates which improves the overall BD-rate coding gains and reduce the encoding/decoding times.
The luma-only RPR tool provides at least same BD-rate gains as regular RPR. However, the regular RPR requires adjusting the chroma qp-offset per sequence and depends on coding configuration to align with BD-rate anchor curves.
The luma-only RPR is a simple extension of RPR which overcomes the issue of additional down-filtering of chroma in 4:2:0. It also facilitates the selection of QP to be consistent across sequence types and configurations.
One proposes following RPR modifications in ECM:
  Enable luma-only RPR in ECM
  Encode chroma-format into PPS

## Slide 7
luma-only RPR: Chroma qp-offset adjustment (4 QPs)

## Slide 8
Chroma qp-offset adjustment (4 QPs)
Luma-only RPR
Regular RPR