## Slide 1: JVET-Z0062 RPR luma filter modifications and RPR enabling fixes in ECM
Ruoyang Yu

## Slide 2: Background
Luma interpolation filter for normal (non-RPR) motion compensation is now 12-tap in ECM
  The 12-tap filter is applied for both non-affine blocks and affine blocks
  It is also used as RPR MC filter for non-affine blocks under “up-sampling” scenario
An overview of the filter taps used in MC
 | Normal MC Non-RPR scenario | RPR scenario 1 “up-sampling” scenario (ref/cur <= 1.25) | RPR scenario 2 “1.5x down-sampling” scenario” (1.25 < ref/cur <=1.75) | RPR scenario 3 “2.0x down-sampling scenario” (ref/cur > 1.75)
Non-affine blocks | 12 | 12 | 8 | 8
Affine blocks | 12 | 6 | 6 | 6

## Slide 3: Proposal
Proposed RPR luma filter modifications:
  (a) Increase the RPR filter for affine blocks also to 12-tap under “up-sampling” scenario
  (b) Propose a 12-tap RPR filter for “1.5x down-sampling” scenario
  (c) Propose a 12-tap RPR filter for “2.0x down-sampling” scenario
Motivation:
  Help demonstrate better compression performance for RPR in ECM
  Improve design consistency (in terms of filter taps) for luma RPR filters in ECM
 | Normal MC Non-RPR scenario | RPR scenario 1 “up-sampling” scenario (ref/cur <= 1.25) | RPR scenario 2 “1.5x down-sampling” scenario” (1.25 < ref/cur <=1.75) | RPR scenario 3 “2.0x down-sampling scenario” (ref/cur > 1.75)
Non-affine blocks | 12 | 12 | 8 -> 12 (b) | 8 -> 12 (c)
Affine blocks | 12 | 6 -> 12 (a) | 6 -> 12 (b) | 6 -> 12 (c)

## Slide 4: Proposed RPR luma filter modification (a)
(a) Increase the RPR filter for affine blocks also to 12-tap under “up-sampling” scenario
  The current 12-tap filter is used
 | Normal MC Non-RPR scenario | RPR scenario 1 “up-sampling” scenario (ref/cur <= 1.25)
Non-affine blocks | 12 | 12
Affine blocks | 12 | 6 -> 12 (a)

## Slide 5: Proposed RPR luma filter modification (b)
(b) Propose 12-tap RPR filter for “1.5x down-sampling” scenario
  Filter is designed based on SHM 1.5x source down-sampling filter
 | RPR scenario 2 “1.5x down-sampling” scenario” (1.25 < ref/cur <=1.75)
Non-affine blocks | 8 -> 12 (b)
Affine blocks | 6 -> 12 (b)

## Slide 6: Proposed RPR luma filter modification (c)
(c) Propose 12-tap RPR filter for “2.0x down-sampling” scenario
  Filter is the same as SHM 2.0x source down-sampling filter, but with filter gain adjusted to 256
 | RPR scenario 3 “2.0x down-sampling scenario” (ref/cur > 1.75)
Non-affine blocks | 8 -> 12 (c)
Affine blocks | 6 -> 12 (c)

## Slide 7: Results
Test 1: RA + RPR 1.5x + picture resolution switch every 16 pics *
Test 2: RA + RPR 2.0x + picture resolution switch every 16 pics*
* The same configuration as in JVET-Y0128
ScalingRatioHor : 1.5
ScalingRatioVer : 1.5
FractionNumFrames : 1.0
RPR : 1
UpscaledOutput : 2
SwitchPocPeriod : 16
 | Random Access Main 10 (PSNR2) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.09% | -0.01% | -0.01% | 101% | 99%
Class A2 | -0.18% | -0.16% | -0.13% | 100% | 99%
Class B | -0.30% | -0.25% | -0.20% | 97% | 98%
Class C | -0.37% | -0.34% | -0.23% | 108% | 103%
Class E |  |  |  |  | 
Overall | -0.25% | -0.21% | -0.16% | 101% | 99%
Class D | -0.40% | -0.02% | 0.04% | 93% | 98%
ScalingRatioHor : 2.0
ScalingRatioVer : 2.0
FractionNumFrames : 1.0
RPR : 1
UpscaledOutput : 2
SwitchPocPeriod : 16
 | Random Access Main 10 (PSNR2) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.05% | 0.07% | -0.05% | 100% | 105%
Class A2 | -0.09% | -0.01% | 0.11% | 100% | 105%
Class B | -0.11% | -0.06% | 0.00% | 98% | 96%
Class C | -0.18% | -0.02% | -0.12% | 100% | 104%
Class E |  |  |  |  | 
Overall | -0.11% | -0.01% | -0.02% | 99% | 102%
Class D | -0.21% | 0.09% | 0.21% | 86% | 92%

## Slide 8: Results (anchor is ECM with MR105)
Test 1: RA + RPR 1.5x + picture resolution switch every 16 pics * (MR105 still have issue in this case)
Test 2: RA + RPR 2.0x + picture resolution switch every 16 pics*
* The same configuration as in JVET-Y0128
 | Random Access Main 10 (PSNR2) |  |  |  | 
 | Over ECM-4.0 with MR105 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B |  |  |  |  | 
Class C | -0.18% | -0.11% | -0.02% | 99% | 101%
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.21% | 0.31% | 0.59% | 97% | 98%
ScalingRatioHor : 1.5
ScalingRatioVer : 1.5
FractionNumFrames : 1.0
RPR : 1
UpscaledOutput : 2
SwitchPocPeriod : 16
ScalingRatioHor : 2.0
ScalingRatioVer : 2.0
FractionNumFrames : 1.0
RPR : 1
UpscaledOutput : 2
SwitchPocPeriod : 16

## Slide 9: Additional Results
Test 3: LDB + RPR 1.5x + picture resolution switch every 0.5 sec
Test 4: LDB + RPR 2.0x + picture resolution switch every 0.5 sec
ScalingRatioHor : 1.5
ScalingRatioVer : 1.5
FractionNumFrames : 1.0
RPR : 1
UpscaledOutput : 2
SwitchPocPeriod : 0
ScalingRatioHor : 2.0
ScalingRatioVer : 2.0
FractionNumFrames : 1.0
RPR : 1
UpscaledOutput : 2
SwitchPocPeriod : 0
 | Low delay B Main10 (PSNR1) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.31% | -0.26% | -0.06% | 100% | 100%
Class C | -0.69% | -0.39% | -0.36% | 99% | 99%
Class E | -2.07% | -1.33% | -0.51% | 99% | 98%
Overall | -0.88% | -0.57% | -0.27% | 99% | 99%
Class D | -0.80% | -0.20% | -0.47% | 102% | 102%
 | Low delay B Main10 (PSNR2) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.28% | -0.25% | -0.10% | 100% | 100%
Class C | -0.38% | -0.41% | -0.41% | 99% | 99%
Class E | -1.43% | -1.28% | -0.48% | 99% | 98%
Overall | -0.60% | -0.56% | -0.30% | 99% | 99%
Class D | -0.50% | -0.23% | -0.39% | 102% | 102%
 | Low delay B Main10 (PSNR1) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.18% | -0.14% | 0.16% | 99% | 95%
Class C | -0.42% | -0.12% | -0.23% | 97% | 101%
Class E | -1.08% | 0.83% | 0.55% | 99% | 102%
Overall | -0.49% | 0.11% | 0.12% | 99% | 99%
Class D | -0.62% | 0.41% | 0.67% | 97% | 101%
 | Low delay B Main10 (PSNR2) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.11% | -0.14% | 0.18% | 99% | 95%
Class C | -0.23% | -0.12% | -0.32% | 97% | 101%
Class E | -0.47% | 0.41% | 0.35% | 99% | 102%
Overall | -0.24% | 0.01% | 0.06% | 99% | 99%
Class D | -0.29% | 0.11% | 0.42% | 97% | 101%

## Slide 10: Conclusion (for RPR luma filter modifications)
The following RPR luma filter modifications are proposed
  (a) Increase the RPR MC filter for affine blocks also to 12-tap under “up-sampling” scenario
  (b) Propose 12-tap RPR MC filter for “1.5x down-sampling” scenario
  (c) Propose 12-tap RPR MC filter for “2.0x down-sampling” scenario
It is asserted that the proposed filter modifications are straightforward and improves the deign consistency for RPR in ECM and helps demonstrating better compression performance for RPR in ECM
  It is proposed to include the proposed filter modification into next version of ECM
 | Normal MC Non-RPR scenario | RPR scenario 1 “up-sampling” scenario (ref/cur <= 1.25) | RPR scenario 2 “1.5x down-sampling” scenario” (1.25 < ref/cur <=1.75) | RPR scenario 3 “2.0x down-sampling scenario” (ref/cur > 1.75)
Non-affine blocks | 12 | 12 | 8 -> 12 (b) | 8 -> 12 (c)
Affine blocks | 12 | 6 -> 12 (a) | 6 -> 12 (b) | 6 -> 12 (c)

## Slide 11: RPR enabling fixes in ECM-4.0
It was noted that ECM-4.0 does not fully support RPR enabling (when picture resolution switching is enabled)
Issue related macros | Proposed fixes
JVET_Y0065_GPM_INTRA | Add coordinates scaling according to the scaling ratio when fetching motion information and IPM from a rescaled reference picture.
JVET_Y0067_ENHANCED_MMVD_MVD_SIGN_PRED | a) For the template-based MVD sign derivation, added a new function isMvsdApplicable(RefPicList, RefIdx) besides the existing isMvsdApplicable() for determining whether the template-based MVD sign derivation is enabled. b) In MMVD candidate reordering (function sortInterMergeMMVDCandidates() and function sortAffineMergeCandidates()), the template generation and cost calculation is bypassed if a MMVD candidate is associated with a rescaled reference picture. The template cost is directly set to 0 for the candidate.
JVET_Y0134_TMVP_NAMVP_CAND_REORDERING | For merge candidate reordering within a same type group (function adjustMergeCandidatesInOneCandidateGroup()), the template generation and cost calculation is bypassed if a merge candidate is associated with a rescaled reference picture. The template cost is directly set to 0 for the candidate. This purpose of this change is to align with what ECM is doing for adjustInterMergeCandidates().
ALF_IMPROVEMENT | The current ALF SIMD code in simdFilter9x9Blk() does not support block input width non-dividable by 8. This corner case can be triggered when RPR is enabled with 1.5x scaling ratio. The boundary chroma CTB for class D will have a width of 12. The fix is to add non-SIMD version of the ALF filtering code for the corner cases.

## Slide 12: Conclusion (for RPR enabling fixes in ECM)
Suggest to study all the RPR fixes contribution and identify preferred fixes
  Especially in terms of
    What value of the template cost should be set to when the candidate is associated with a rescaled reference picture
    Should we always by-pass the template cost calculation when the candidate is associated with a rescaled reference picture

## Slide 14: Back-up slides
Ruoyang Yu

## Slide 15: Filter comparisons for RPR 1.5x at subpel 6/16

## Slide 16: Filter comparisons for RPR 2x at subpel 6/16

## Slide 17: Additional Results
Test 3: LDB + RPR 1.5x + picture resolution switch every 0.5 sec
Test 4: LDB + RPR 2.0x + picture resolution switch every 0.5 sec
ScalingRatioHor : 1.5
ScalingRatioVer : 1.5
FractionNumFrames : 1.0
RPR : 1
UpscaledOutput : 2
SwitchPocPeriod : 0
ScalingRatioHor : 2.0
ScalingRatioVer : 2.0
FractionNumFrames : 1.0
RPR : 1
UpscaledOutput : 2
SwitchPocPeriod : 0
 | Low delay B Main10 (PSNR1) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.31% | -0.26% | -0.06% | 100% | 100%
Class C | -0.69% | -0.39% | -0.36% | 99% | 99%
Class E | -2.07% | -1.33% | -0.51% | 99% | 98%
Overall | -0.88% | -0.57% | -0.27% | 99% | 99%
Class D | -0.80% | -0.20% | -0.47% | 102% | 102%
 | Low delay B Main10 (PSNR2) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.28% | -0.25% | -0.10% | 100% | 100%
Class C | -0.38% | -0.41% | -0.41% | 99% | 99%
Class E | -1.43% | -1.28% | -0.48% | 99% | 98%
Overall | -0.60% | -0.56% | -0.30% | 99% | 99%
Class D | -0.50% | -0.23% | -0.39% | 102% | 102%
 | Low delay B Main10 (PSNR1) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.18% | -0.14% | 0.16% | 99% | 95%
Class C | -0.42% | -0.12% | -0.23% | 97% | 101%
Class E | -1.08% | 0.83% | 0.55% | 99% | 102%
Overall | -0.49% | 0.11% | 0.12% | 99% | 99%
Class D | -0.62% | 0.41% | 0.67% | 97% | 101%
 | Low delay B Main10 (PSNR2) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.11% | -0.14% | 0.18% | 99% | 95%
Class C | -0.23% | -0.12% | -0.32% | 97% | 101%
Class E | -0.47% | 0.41% | 0.35% | 99% | 102%
Overall | -0.24% | 0.01% | 0.06% | 99% | 99%
Class D | -0.29% | 0.11% | 0.42% | 97% | 101%
 | Normal MC Non-RPR scenario | RPR scenario 1 “up-sampling” scenario (ref/cur <= 1.25) | RPR scenario 2 “1.5x down-sampling” scenario” (1.25 < ref/cur <=1.75) | RPR scenario 3 “2.0x down-sampling scenario” (ref/cur > 1.75)
Non-affine blocks | 12 | 12 | 8 -> 12 (b) | 8 -> 12 (c)
Affine blocks | 12 | 6 -> 12 (a) | 6 -> 12 (b) | 6 -> 12 (c)

## Slide 18: Additional Results
Test X: LDB + RPR 1.5x + picture resolution switch every 0.5 sec
Test Y: LDB + RPR 2.0x + picture resolution switch every 0.5 sec
 | Low delay B Main10 (PSNR2) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.15% | 0.15% | 0.22% | 94% | 91%
Class C | -0.14% | -0.05% | -0.07% | 93% | 98%
Class E | -0.39% | 0.80% | -0.32% | 91% | 90%
Overall | -0.21% | 0.25% | -0.01% | 93% | 93%
Class D | -0.21% | 0.59% | 0.70% | 95% | 91%
 | Low delay B Main10 (PSNR1) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.17% | 0.13% | 0.15% | 94% | 91%
Class C | -0.31% | 0.00% | -0.01% | 93% | 98%
Class E | -0.94% | 0.87% | -0.29% | 91% | 90%
Overall | -0.41% | 0.27% | -0.01% | 93% | 93%
Class D | -0.39% | 0.75% | 0.81% | 95% | 91%
 | Low delay B Main10 (PSNR2) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.24% | -0.34% | -0.16% | 95% | 96%
Class C | -0.31% | -0.39% | -0.23% | 94% | 95%
Class E | -1.32% | -0.50% | -0.24% | 95% | 94%
Overall | -0.53% | -0.40% | -0.21% | 95% | 95%
Class D | -0.40% | -0.08% | -0.67% | 97% | 95%
 | Low delay B Main10 (PSNR1) |  |  |  | 
 | Over ECM-4.0 with proposed RPR fix |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.29% | -0.34% | -0.17% | 95% | 96%
Class C | -0.58% | -0.32% | -0.21% | 94% | 95%
Class E | -1.97% | -0.54% | -0.31% | 95% | 94%
Overall | -0.81% | -0.39% | -0.22% | 95% | 95%
Class D | -0.62% | -0.08% | -0.75% | 97% | 95%
ScalingRatioHor : 1.5
ScalingRatioVer : 1.5
FractionNumFrames : 1.0
RPR : 1
UpscaledOutput : 2
SwitchPocPeriod : 0
ScalingRatioHor : 2.0
ScalingRatioVer : 2.0
FractionNumFrames : 1.0
RPR : 1
UpscaledOutput : 2
SwitchPocPeriod : 0
 | Normal MC Non-RPR scenario | RPR scenario 1 “up-sampling” scenario (ref/cur <= 1.25) | RPR scenario 2 “1.5x down-sampling” scenario” (1.25 < ref/cur <=1.75) | RPR scenario 3 “2.0x down-sampling scenario” (ref/cur > 1.75)
Non-affine blocks | 12 | 12 | 8 -> 12 (b) | 8 -> 12 (c)
Affine blocks | 12 | 6 | 6 | 6