## Slide 1
JVET-Z0079:
Non-EE2: Support RPR on ECM-4.0
and handling method for template maching based coding tools
Hyeongmun Jang (hm.jang@lge.com)
LG Electronics Inc.

## Slide 2
Summary
Proposes to fix regarding the RPR on ECM-4.0 and further handle template matching based coding tools for RPR
Related coding tool | Z0079(LGE)
GPM INTRA | Fetch IPM information after scaling reference picture by following same spirit of JVET-X0121
MVSD | For each reference list, RefPicLX is resampled, MVSD is disabled and Sign of the MVD is coded using conventional VVC way RefPicLX is not resampled, MVSD is enabled.
TMVP/NAMVP | After construct candidate list, If The candidates’ reference picture is resampled then the template cost is set to MAX value by following same spirit of JVET-Y0128
MMVD/Affine MMVD | After construction of the candidate list, If the reference picture of the base candidate for the MMVD or Affine MMVD is resampled. the template cost is set to MAX without TM by following spirit of JVET-X0121 and Y0128
ARMC | From the JVET-X0121 and Y0128, The reference picture of candidate is resampled, the TM is bypassed but the cost is set to 0 not MAX. Hence it is suggest to fix to set cost as MAX.

## Slide 3
Background
 | Z0079(LGE) | Z0062 | MR105+Z0067
GPM INTRA | Fetch IPM information after scaling reference picture by following same spirit of JVET-X0121 | Same | Same
MVSD | For each reference list, RefPicLX is resampled, MVSD is disabled and Sign of the MVD is coded using conventional VVC way RefPicLX is not resampled, MVSD is enabled. | Same | Sign of the MVD is always coded by index. However, during calculation of the template cost of each sign-pair for MVD, the reference picture is resampled, that processing is bypassed.
TMVP/ NAMVP | After construct candidate list, If The candidates’ reference picture is resampled then the template cost is set to MAX value | Same | None
MMVD/ AffineMMVD | After construction of the candidate list, If the reference picture of the base candidate for the MMVD or Affine MMVD is resampled, the template cost is set to MAX by following spirit of JVET-X0121 and Y0128 | Same | Similar but different implementation, This implementation set the cost as MAX_UINT>>1 not std::numeric_limits<Distortion>::max().
ARMC | From the JVET-X0121 and Y0128, The reference picture of candidate is resampled, the TM is bypassed but the cost is set to 0 not MAX. Hence it is suggest to fix to set cost as MAX. | None | None
ALF improvement | None | Modify SIMD to support input width being non-dividable by 8. | None
Regarding the detail fixes for each contribution

## Slide 4
Simulation results
ind
 | Random Access Main 10 |  |  |  |  | Low Delay Main 10 |  |  |  | 
 | Over ECM-4.0 with anchor configuration setting |  |  |  |  | Over ECM-4.0 with anchor configuration setting |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -61.29% | -43.12% | -35.38% | 27% | 31% |  |  |  |  | 
Class A2 | -57.11% | -72.94% | -67.00% | 26% | 31% |  |  |  |  | 
Class B | -58.75% | -62.36% | -50.09% | 28% | 31% | -57.11% | -58.62% | -44.55% | 26% | 29%
Class C | -61.96% | -56.96% | -50.03% | 29% | 32% | -63.42% | -55.89% | -47.46% | 27% | 31%
Class E |  |  |  |  |  | -50.77% | -37.85% | -33.69% | 28% | 33%
Overall | -59.79% | -59.19% | -50.51% | 28% | 32% | -57.63% | -52.51% | -42.80% | 27% | 31%
Class D | -63.61% | -55.63% | -51.90% | 27% | 32% | -63.53% | -53.70% | -47.94% | 26% | 30%
Class F | -38.51% | -39.53% | -37.23% | 35% | 36% | -39.01% | -31.07% | -30.31% | 33% | 35%
 | Random Access Main 10 |  |  |  |  | Low Delay Main 10 |  |  |  | 
 | Over ECM-4.0 with anchor configuration setting |  |  |  |  | Over ECM-4.0 with anchor configuration setting |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | -36.01% | -18.62% | -13.62% | 71% | 69% |  |  |  |  | 
Class A2 | -30.37% | -52.38% | -42.82% | 73% | 69% |  |  |  |  | 
Class B | -34.07% | -46.34% | -31.71% | 74% | 70% | -34.41% | -44.42% | -30.99% | 70% | 74%
Class C | -23.74% | -25.99% | -17.79% | 73% | 71% | -30.20% | -30.36% | -21.11% | 70% | 74%
Class E |  |  |  |  |  | -29.16% | -30.96% | -28.75% | 75% | 83%
Overall | -30.96% | -36.58% | -26.60% | 73% | 70% | -31.70% | -36.37% | -27.14% | 71% | 76%
Class D | -26.31% | -25.89% | -20.06% | 74% | 72% | -30.40% | -32.56% | -26.18% | 70% | 74%
Class F | -9.23% | -11.44% | -8.94% | 78% | 81% | -11.42% | -12.32% | -10.19% | 80% | 88%
PSNR1 for configuration1
PSNR1 for configuration2

## Slide 5
Supplemental result
ind
 | Random Access Main 10 |  |  | Low Delay Main 10 |  | 
 | Over ECM-4.0 with anchor configuration setting |  |  | Over ECM-4.0 with anchor configuration setting |  | 
 | Y | U | V | Y | U | V
Class A1 | -3.31% | -4.24% | -2.66% |  |  | 
Class A2 | -2.52% | -2.68% | -4.52% |  |  | 
Class B | -3.41% | -2.64% | -2.33% | -3.68% | -4.35% | -4.95%
Class C | -3.29% | -2.34% | -2.52% | -3.54% | -4.70% | -5.49%
Class E |  |  |  | -1.27% | -2.06% | -0.43%
Overall | -3.18% | -2.89% | -2.88% | -3.03% | -3.89% | -4.00%
Class D | -3.13% | -2.19% | -2.37% | -3.02% | -3.19% | -5.60%
Class F | -3.39% | -2.38% | -2.87% | -3.79% | -4.06% | -4.18%
 | Random Access Main 10 |  |  | Low Delay Main 10 |  | 
 | Over ECM-4.0 with anchor configuration setting |  |  | Over ECM-4.0 with anchor configuration setting |  | 
 | Y | U | V | Y | U | V
Class A1 | -8.12% | -5.12% | -3.78% |  |  | 
Class A2 | -10.92% | -10.62% | -9.89% |  |  | 
Class B | -10.77% | -12.79% | -8.88% | -9.32% | -12.34% | -10.94%
Class C | -4.23% | -4.04% | -3.72% | -5.09% | -7.01% | -6.89%
Class E |  |  |  | -4.71% | -5.11% | -4.38%
Overall | -8.53% | -8.49% | -6.69% | -6.76% | -8.76% | -7.95%
Class D | -7.52% | -6.46% | -5.72% | -5.74% | -9.27% | -9.00%
Class F | -5.24% | -4.24% | -4.07% | -5.96% | -6.97% | -6.18%
PSNR1 for configuration1 over ECM-3.1 RPR ( reported at JVET-Y0128 table 4.1 )
PSNR1 for configuration2 over ECM-3.1 RPR ( reported at JVET-Y0128 table 4.2)

## Slide 6
Conclusion
ind
It is recommend to adopt the suggested fixes for supporing the RPR in ECM-4.0

## Slide 7
ind
 | Z0079(LGE) | Z0062(Ericsson) | MR105+Z0067(InterDigital)
Up/down sampling filter | None | Proposed to use existing 12-tap filter as the upsampling for Affine. Proposed to 1.5x down-sampling luma filter | None
Chroma format adaptation | None | None | Luma only RPR
Regarding the non-fixes for each contribution
Appendix