## Slide 1: JVET-AA0047 [AHG 11] Brief information about JPEG AI CfP status
E. Alshina, J. Ascenso, T. Ebrahimi, F. Pereira, T. Richter

## Slide 2: JPEG AI is multi-task standard
Object Classification: Resnet50
Super Res: WDSR
Submission tracks | Selection
A. Standard Reconstruction (mandatory) | X
B. Compressed Domain Super-resolution | 
C. Compressed Domain Denoising | 
D. Compressed Domain Image Classification | 

## Slide 3: High-lights (Standard Reconstruction task)
12 teams registered
10 teams submitted bit-streams
5 passed cross-check successfully
3 teams outperform VVC anchor ~20...30%
CPU decoder run time ~ of VVC

## Slide 4: Standard Reconstruction task
4 anchors
  JPEG
  JPEG200
  HEVC
  VVC
7 metrics
  MS-SSIM
  IW-SSIM
  VIF
  PSNR-HVS-M
  NLDP
  FSIM
  VMAF
Common training set
  5264 images
  camera captured
  up to 8K

## Slide 5: HEVC/VVC anchors generation
RGB
YUV 4:4:4
bits
BT.709
YUV 4:4:4
10 bits
BT.709
RGB
HEVC anchor
HM-16.20+SCM-8.8
encoder_intra_main_scc_10.cfg
VVC anchor
VTM11.1
encoder_intra_vtm.cfg
classSCC.cfg (only for screen content)
ffmpeg
ffmpeg
Target rates: 0.06, 0,12, 0.25, 0.50, 0.75 bpp
For VVC anchor
QP=27~0.75 bpp, QP=31~0.5 bpp, QP=37~0.25 bpp , QP=42~0.12 bpp, , QP=46~0.06 bpp

## Slide 6: Three-phases CfP submissions
Registration of proposals (Feb. 25)
Phase #1: submission of decoder and models (write access to decoder and models folders is closed after this phase, decoder can be encrypted) (March, 14)
Announcement of hidden test set (March, 20)
Phase #2: submission of bit-streams and reconstructed images (May, 4)
Cross-check of decoders and report cross-check results (June, 13)
Visual quality assessment and results cross-check (July, 13)
Phase #3: submission of encoder, training scripts and decoder in readable form (July, 18),
Results announcement (July, 25)

## Slide 7: Hidden test set
Screen
content

## Slide 8: Device interoperability issue
Adoption to the standard draft and reference SW requires support for device interoperability but for CfP submission it is allowed not to meet this requirement.
Reconstructions on difference devices can deviate, allowed difference limited to 0.5% BD-rate (tentatively)
Encoded/decoded
same device
Encoded/decoded
different device
If entropy sub-net operates in float
The part of the cross-check is to run decoder on 2 different platforms (CPU and GPU) and report the difference

## Slide 9: Objective performance results
  BD-rate computed in MS-SSIM, IW-SSIM, VIF, PSNR-HVS-M, NLDP, FSIM, VMAF
PSNR_Y, 14.7%

## Slide 10: Objective performance results (anchors)
MS-SSIM vs bpp VMAF vs bpp PSNR-Y vs bpp

## Slide 11: Objective performance results (test and VVC)
MS-SSIM vs bpp VMAF vs bpp PSNR-Y vs bpp

## Slide 12
VVC 0.12 bpp

## Slide 13
TEAM16 0.12 bpp

## Slide 14
VVC 0.25 bpp

## Slide 15
TEAM14 0.25 bpp

## Slide 16
VVC 0.25 bpp

## Slide 17
TEAM24 0.25 bpp

## Slide 18
VVC 0.12 bpp

## Slide 19
TEAM14 0.12 bpp

## Slide 20: Conclusion
More details in JPEG AI