## Slide 1
JVET-AA0069: Non-EE2: amvpMerge for low delay.
Hyeongmun Jang (hm.jang@lge.com)
LG Electronics Inc.

## Slide 2
Summary
In order to enable amvpMerge for low-delay, if current slice is low delay picture,
Construct reference picture pair with non true bi-directional pictures. Additionally the restriction condition on the resampled, long-term and WP reference pictures are relaxed for reference picture pair of amvpMerge mode.
Skip bilateral matching based merge candidate reordering for non true bi-directional reference picture pair by setting the cost as maximum value.
Bypass the “decoder-side motion vector refinement”.
Two alternative methods are tested.
Method 1 : aspect 1 + aspect 2
Method 2 : aspect 1 + aspect 2 + aspect 3

## Slide 3
Background
In ECM-5.0,
amvpMerge is based on bilateral matching so it has been applied for only random access configuration because amvpMerge is enabled only when the reference picture pair can be constructed as one is a forward picture and the other is a backward picture.
Therefore amvpMerge has not been applied in the low-delay picture due to the reference pictures being all forward pictures.
However, it is investigated that amvpMerge is effective even for the low-delay case without bilateral matching-based reordering and decoder side motion vector refinement

## Slide 4
Proposed aspects
For low-delay picture,
The amvpMerge is enabled even the reference picture pair is not true bi-directional pictures. Additionally the restriction condition on the resampled, long-term and WP reference pictures are relaxed.
BM cost of an amvpMerge candidate which is not true bi-directional is set to be the maximum value during merge candidate reordering.
The decoder side motion vector refinement process of the conventional amvpMerge is bypassed.

## Slide 5
Decoding flow for the low-delay by the proposed methods
(b) method 1
(c) method 2
The decoding flow for the low-delay picture is lined in red and the shaded module means skipped block for low-delay picture
(a) ECM-5.0

## Slide 6
Simulation results with CTC
ind
 | Random Access Main 10 |  |  |  |  | Low Delay Main 10 |  |  |  | 
 | Over ECM-5.0 CTC |  |  |  |  | Over ECM-5.0 CTC |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.13% | 0.02% | 101% | 102% |  |  |  |  | 
Class A2 | -0.02% | 0.04% | -0.04% | 102% | 101% |  |  |  |  | 
Class B | 0.00% | 0.02% | -0.05% | 101% | 101% | -0.34% | -0.62% | -0.88% | 107% | 102%
Class C | 0.00% | -0.05% | -0.02% | 101% | 100% | -0.29% | -0.43% | -0.80% | 107% | 103%
Class E |  |  |  |  |  | -0.56% | -0.21% | -0.91% | 106% | 101%
Overall | 0.00% | 0.03% | -0.03% | 101% | 101% | -0.38% | -0.45% | -0.86% | 107% | 102%
Class D | 0.00% | -0.20% | 0.05% | 101% | 101% | -0.28% | 0.21% | 0.19% | 106% | 100%
Class F | 0.00% | -0.03% | 0.00% | 101% | 101% | -0.34% | -0.33% | 0.14% | 104% | 100%
Method 1 : aspect 1 + aspect 2
Method 2 : aspect 1 + aspect 2 + aspect 3
 | Random Access Main 10 |  |  |  |  | Low Delay Main 10 |  |  |  | 
 | Over ECM-5.0 CTC |  |  |  |  | Over ECM-5.0 CTC |  |  |  | 
 | Y | U | V | EncT | DecT | Y | U | V | EncT | DecT
Class A1 | 0.00% | 0.13% | 0.03% | 101% | 103% |  |  |  |  | 
Class A2 | -0.01% | 0.04% | -0.05% | 102% | 102% |  |  |  |  | 
Class B | 0.00% | 0.03% | -0.05% | 100% | 101% | -0.26% | -0.59% | -0.44% | 105% | 101%
Class C | 0.00% | -0.05% | -0.03% | 101% | 101% | -0.27% | -0.44% | -0.45% | 105% | 102%
Class E |  |  |  |  |  | -0.47% | -0.14% | -0.41% | 105% | 102%
Overall | 0.00% | 0.03% | -0.03% | 101% | 102% | -0.32% | -0.43% | -0.44% | 105% | 102%
Class D | 0.00% | -0.19% | 0.07% | 99% | 99% | -0.28% | 0.01% | -0.41% | 104% | 100%
Class F | 0.00% | -0.03% | 0.00% | 99% | 99% | -0.30% | -0.89% | -0.21% | 102% | 100%
Simulation result : method 1
Simulation result : method 2

## Slide 7
Conclusion
ind
It is recommended to adopt the proposed method in order to enable amvpMerge for low-delay.

## Slide 8
END
ind
Appreciate Qualcomm for cross-checking
Question / Comment ?