## Slide 1: JVET-AA0090 EE1-related: One luma model with IPB and skip for filtering intra and inter luma slices
Du Liu, Jacob Ström, Mitra Damghanian, Per Wennersten, Yun Li

## Slide 2: Overview
Propose to use one luma model with block type information and block skip information for NN-filtering
  Block type information: I, P, B
  Block skip information: bypassed or not
The proposed model is used for both intra luma and inter luma slices
Reduce the total number of models from 4 (JVET-Z0112) to 3
Reduce the total number of parameters from 6.24M (JVET-Z0112) to 4.70M
IPB+skip model (trained with AI and RA data):
  BDR-Y -9.99% RA, -7.44% AI, and -8.47% LDB.
  Worst case kMAC/pixel 660 (1.7% higher than JVET-Z0112).
Inter luma model from JVET-Z0112 (retrained with AI and RA data):
  BDR-Y -9.64% RA, -7.48% AI, and -8.47% LDB.
  Worst case kMAC/pixel 638.

## Slide 3: NN structure with IPB and skip
Head of the network
Eight residual blocks
Last part of the network

## Slide 4: Complexity
Luma model | kMAC/sample (Y) | kMAC/pix (YUV) for AI | kMAC/pix (YUV) for RA | kMAC/pix (YUV) worst case | Num. of param. of the inter luma model (10^6) | Num. of parameters in total (10^6) | Total memory (106 bytes)
JVET-Z0112 | 429 for intra 418 for inter | 649 | 632 | 649 | 1.551 | 6.24 (luma inter + luma intra + chroma inter + chroma intra) | 24.94
Retrained inter model from JVET-Z0112 | 418 | 638 | 632 | 638 | 1.551 | 4.67 (luma + chroma inter + chroma intra) | 18.69
Model with IPB+skip | 440 | 660 | 654 | 660 | 1.576 | 4.70 (luma + chroma inter + chroma intra) | 18.79

## Slide 5: Training
Table 2. Network Information for NN-based video coding tool testing in training stage for the luma model. The intra chroma and inter chroma models are the same as in JVET-Z0112. |  | 
Network Information in Training Stage |  | 
Mandatory | GPU Type | GPU: NVIDIA A100-PCIE-40GB
 | Framework: | PyTorch v1.9
 | Number of GPUs per Task | 1
 | Epoch: | 330
 | Batch size: | 32 (L1) and 16 (L2) for the IPB+skip model 64 (L1) and 32 (L2) for the retrained JVET-Z0112 model
 | Loss function: | Weighted L1 and L2
 | Training time: | 15 days (IPB+skip model) 12 days (retrained Z0112 model)
 | Training data information: | DIV2K, BVI-DVC
 | Training configurations for generating compressed training data (if different to VTM CTC): | VTM-11.0 + new MCTF, qp {17, 22, 27, 32, 37, 42}
Optional |  | 
 | Number of iterations | 
 | Patch size | 256x256
 | Learning rate: | 1e-4 and 1e-5
 | Optimizer: | ADAM
 | Preprocessing: | 
 | Mini-batch selection process: | 
 | Other information: | Since the IPB+skip model is larger, it does not fit in the GPU memory using a batch size of 64, so a batch size of 32 is used for L1 training. However, the same number of patches (and samples) are trained in both cases.

## Slide 6: Inference
Table 3. Network Information for NN-based video coding tool testing in inference stage for the luma model. The intra chroma and inter chroma models are the same as in JVET-Z0112. |  | 
Network Information in Inference Stage |  | 
Mandatory | HW environment: | 
 | GPU Type | N/A
 | Framework: | libtorch
 | Number of GPUs per Task | 0
 | Total Parameter Number | 4.70M for the IPB+skip model 4.67M for the retrained JVET-Z0112 model
 | Parameter Precision (Bits) | fp32
 | Memory Parameter (MB) | 18.79 for the IPB+skip model 18.69 for the retrained JVET-Z0112 model
 | Multiplay Accumulate (MAC) | 660 kMAC/pix for the IPB+skip model 638 kMAC/pix for the retrained JVET-Z0112 model
Optional |  | 
 | Total Conv. Layers | 
 | Total FC Layers | 
 | Total Memory (MB) | 
 | Batch size: | 1
 | Patch size | 128x128, 256x256
 | Changes to network configuration or weights required to generate rate points | 
 | Peak Memory Usage (Total) | 
 | Peak Memory Usage (per Model) | 
 | Border handling | 
 | Other information: | 

## Slide 7: Results
IPB+skip model
Retrained inter model
Encoding time not reliable
Encoding time not reliable

## Slide 8: Conclusions
This contribution proposes to use one luma model with additional IPB and skip inputs for NN-filtering of intra luma and inter luma blocks.
With additional IPB and skip inputs, the model gives 0.35% (= 9.99% − 9.64%) higher gain for RA than the model without IPB or skip inputs in the tests carried out in the contribution.
The contribution proposes to further study the IPB+skip model for NN loop filters in an exploration experiment and study if we can get the same gain using just IPB or just skip as an input
Thanks to Tencent for cross-checking!