## Slide 1: Division-free operation and mean-compensation for convolutional cross-component model (CCCM)
JVET-AA0114
Alireza Aminlou, Jani Lainema, Pekka Astola

## Slide 2
Proposing two modifications to CCCM (Cross-Component Linear Model) prediction to simplify the CCCM implementations
Remove the mean sample value from luma and chroma samples used in the CCCM process (and reduce the fixed-point precision to 16-bit decimal part)
Substitute division operations by multiply-and-shift operations
JVET-AA0114: Introduction

## Slide 3
Proposing to substitute the input to the CCCM operations with mean removed parameters. That is, prediction of a chroma sample changes from:
predChromaVal = c0C + c1N + c2S + c3E + c4W + c5P + c6B
to:
predChromaVal = c0C' + c1N' + c2S' + c3E' + c4W' + c5P' + c6B + meanC
where:
C' = C - meanY
N' = N - meanY
S' = S - meanY
E' = E - meanY
W' = W - meanY
P' = P -(meanY * meanY) >> bitdepth
Mean removal
meanY: average luma of reference samples meanC: average chroma of reference samples

## Slide 4
Mean removal applied in both model creation and final prediction
As a result, the magnitudes of the values in the model calculation are reduced and less precision is needed for fixed-point arithmetic
  Proposed to use 16-bit decimal precision in fixed-point operations (down from 22-bit precision)
Mean removal

## Slide 5
Division operations used in the model creation are substituted with multiply-and-shift approach (in the spirit of what is done for CCLM)
result = num * scale >> shift
Second order model for the scale (first order in CCLM)
3 x 8 look-up table entries (1 x 16 in CCLM)
Improves the accuracy of division for larger numbers
Division removal

## Slide 6
Experimental results
 | All Intra Main10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.19 % | -2.59 % | -4.53 % | 100 % | 100 %
Class A2 | -5.59 % | -4.25 % | -7.10 % | 102 % | 98 %
Class B | -0.59 % | -3.39 % | -1.65 % | 102 % | 100 %
Class C | -0.14 % | -0.84 % | -0.76 % | 103 % | 99 %
Class E | -0.34 % | -3.38 % | -1.50 % | 102 % | 99 %
Overall | -1.38 % | -2.83 % | -2.81 % | 102 % | 99 %
Class D | -0.09 % | -0.74 % | -0.55 % | 103 % | 97 %
Class F | -0.86 % | -3.15 % | -2.84 % | 102 % | 99 %
Class TGM | -2.85 % | -5.24 % | -5.03 % | 102 % | 100 %
 | Random Access Main 10 |  |  |  | 
 | Over ECM-5.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -1.14 % | -2.20 % | -3.91 % | 101 % | 94 %
Class A2 | -2.10 % | -1.98 % | -3.91 % | 101 % | 95 %
Class B | -0.35 % | -3.29 % | -2.18 % | 103 % | 93 %
Class C | -0.08 % | -0.60 % | -0.68 % | 104 % | 97 %
Class E |  |  |  |  | 
Overall | -0.79 % | -2.09 % | -2.47 % | 102 % | 94 %
Class D | -0.06 % | -0.75 % | -0.50 % | 104 % | 95 %
Class F | -1.21 % | -2.97 % | -2.88 % | 102 % | 95 %
Class TGM | -1.54 % | -2.42 % | -2.34 % | 102 % | 97 %
 | All Intra Main10 |  |  |  | 
 | Over ECM-5.0+CCCM (EE2 Test1.1a) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.02 % | -0.04 % | 0.30 % | 100 % | 99 %
Class A2 | 0.01 % | -0.02 % | -0.08 % | 101 % | 99 %
Class B | 0.00 % | 0.05 % | -0.01 % | 101 % | 99 %
Class C | 0.00 % | 0.03 % | 0.00 % | 100 % | 98 %
Class E | 0.01 % | -0.20 % | -0.08 % | 100 % | 97 %
Overall | 0.01 % | -0.02 % | 0.02 % | 100 % | 98 %
Class D | 0.00 % | -0.20 % | 0.09 % | 101 % | 97 %
Class F | 0.02 % | 0.06 % | -0.02 % | 100 % | 99 %
Class TGM | 0.01 % | -0.01 % | 0.03 % | 99 % | 100 %
 | Random Access Main 10 |  |  |  | 
 | Over ECM-5.0+CCCM (EE2 Test1.1a) |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.01 % | -0.19 % | 0.04 % | 100 % | 95 %
Class A2 | 0.01 % | -0.01 % | -0.12 % | 100 % | 96 %
Class B | 0.00 % | 0.17 % | -0.04 % | 102 % | 93 %
Class C | -0.01 % | -0.03 % | -0.07 % | 103 % | 96 %
Class E |  |  |  |  | 
Overall | 0.00 % | 0.01 % | -0.05 % | 101 % | 95 %
Class D | -0.02 % | 0.00 % | 0.03 % | 104 % | 96 %
Class F | -0.07 % | 0.10 % | -0.05 % | 102 % | 97 %
Class TGM | 0.05 % | 0.06 % | 0.05 % | 100 % | 97 %

## Slide 7
Proposing two modifications to CCCM
Use 16-bit decimal precision after mean removal
Substitute division operations by multiply-and-shifts
No practical impact for coding efficiency
Suggested to include the modifications to the next version of ECM
Summary