## Slide 1: JVET-AB0108 AHG11: ALF-SPLIT for NCS-1.0
Wenjie Zou, Yi Zhou, Chengming Gu (Xidian University)
Cheng Huang, Yaxian Bai, Yuanjian Zhang (ZTE Corporation)
2022.10

## Slide 2
NCS1.0：
  An ALF flag is used to indicate whether ALF is on or off for luma and chroma component.
  This flag is off in several cases due to the high-quality of NN filter
                JVET-Y0046
  An additional ALF flag is introduced to indicate whether chroma ALF and CCALF is on or off.
Introduction

## Slide 3
Experimental results on top of NCS-1.0 (filter set #0)
 | NCS-1.0 (filter set #0) |  | 
 |  | All Intra | 
 | Y | U | V
Class A1 | 0.00% | 0.00% | -0.01%
Class A2 | 0.00% | 0.00% | 0.00%
Class B | 0.00% | -0.11% | -0.17%
Class C | 0.03% | -0.98% | -0.61%
Class E | 0.01% | 0.00% | 0.00%
Overall | 0.01% | -0.25% | -0.14%
Class D | 0.08% | -1.37% | -0.65%
Class F | 0.00% | 0.00% | 0.00%
 |  | Random Access | 
 | Y | U | V
Class A1 |  |  | 
Class A2 |  |  | 
Class B | 0.02% | -0.28% | -0.06%
Class C | 0.02% | -0.15% | -0.19%
Class E |  |  | 
Overall |  |  | 
Class D | 0.02% | -0.58% | -0.59%
Class F | 0.00% | -0.02% | -0.05%

## Slide 4
Experimental results on top of NCS-1.0 (filter set #0)

## Slide 5
Experimental results on top of NCS-1.0 (filter set #1)
 | NCS-1.0 (filter set #1) |  | 
 |  | All Intra | 
 | Y | U | V
Class A1 | 0.06% | -0.99% | -2.70%
Class A2 | 0.00% | -0.04% | -0.02%
Class B | 0.01% | -0.57% | -0.57%
Class C | 0.05% | -1.73% | -1.16%
Class E | 0.00% | 0.00% | 0.00%
Overall | 0.02% | -0.71% | -0.87%
Class D | 0.11% | -1.64% | -1.51%
Class F | 0.00% | 0.00% | 0.00%
 |  | Random Access | 
 | Y | U | V
Class A1 |  |  | 
Class A2 |  |  | 
Class B | 0.02% | -0.28% | -0.06%
Class C | 0.02% | -0.15% | -0.15%
Class E |  |  | 
Overall |  |  | 
Class D | 0.02% | -0.48% | -0.28%
Class F | 0.01% | -0.06% | -0.07%

## Slide 6
Experimental results on top of NCS-1.0 (filter set #1)

## Slide 7
Luma ALF and chorma ALF can be configured separately to provide more flexibility.
Coding performance compared with NCS-1.0 (filter set #0)
AI: 0.01%/-0.25%/-0.14%
Coding performance compared with NCS-1.0 (filter set #1)
AI: 0.02%/-0.71%/-0.87%
Recommend to investigate in EE based on the next version of NCS
Conclusion

## Slide 8
Thank you