## Slide 1: AHG12 Template-based Intra Mode Derivation with directional blending JVET-AB0117
Saverio Blasi, Jani Lainema,
Ivan Zupancic, Done Bugdayci Sansli

## Slide 2
It is proposed to use directional blending of two
TIMD-derived predictors:
one derived from template ABOVE
one derived from template LEFT
When proposed mode is active, two TIMD searches performed on each template:
MPM candidates used for search as in TIMD
Refinement around best direction found in the other template
Search only considers “normal” VVC directions, no extended angular modes.
Proposed approach

## Slide 3
The two directional TIMD predictors are spatially blended:
Higher weights on top part of block for mode derived from template ABOVE
Higher weights on left part of block for mode derived from template LEFT
Weights depend on the SATDs
Method is signalled as sub-mode of TIMD.
One more RD check in luma intra loop.
Proposed approach (2)

## Slide 4
Experimental results
 | All Intra Main10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.18% | -0.22% | -0.08% | 106% | 102%
Class A2 | -0.15% | -0.03% | -0.05% | 107% | 102%
Class B | -0.16% | -0.03% | -0.09% | 109% | 102%
Class C | -0.19% | 0.03% | -0.03% | 108% | 103%
Class E | -0.27% | -0.20% | -0.24% | 108% | 103%
Overall | -0.19% | -0.08% | -0.09% | 108% | 102%
Class D | -0.18% | -0.04% | -0.08% | 107% | 104%
Class F | -0.14% | -0.18% | 0.03% | 104% | 103%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.12% | 0.03% | -0.06% | 101% | 99%
Class A2 | -0.11% | -0.04% | -0.12% | 100% | 98%
Class B | -0.09% | 0.05% | -0.27% | 98% | 99%
Class C | -0.10% | -0.02% | 0.06% | 99% | 98%
Class E |  |  |  |  | 
Overall | -0.10% | 0.01% | -0.11% | 99% | 99%
Class D | -0.04% | 0.12% | -0.12% | 99% | 98%
Class F | -0.10% | -0.21% | -0.21% | 98% | 99%

## Slide 5
Additional information: combination with JVET-AB0116
 | All Intra Main10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.24% | -0.13% | -0.15% | 107% | 102%
Class A2 | -0.19% | -0.24% | -0.16% | 108% | 102%
Class B | -0.20% | 0.03% | -0.18% | 110% | 102%
Class C | -0.26% | -0.05% | -0.22% | 108% | 103%
Class E | -0.35% | -0.29% | -0.32% | 109% | 103%
Overall | -0.24% | -0.11% | -0.20% | 109% | 103%
Class D | -0.21% | -0.01% | -0.27% | 108% | 103%
Class F | -0.17% | -0.06% | 0.25% | 104% | 100%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.19% | 0.00% | -0.15% | 101% | #NUM!
Class A2* | -0.11% | -0.13% | -0.15% | 99% | #NUM!
Class B | -0.11% | -0.13% | -0.25% | 99% | #NUM!
Class C | -0.13% | -0.08% | -0.05% | 100% | #NUM!
Class E |  |  |  |  | 
Overall | -0.13% | -0.09% | -0.16% | 100% | #NUM!
Class D | -0.10% | 0.11% | 0.02% | 99% | #NUM!
Class F | -0.08% | -0.13% | 0.01% | 98% | #NUM!
*For RA tests, 3 test points in Class A2 still running, copied from the anchor.

## Slide 6
Additional information:
encoder optimization of combination with JVET-AB0116
 | All Intra Main10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.15% | -0.23% | -0.16% | 105% | #NUM!
Class A2* | -0.15% | -0.18% | -0.13% | 105% | #NUM!
Class B | -0.15% | -0.03% | -0.13% | 107% | #NUM!
Class C | -0.20% | -0.09% | -0.18% | 106% | #NUM!
Class E | -0.30% | -0.20% | -0.14% | 107% | #NUM!
Overall | -0.19% | -0.13% | -0.15% | 106% | #NUM!
Class D | -0.17% | -0.01% | -0.06% | 106% | #NUM!
Class F | -0.14% | -0.07% | -0.16% | 103% | #NUM!
*1 test point in Class A2 still running, copied from the anchor.

## Slide 7
We propose to allow directional blending for TIMD predictors
Two predictors computed from left and above templates.
Approach provides -0.19% luma gains for AI with 108% encoder complexity, and -0.10% luma gains for RA for no additional encoder complexity.
Combination with JVET-AB0116 shows gains are mostly additive.
We propose to study this in the next round of the EE.
Summary