## Slide 1: Non-EE2: Gradient and location based convolutional cross-component model (GL-CCCM) for intra prediction JVET-AB0119
Ramin G. Youvalari, Pekka Astola, Jani Lainema

## Slide 2
Chroma samples are predicted using (downsampled) luma samples in the spirit of CCLM modes:
predChromaVal = c0C + c1N + c2S + c3E + c4W + c5P + c6B
Input to the above convolution consists of the 7 filter coefficients ci and:
Collocated luma sample C and its neighbors N, S, W, E
Nonlinear term P:
P = ( C*C + midVal ) >> bitDepth
Bias term B:
B = midVal
Convolutional cross-component model (CCCM)

## Slide 3
Chroma samples are predicted using 7-tap filter:
predChromaVal = c0C + c1Gy + c2Gx + c3Y + c4X + c5P + c6B
Gy and Gx are the vertical and horizontal gradients, respectively:
Gy = (2N + NW + NE) – (2S + SW + SE)
Gx = (2W + NW + SW) – (2E + NE + SE)
Y and X are the vertical and horizontal coordinate/location of the center sample with respect to the top-left coordinates of the block.
Rest of the parameters are the same as CCCM tool:
  Center spatial luma sample
  Nonlinear term
  Bias term
Gradient and Location based convolutional cross-component model (GL-CCCM)

## Slide 4
GL-CCCM uses the same solver as CCCM for coefficients calculation
GL-CCCM uses the same reference area as CCCM for model derivation
GL-CCCM is used as a sub-mode of CCCM
  Supports both single-model and multi-model case
Signaling using a single flag which
  Enables/disables single model GL-CCCM if CCCM is enabled and intra mode is LM_CHROMA_IDX
  Enables/disables dual model GL-CCCM if if CCCM is enabled and intra mode is MMLM_CHROMA_IDX
Encoder search
RDO check for both single model and dual model GL-CCCM mode
Further details

## Slide 5
Experimental results

## Slide 6
Integration with EE2-1.13
EE2-1.13 proposes two extensions for CCCM:
EE2-1.13.A: Extend the CCLM template selection to CCCM to use left, top or top and left templates for model derivation.
EE2-1.13.B: MMLM fusion is replaced with multi-model CCCM fusion. More specifically, the predictors of a non-CCLM chroma mode can be fused with the predictors of multi-model CCCM mode. The derivation of fusion weights is kept unchanged.
Similar extensions as in EE2-1.13.A
6 modes are defined for GL-CCCM method in which the tool can use top or left or top and left templates in both single-model and multi-model cases.
Same SATD check as in EE is considered for the new modes. It doesn’t increase maximum number of full-RDOs compared to EE tests.

## Slide 7
Experimental results on top of EE2-1.13.A

## Slide 8
Experimental results on top of EE2-1.13.B

## Slide 9
Proposing gradient and location based CCCM
Provides further coding efficiency improvements in ECM
The coding gains are additive to the CCCM extensions in EE2-1.13
Has minimal impact on encoder/decoder runtimes
It is suggested to include the technique in the next round of EEs.
Summary