## Slide 1: JVET-AB0142 AHG12: optimizing the use of available decoded reference samples
Thierry Dumas, Kévin Reuzé, Ya Chen, Karam Naser

## Slide 2: 1. Three small optimization of the available decoded reference samples
1.1. Partial MPM reordering depending on the available decoded reference samples
neighboring luma CB mode being a “less probable” mode placed after the other neighboring luma CBs modes in the MPM list
1.2. Extension of the DIMD region depending on the available decoded reference samples
DIMD region of decoded reference samples of the current luma CB extended to
decoded reference samples on the above-right side of the current luma CB available
last vertical positive modes viewed as “less probable” (66, 65, 64, 63, 62) for square CB
decoded reference samples on the bottom-left side of the current luma CB available
first horizontal positive modes viewed as “less probable” (2, 3, 4, 5, 6 for square CB)
MPM list being created
0 49 64 65 …
64
65
reserve
above-right, up to available ones
bottom-left, up to available ones

## Slide 3: 1. Three small optimization of the available decoded reference samples
1.3. Wide-angle modes for TIMD depending on the available decoded reference samples
current luma CB with TIMD
availability of decoded reference samples on above-right/bottom-left checked
addition of wide-angle modes in the TIMD derivation step for the available sides
Example: luma CB, 8 above-right decoded reference samples available
adding first 10 wide-angle vertical positive modes

## Slide 4
3. Results in ECM-6.0
 | All Intra Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,06% | -0,13% | -0,01% | 101% | 100%
Class A2 | -0,04% | -0,06% | -0,06% | 101% | 101%
Class B | -0,07% | 0,00% | -0,03% | 100% | 101%
Class C | -0,06% | -0,04% | -0,13% | 100% | 102%
Class E | -0,04% | 0,01% | -0,19% | 101% | 101%
Overall | -0,05% | -0,04% | -0,08% | 100% | 101%
Class D | -0,06% | -0,10% | -0,08% | 102% | 102%
Class F | -0,06% | -0,09% | 0,05% | 100% | 102%
Class TGM |  |  |  |  | 
 | Random Access Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0,05% | -0,05% | 0,01% | 101% | 101%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -0,04% | 0,03% | -0,24% | 100% | 101%
Class C | -0,02% | -0,18% | -0,06% | 101% | 100%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0,04% | 0,07% | -0,02% | 101% | 101%
Class F | -0,01% | 0,01% | -0,21% | 101% | 101%
Class TGM |  |  |  |  | 

## Slide 5
Three simple optimizations of the available decoded reference of a luma CB yield
  AI: -0.05% -0.04% -0.08%
  RA ~ -0.03% at the current state of the simulations.
4. Conclusion
Thanks for your attention Thanks to b-com for cross-checking
Suggestion
Going to EE2.

## Slide 6
3. Results: early combination with JVET-AB0116
 | All Intra Main 10 |  |  |  | 
 | Over ECM-6.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class C | -0.13% | -0.04% | -0.19% | 102% | 103%
Class E | -0.18% | -0.07% | -0.31% | 98% | 103%
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.09% | -0.01% | -0.02% | 101% | 109%
Class F | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!