## Slide 1: JVET-AC0059 AHG12: TMP using Reconstruction-Reordered for screen content coding (RR-TMP)
Jung-Kyung Lee, Damian Ruiz Coll, Vikas Warudkar

## Slide 2: Summary
Proposals
  TMP using Reconstruction-Reordered (RR-TMP) for screen content coding for SCC.
Experimental Results
  AI: Class F -0.14%, 0.08%, -0.12%, 101%, 101%; Class TGM -0.28%, -0.25%, -0.24%, 101%, 104%
  RA: Class F -0.06%, -0.27%, -0.14%, 100%, 100%; Class TGM -0.16%, -0.27%, -0.14%, 100%, 100%

## Slide 3: TMP using Reconstruction-Reordered (RR-TMP)
TMP block is flipped according to flip type, horizontal or vertical flip, and used as a prediction block.
Search for the most similar template to the flipped template in a predefined search range.
Horizontal flip
TMP
Vertical flip
CB

## Slide 4: Predefined area for RR-TMP
Horizontal flip : partial of the current CTU (R1) and left region (R4)
Vertical flip : partial of the current CTU (R1) and above region (R3)
Figure 1. RR-TMP search region for (a) horizontal flip, and (b) vertical flip.
SRW: 5* CbWidth
SRH: 5* CbHeight

## Slide 5: Results
On top of ECM-7.0:

## Slide 6: Conclusion
TMP using Reconstruction-Reordered (RR-TMP) for screen content coding for SCC.
Average of {-0.21%, -0.09%, -0.18%} coding gain in Class F/TGM.
Moderate complexity of 101%(ENC) and 103%(DEC).