## Slide 1: JVET-AD0308 Non-EE2: Extension of unified PDPC
Gagan Rath, Thierry Dumas, Fabrice Le Léannec, Kevin Reuzé

## Slide 2: Unified PDPC for intra angular modes
PDPC: pdpcScale >= 0
Gradient PDPC: pdpcScale < 0
P(x,y) = P(x,y) + (wL * G(-1,y’) + 32) >> 6;
G(-1,y’) = R(-1,y’) - P(x,y);
wL = 32 >> (2*x >> scale);
scale = pdpcScale
P(x,y) = Clip(P(x,y) + (wL * G(-1,y) + 32) >> 6);
G(-1,y) = R(-1,y) – R(x’’,-1);
wL = 32 >> (2*x >> scale);
scale = (Log2(height) + Log2(width) - 2) >> 2;

## Slide 3
P(x,y) = Clip(P(x,y) + (wL * G(-1,y’) + * (G(-1,y)-G(-1,y’)) + 32) >> 6)
= wL >> (2 + 2*scale);
P(x,y) = Clip(P(x,y) + (wL * G(-1,y) + * (G(-1,y’)-G(-1,y)) + 32) >> 6)
= wL >> (2 - 2*pdpcScale)
G(-1,y’) = R(-1,y’) – P(0,y);
1. Combine PDPC and gradient PDPC
Three refinements:
Eqv. to PDPC for pdpcScale >= 2
Eqv. to grad PDPC for pdpcScale <= -2

## Slide 4
3. Turn off unified PDPC when the side neighbor is not available
2. Use 4-tap filter for interpolation instead
of nearest neighbor or linear interpolation

## Slide 5
Simulation results
Thanks
 | All Intra Main 10 |  |  |  | 
 | Over ECM-8.0-IDG |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.03% | -0.09% | 100% | 103%
Class A2 | -0.04% | -0.10% | 0.02% | 101% | 98%
Class B | -0.05% | -0.05% | -0.09% | 100% | 98%
Class C | -0.04% | -0.09% | -0.17% | 103% | 103%
Class E | -0.05% | -0.06% | 0.00% | 100% | 102%
Overall | -0.04% | -0.06% | -0.08% | 101% | 101%
Class D | -0.06% | -0.12% | -0.07% | 101% | 104%
Class F | -0.04% | -0.11% | -0.05% | 99% | 97%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
 | Random Access Main 10 |  |  |  | 
 | Over ECM-8.0-IDG |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class B | -0.02% | -0.02% | -0.06% | 98% | 97%
Class C | -0.02% | -0.21% | -0.04% | 101% | 101%
Class E |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!
Class D | -0.01% | 0.03% | 0.01% | 103% | 105%
Class F | -0.09% | -0.34% | -0.18% | 102% | 103%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM!