## Slide 1: Changes on TIMD and SGPM for ECM decoder acceleration
JVET-AExxxx
Sharp Corporation
Zheming Fan
Tomohiro Ikai
Yukinobu Yasugi

## Slide 2: Introduction
Copyright © All rights reserved, SHARP CORPORATION
With each update, ECM has gradually become more complex, manifested primarily by an increase in runtime. This proposal aims to reduce the comlexity of the ECM decoder. There are two changes made in this proposal for ECM.
The first change is replacing timdHor and timdVer with dimdHor and dimdVer in the SGPM candidate list. This allows for the SGPM method to be used without the need to run the additional template matching process of TIMD.
The second change involves reducing the number of template matching / number of candidate in TIMD.

## Slide 3: Replacing cu.timdVer and cu.timdHor with cu.dimdVer and cu.dimdHor
SGPM method requires derivation of a partition mode and two angular modes. Regarding angular modes, a candidate list is generated. This list generation involves the use of two angular modes generated by the TIMD method, namely cu.timdVer and cu.timdHor. This necessitates running the TIMD method before running SGPM.
This change replaces cu.timdVer and cu.timdHor with two angular modes, cu.dimdVer and cu.dimdHor, derived by the DIMD method, thus breaking the association between SGPM and TIMD. The derivation of cu.dimdVer and cu.dimdHor are derived using the DIMD method from the top and left reference.
Copyright © All rights reserved, SHARP CORPORATION

## Slide 4: Removing modes with less selection frequently from TIMD candidate list
Copyright © All rights reserved, SHARP CORPORATION
The TIMD method generates two prediction modes. The generation is based on a candidate list. The candidate list consists of two parts: the first part is copied from the MPM list (which contains 22 prediction modes), and the second part is appended based on an add list ({DC_IDX, HOR_IDX, VER_IDX}).
Then the SATD cost is calculated for each mode in the candidate list, and a selection is made. However, the selection frequency of each mode is different. Therefore, this change proposes to remove the less frequently selected ones, in order to reduce the complexity of TIMD method.

## Slide 5: Removing modes with less selection frequently from TIMD candidate list
Figure illustrates the selection of each mode in the candidate list. It can be observed that modes of first half of the MPM list and the add list are selected with a relatively high frequently.
First, iterate through the MPM list and identify the elements in the add list that are not included in the MPM list. The number of such elements, denoted as 'n', will determine the length of the new candidate list. If n is 0, 1, 2, or 3, the length of the new candidate list will be 11, 12, 12, or 13, respectively (which is half of the original length in the same scenario).
Before green line plus after red line

## Slide 6: Results
 | All Intra Main10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.03% | 0.07% | 0.04% | 99% | 98%
Class A2 | 0.04% | 0.03% | 0.06% | 99% | 96%
Class B | 0.03% | 0.12% | 0.14% | 99% | 95%
Class C | 0.03% | 0.03% | 0.05% | 99% | 93%
Class E | 0.08% | 0.16% | 0.23% | 99% | 95%
Overall | 0.04% | 0.08% | 0.10% | 99% | 95%
Class D | 0.07% | 0.17% | 0.18% | 100% | 92%
Class F | -0.01% | 0.07% | 0.10% | 98% | 96%
 | Random Access Main 10 |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.04% | -0.17% | 0.02% | 101% | 101%
Class A2 | 0.04% | 0.02% | -0.04% | 101% | 101%
Class B | 0.04% | 0.14% | -0.14% | 100% | 101%
Class C | 0.08% | -0.10% | 0.09% | 100% | 100%
Class E |  |  |  |  | 
Overall | 0.05% | -0.01% | -0.03% | 100% | 101%
Class D | 0.05% | -0.37% | -0.11% | 99% | 101%
Class F | 0.00% | -0.08% | 0.21% | 99% | 100%

## Slide 7: Conclusion
Copyright © All rights reserved, SHARP CORPORATION
This proposal includes two changes, targeting the SGPM and TIMD methods, with the aim of reducing the complexity of ECM. Based on the experiment, we obtained the following results:
AI: 0.04% 0.08% 0.10% 99% 95%
RA: 0.05% -0.01% -0.03% 100% 101%
Thanks OPPO Corporation for crosschecking!