## Slide 1: JVET-AE0114 AHG10: Low-Delay configuration improvements
Jack Enhorn
Per Wennersten
Ericsson AB

## Slide 2: Introduction
In Random Access compression efficiency is boosted considerably by high quality periodic intra pictures
For Low-Delay coding the benefits from the first and only intra pictures dissipates with the distance
This contribution proposes a LD coding structure with periodic higher quality “boost” pictures

## Slide 3: Proposed method overview
Four aspects of coding structure modification
  Adjusted IntraQPOffset, from -1 to -3
  Every 64th picture boosted from QP +1 to -2
  Adjusted reference structure with longer reference distances in a GOP-16 configuration too better utilize the boosted pictures
  The “middle” picture in the GOP-16 get an adjusted QP to +3

## Slide 4: Detailed description
Intra QP offset
  Simple configuration change
  IntraQPOffset : -3
Boost picture QP adjustment
  Added to new parameters to the software, applied in getQPForPicture()
  LowdelayBoostPeriod : 64
  LowdelayBoostQPOffset : -3
if ((getIntraPeriod() == -1) && (getLowdelayBoostPeriod() > 0) && (pSlice->getPOC() % getLowdelayBoostPeriod() == 0) )
{
qp += getLowdelayBoostQPOffset();
}

## Slide 5: Detailed description (cont.)
Reference picture structure adjustments
  First reference in RPL (previous picture) kept as anchor
  The rest are increased in distance to approximately the double
QPOffset set to 3 for Frame8
Anchor | Proposed method
POC 48 ( QP 23 ) [L0 47 40 32 24] [L1 47c 46 44 16] POC 49 ( QP 28 ) [L0 48 40 32 24] [L1 48c 46 44 16] POC 50 ( QP 26 ) [L0 49 48 40 32] [L1 49c 48 46 24] POC 51 ( QP 28 ) [L0 50 48 40 32] [L1 50c 48 46 24] POC 52 ( QP 26 ) [L0 51 48 40 32] [L1 51c 50 48 24] POC 53 ( QP 28 ) [L0 52 48 40 32] [L1 52c 50 48 24] POC 54 ( QP 26 ) [L0 53 48 40 32] [L1 53c 52 48 24] POC 55 ( QP 28 ) [L0 54 48 40 32] [L1 54c 52 48 24] POC 56 ( QP 23 ) [L0 55 48 40 32] [L1 55c 54 52 24] POC 57 ( QP 28 ) [L0 56 48 40 32] [L1 56c 54 52 24] POC 58 ( QP 26 ) [L0 57 56 48 40] [L1 57c 56 54 32] POC 59 ( QP 28 ) [L0 58 56 48 40] [L1 58c 56 54 32] POC 60 ( QP 26 ) [L0 59 56 48 40] [L1 59c 58 56 32] POC 61 ( QP 28 ) [L0 60 56 48 40] [L1 60c 58 56 32] POC 62 ( QP 26 ) [L0 61 56 48 40] [L1 61c 60 56 32] POC 63 ( QP 28 ) [L0 62 56 48 40] [L1 62c 60 56 32] POC 64 ( QP 23 ) [L0 63 56 48 40] [L1 63c 62 60 32] | POC 48 ( QP 23 ) [L0 47 32 16 0] [L1 47c 44 40 32] POC 49 ( QP 28 ) [L0 48 32 16 0] [L1 48c 44 40 32] POC 50 ( QP 26 ) [L0 49 32 16 0] [L1 49c 48 44 32] POC 51 ( QP 28 ) [L0 50 48 32 16] [L1 50c 48 44 0] POC 52 ( QP 26 ) [L0 51 48 32 16] [L1 51c 48 44 0] POC 53 ( QP 28 ) [L0 52 48 32 16] [L1 52c 48 44 0] POC 54 ( QP 26 ) [L0 53 48 32 16] [L1 53c 52 44 0] POC 55 ( QP 28 ) [L0 54 48 32 16] [L1 54c 52 48 0] POC 56 ( QP 25 ) [L0 55 48 32 16] [L1 55c 52 48 0] POC 57 ( QP 28 ) [L0 56 48 32 16] [L1 56c 52 48 0] POC 58 ( QP 26 ) [L0 57 48 32 16] [L1 57c 56 48 0] POC 59 ( QP 28 ) [L0 58 48 32 16] [L1 58c 56 48 0] POC 60 ( QP 26 ) [L0 59 48 32 16] [L1 59c 56 48 0] POC 61 ( QP 28 ) [L0 60 48 32 16] [L1 60c 56 48 0] POC 62 ( QP 26 ) [L0 61 48 32 16] [L1 61c 60 56 0] POC 63 ( QP 28 ) [L0 62 48 32 16] [L1 62c 60 56 0] POC 64 ( QP 20 ) [L0 63 48 32 16] [L1 63c 60 56 0]

## Slide 6: QP-hierarchy

## Slide 7: Objective results
 | Low delay B |  |  |  | 
 | Over VTM-20.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -2,28% | -6,73% | -7,10% | 107% | 100%
Class C | -6,48% | -9,72% | -9,33% | 111% | 98%
Class E | -10,06% | -17,19% | -20,67% | 104% | 99%
Overall | -5,62% | -10,34% | -11,24% | 107% | 99%
Class D | -2,55% | -8,99% | -9,24% | 105% | 98%
Class F | -7,60% | -8,23% | -8,00% | 104% | 98%
 | Low delay P |  |  |  | 
 | Over VTM-20.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -1,13% | -5,70% | -6,32% | 103% | 99%
Class C | -6,19% | -9,32% | -8,95% | 98% | 100%
Class E | -9,60% | -17,11% | -19,87% | 97% | 101%
Overall | -4,94% | -9,76% | -10,58% | 99% | 100%
Class D | -2,23% | -10,02% | -9,62% | 101% | 100%
Class F | -5,30% | -5,57% | -5,21% | 102% | 100%
 | Low delay B |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B* | -1,23% | -3,88% | -5,45% | 104% | 100%
Class C | -6,05% | -10,04% | -8,74% | 99% | 99%
Class E | -7,84% | -16,44% | -17,15% | 105% | 100%
Overall | -4,49% | -9,08% | -9,47% | 103% | 100%
Class D | -3,02% | -7,06% | -7,73% | 101% | 99%
Class F | -2,62% | -2,63% | -2,36% | 99% | 100%
Class TGM | 1,23% | 1,98% | 2,21% | 99% | 99%
 | Low delay P |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,05% | -2,56% | -3,82% | 99% | 99%
Class C | -5,53% | -8,73% | -7,56% | 97% | 98%
Class E | -7,00% | -15,84% | -16,71% | 99% | 100%
Overall | -3,57% | -7,94% | -8,29% | 99% | 99%
Class D | -2,28% | -6,82% | -7,22% | 99% | 100%
Class F | -2,83% | -2,39% | -1,77% | 98% | 99%
Class TGM | -2,46% | -2,74% | -2,32% | 105% | 102%
*Estimated, anchor results copied for BQTerrace and BasketballDrive QP 22

## Slide 8: Subjective results
Better quality at static (and slow moving) areas, faster recover when object goes from moving to static
Better stability around moving foreground objects
Figure 3: Anchor
Figure 4: Proposed method

## Slide 9: Conclusion
The Low-Delay settings presented has significant objective and subjective gains over current settings
  Especially large gains on low-delay content (Class E)
It is proposed to adopt the method to VTM and ECM software and CTC
Thanks to Nokia for crosschecking!

## Slide 11: VTM 5 second results vs ECM
 | Low delay B |  |  |  | 
 | Over VTM-20.0 5s |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0,90% | -5,03% | -5,66% | 112% | 104%
Class C | -6,02% | -10,42% | -9,24% | 112% | 113%
Class E | -7,96% | -15,33% | -18,85% | 104% | 101%
Overall | -4,37% | -9,40% | -10,15% | 110% | 106%
Class D | -2,78% | -8,67% | -8,90% | 108% | 112%
Class F | -2,41% | -2,38% | -1,48% | 103% | 101%
 | Low delay P |  |  |  | 
 | Over VTM-20.0 5s |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,09% | -3,60% | -4,61% | 100% | 98%
Class C | -5,41% | -9,53% | -8,74% | 97% | 99%
Class E | -7,61% | -15,14% | -18,16% | 98% | 95%
Overall | -3,67% | -8,46% | -9,37% | 99% | 97%
Class D | -2,41% | -9,35% | -8,01% | 99% | 95%
Class F | -2,71% | -2,23% | -2,36% | 97% | 95%
 | Low delay B |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B* | -1,23% | -3,88% | -5,45% | 104% | 100%
Class C | -6,05% | -10,04% | -8,74% | 99% | 99%
Class E | -7,84% | -16,44% | -17,15% | 105% | 100%
Overall | -4,49% | -9,08% | -9,47% | 103% | 100%
Class D | -3,02% | -7,06% | -7,73% | 101% | 99%
Class F | -2,62% | -2,63% | -2,36% | 99% | 100%
Class TGM | 1,23% | 1,98% | 2,21% | 99% | 99%
 | Low delay P |  |  |  | 
 | Over ECM-9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0,05% | -2,56% | -3,82% | 99% | 99%
Class C | -5,53% | -8,73% | -7,56% | 97% | 98%
Class E | -7,00% | -15,84% | -16,71% | 99% | 100%
Overall | -3,57% | -7,94% | -8,29% | 99% | 99%
Class D | -2,28% | -6,82% | -7,22% | 99% | 100%
Class F | -2,83% | -2,39% | -1,77% | 98% | 99%
Class TGM | -2,46% | -2,74% | -2,32% | 105% | 102%

## Slide 12
IntraQPOffset : -3
LowdelayBoostPeriod : 64
LowdelayBoostQPOffset : -3
# Type POC QPoffset QPOffsetModelOff QPOffsetModelScale CbQPoffset CrQPoffset QPfactor tcOffsetDiv2 betaOffsetDiv2 CbTcOffsetDiv2 CbBetaOffsetDiv2 CrTcOffsetDiv2 CrBetaOffsetDiv2 temporal_id #ref_pics_active_L0 #ref_pics_L0 reference_pictures_L0 #ref_pics_active_L1 #ref_pics_L1 reference_pictures_L1
Frame1: B 1 6 -6.5 0.2450 0 0 1.0 0 0 0 0 0 0 0 4 4 1 17 33 49 4 4 1 5 9 65
Frame2: B 2 4 -6.5 0.2590 0 0 1.0 0 0 0 0 0 0 0 4 4 1 18 34 50 4 4 1 2 6 66
Frame3: B 3 6 -6.5 0.2450 0 0 1.0 0 0 0 0 0 0 0 4 4 1 3 19 35 4 4 1 3 7 51
Frame4: B 4 4 -6.5 0.2590 0 0 1.0 0 0 0 0 0 0 0 4 4 1 4 20 36 4 4 1 4 8 52
Frame5: B 5 6 -6.5 0.2450 0 0 1.0 0 0 0 0 0 0 0 4 4 1 5 21 37 4 4 1 5 9 53
Frame6: B 6 4 -6.5 0.2590 0 0 1.0 0 0 0 0 0 0 0 4 4 1 6 22 38 4 4 1 2 10 54
Frame7: B 7 6 -6.5 0.2450 0 0 1.0 0 0 0 0 0 0 0 4 4 1 7 23 39 4 4 1 3 7 55
Frame8: B 8 3 0.0 0.0 0 0 1.0 0 0 0 0 0 0 0 4 4 1 8 24 40 4 4 1 4 8 56
Frame9: B 9 6 -6.5 0.2450 0 0 1.0 0 0 0 0 0 0 0 4 4 1 9 25 41 4 4 1 5 9 57
Frame10: B 10 4 -6.5 0.2590 0 0 1.0 0 0 0 0 0 0 0 4 4 1 10 26 42 4 4 1 2 10 58
Frame11: B 11 6 -6.5 0.2450 0 0 1.0 0 0 0 0 0 0 0 4 4 1 11 27 43 4 4 1 3 11 59
Frame12: B 12 4 -6.5 0.2590 0 0 1.0 0 0 0 0 0 0 0 4 4 1 12 28 44 4 4 1 4 12 60
Frame13: B 13 6 -6.5 0.2450 0 0 1.0 0 0 0 0 0 0 0 4 4 1 13 29 45 4 4 1 5 13 61
Frame14: B 14 4 -6.5 0.2590 0 0 1.0 0 0 0 0 0 0 0 4 4 1 14 30 46 4 4 1 2 6 62
Frame15: B 15 6 -6.5 0.2450 0 0 1.0 0 0 0 0 0 0 0 4 4 1 15 31 47 4 4 1 3 7 63
Frame16: B 16 1 0.0 0.0 0 0 1.0 0 0 0 0 0 0 0 4 4 1 16 32 48 4 4 1 4 8 64

## Slide 13: Example bits per picture
Chart: