## Slide 1
BBAAD9C20180234D78A0072836F0B3D0B2B9B20E1D588B80A6D98633B1632B763B49B8389164AB0322992F08C846F5EB8AF9210AA1D0AB611BBFC213736E25D824F696AD582596B794A028E767D246FE7E02E0E17042018528CAA19A31EE9C28DE16269C4E3
AHG 8: A spatial resampling algorithm and an exemplar software implementation
Shurun Wang, Binzhe Li, Jie Chen, Yan Ye, Shiqi Wang
Jul. 2023

## Slide 2: Outline
Architecture
Analysis and Resampling
Performance
Conclusion

## Slide 3: Architecture
The architecture of software implementation:
  Pre-analysis
  Spatial downsampling
  Encoder and Decoder (VTM)
  Spatial upsampling
  Machine consumption

## Slide 4: Outline
Architecture
Analysis and Resampling
Performance
Conclusion

## Slide 5: Analysis
Analysis: distinguish videos with different characteristics and use corresponding pre-processing methods.
  Characteristics :
    Resolution: the larger resolution of the input video, the better for spatial resampling
    Further analysis: Averaged object ratio, measuring the spatial complexity
      Perform object detection analysis on the input video
      Achieve object region proportion () and object number ()
      Calculate the averaged object ratio (),
      Make decision based on object number () and averaged object ratio ()
Resolution | Larger than 1920x1080 | Equal to 1920x1080 | Smaller than 1920x1080
Decision | Spatial resampling | Further analysis | No spatial resampling
Object number () | Averaged object ratio () | Decision
 |  | Spatial resampling
Others | Others | No spatial resampling
 |  | Decision
 |  | Spatial resampling
Others | Others | No spatial resampling

## Slide 6: Resampling
Network Structure of the spatial resampling network
  Spatial downsampling
  Lightweight spatial upsampling
Model size of spatial upsampling | Model size of spatial upsampling with NNC lossless compression
177540 bytes | 42495 bytes
x2
Notes: Original net_rec with 20 layers, 2676137 bytes(without NNC)

## Slide 7: Showcase for using NNPF for VCM
Syntax | Value | Syntax | Value
nnpfc_purpose | 0x04 | nnpfc_out_format_idc | 1
nnpfc_mode_idc | 0 | nnpfc_out_order_idc | 2
nnpfc_num_input_pics_minus1 | 0 | nnpfc_out_tensor_luma_bitdepth_minus8 | 2
nnpfc_pic_width_num_minus1 | 1 | nnpfc_out_tensor_chroma_bitdepth_minus8 | 2
nnpfc_pic_width_denom_minus1 | 0 | nnpfc_chroma_loc_info_present_flag | 0
nnpfc_pic_height_num_minus1 | 1 | nnpfc_overlap | 0
nnpfc_pic_height_denom_minus1 | 0 | nnpfc_constant_patch_size_flag | 1
nnpfc_component_last_flag | 0 | nnpfc_patch_width_minus1 | CroppedWidth − 1
nnpfc_inp_format_idc | 1 | nnpfc_patch_height_minus1 | CroppedHeight − 1
nnpfc_auxiliary_inp_idc | 0 | nnpfc_padding_type | 0
nnpfc_inp_order_idc | 2 | nnpfc_complexity_info_present_flag | 0
nnpfc_inp_tensor_luma_bitdepth_minus8 | 2 | nnpfc_metadata_extension_num_bits | 0
nnpfc_inp_tensor_chroma_bitdepth_minus8 | 2 |  | 

## Slide 8: Outline
Architecture
Analysis and Resampling
Performance
Conclusion

## Slide 9: Performance: Option1-Strict
The overall Pareto BD-rate savings over VVC
  For TVD video dataset, no sequence is selected to resample: SAME with the anchor
 | RA |  | AI |  | LD | 
Sequence Name | Pareto BD-rate | BD-mAP | Pareto BD-rate | BD-mAP | Pareto BD-rate | BD-mAP
Traffic_2560x1600_30 | -13.16% | 0.53 | -20.37% | 3.07 | -31.67% | 3.73
ParkScene_1920x1080_24 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
Cactus_1920x1080_50 | -64.65% | 20.08 | -50.43% | 28.42 | -42.18% | 24.14
BasketballDrive_1920x1080_50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
BQTerrace_1920x1080_60 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
BasketballDrill_832x480_50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
BQMall_832x480_60 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
PartyScene_832x480_50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
RaceHorses_832x480_30 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
BasketballPass_416x240_50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
BQSquare_416x240_60 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
BlowingBubbles_416x240_50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
RaceHorses_416x240_30 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
AVG | -5.99% | 1.59 | -5.45% | 2.42 | -5.68% | 2.14

## Slide 10: Performance: Option2-Loose
For SFU-HW dataset
 | RA |  | AI |  | LD | 
Sequence Name | Pareto BD-rate | BD-mAP | Pareto BD-rate | BD-mAP | Pareto BD-rate | BD-mAP
Traffic_2560x1600_30 | -10.37% | 0.90 | -20.37% | 3.07 | -31.67% | 3.73
ParkScene_1920x1080_24 | -6.14% | 0.71 | 0.14% | 0.11 | 19.66% | -1.99
Cactus_1920x1080_50 | -67.60% | 13.61 | -50.43% | 28.42 | -42.18% | 24.14
BasketballDrive_1920x1080_50 | 2.64% | -0.59 | -1.55% | 0.38 | -6.13% | 0.75
BQTerrace_1920x1080_60 | -8.92% | 2.04 | -13.02% | 2.41 | -14.80% | 3.13
BasketballDrill_832x480_50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
BQMall_832x480_60 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
PartyScene_832x480_50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
RaceHorses_832x480_30 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
BasketballPass_416x240_50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
BQSquare_416x240_60 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
BlowingBubbles_416x240_50 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
RaceHorses_416x240_30 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
AVG | -6.95% | 1.28 | -6.56% | 2.65 | -5.78% | 2.29

## Slide 11: Performance: Option2-Loose
For TVD video dataset
 | RA |  | AI |  | LD | 
Sequence Name | Pareto BD-rate | BD-mAP | Pareto BD-rate | BD-mAP | Pareto BD-rate | BD-mAP
TVD-01_1 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
TVD-01_2 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
TVD-01_3 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00 | 0.00
TVD-02_1 | 18.12% | -1.11 | 12.91% | -0.75 | -18.72% | 1.94
TVD-03_1 | 18.10% | -2.22 | 18.05% | -2.96 | 4.95% | -0.98
TVD-03_2 | -15.88% | 0.91 | 11.57% | -0.92 | 3.87% | 0.13
TVD-03_3 | -3.83% | 0.53 | -11.09% | 1.86 | -7.61% | 0.87
Average | 2.36% | -0.27 | 4.49% | -0.40 | -2.50% | 0.28

## Slide 12: Performance: Image dataset
For TVD image dataset
  Object detection and instance segmentation task
Object detection |  |  |  |  |  | Instance segmentation |  |  |  |  | 
VTM-12.0 |  | Proposed |  | Pareto BD-rate | BD-mAP | VTM-12.0 |  | Proposed |  | Pareto BD-rate | BD-mAP
bpp | mAP | bpp | mAP | -0.14% | 0.31 | bpp | mAP | bpp | mAP | -6.35% | 0.57
0.475 | 55.748 | 0.198 | 52.030 | -0.14% |  | 0.475 | 45.005 | 0.198 | 42.188 | -6.35% | 
0.266 | 53.752 | 0.116 | 48.690 |  |  | 0.266 | 43.822 | 0.116 | 39.218 |  | 
0.145 | 50.632 | 0.061 | 44.617 |  |  | 0.145 | 40.746 | 0.061 | 35.872 |  | 
0.075 | 45.311 | 0.030 | 34.770 |  |  | 0.075 | 36.796 | 0.030 | 27.103 |  | 
0.037 | 38.586 | 0.015 | 18.672 |  |  | 0.037 | 29.091 | 0.015 | 18.158 |  | 
0.017 | 20.155 | 0.007 | 6.538 |  |  | 0.017 | 18.346 | 0.007 | 7.305 |  | 
Notes: 0.31 0.57

## Slide 13: Outline
Architecture
Analysis and Resampling
Performance
Conclusion

## Slide 14: Conclusion
Propose a lightweight spatial resampling network
Achieve performance gain on various datasets and machine tasks, especially for large resolution
Provide a showcase for using NNPF for VCM
Suggest including proposed spatial resampling software and algorithm into the next version of the technical report (TR)
  Optimization of encoders and receiving systems for machine analysis of coded video content (JVET-AE2030)

## Slide 15
Thanks
BBAAD9C20180234D78A0072836F0B3D0B2B9B20E1D588B80A6D98633B1632B763B49B8389164AB0322992F08C846F5EB8AF9210AA1D0AB611BBFC213736E25D824F696AD582596B794A028E767D246FE7E02E0E17042018528CAA19A31EE9C28DE16269C4E3