## Slide 1: JVET-AE0163 Ahg 12: modified CTC proposal for low-delay configuration
Saurabh Puri, Charles Bonnineau, Fabrice Le Léannec, Tangi Poirier, Edouard François

## Slide 2: Motivation
Revisit of previous contribution (JVET-AD0128) with slight modification and additional tests
ECM encoding time for LDB is problematic for investigating new coding tools
ECM-9.0 encoding time has increased by an average 23.1% in LDB compared to the ECM-8.0
worst case LDB (BQ Terrace QP22) takes approx. 17.5 days to complete

## Slide 3: Proposal in JVET-AD0128
Increase Maximum MTT depth in I slice:
    MaxBTLumaISlice=128
    MaxBTChromaISlice=128
    MaxTTLumaISlice=128
    MaxTTChromaISlice=128
    MaxMTTHierarchyDepthISliceL=4
    MaxMTTHierarchyDepthISliceC=4
Reduce maximum MTT depth in slices with slice temporal depth >= 2
    MaxMTTHierarchyDepthByTidOverrideByQP: 22 332222
    (for class B and ArenaOfValor, QP 22)

## Slide 4: Current Proposal
Test 1:
  Increase Maximum MTT depth in I slice:
      MaxBTLumaISlice=128
      MaxBTChromaISlice=128
      MaxTTLumaISlice=128
      MaxTTChromaISlice=128
      MaxMTTHierarchyDepthISliceL=4
      MaxMTTHierarchyDepthISliceC=4
  Reduce maximum MTT depth in slices with slice temporal depth >= 2
    MaxMTTHierarchyDepthByTidOverrideByQP: 22 332222
    (for class B and ArenaOfValor, QP 22)
Test 2:
  Reduce maximum MTT depth in slices with slice temporal depth >=2
    MaxMTTHierarchyDepthByTidOverrideByQP: 22 332222
    (for class B QP 22)
* No CTC change for Class F

## Slide 5: Impact on performances
 | Low delay B Main 10 |  |  |  | 
 | Over ECM 9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | -0.01% | -0.35% | -0.22% | 89.5% | 94.6%
Class C | -0.06% | -1.13% | -0.53% | 110.5% | 108.0%
Class E | -0.32% | -3.60% | -1.45% | 105.1% | 106.5%
Overall | -0.10% | -1.42% | -0.63% | 99.9% | 101.8%
Class D | -0.13% | 0.43% | -1.64% | 98.9% | 100.4%
Class F | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay P Main 10 |  |  |  | 
 | Over ECM 9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.00% | -0.38% | -0.06% | 100.6% | 109.3%
Class C | -0.07% | -0.69% | -0.10% | 107.6% | 112.9%
Class E | -0.28% | -4.08% | -1.90% | 99.0% | 98.0%
Overall | -0.09% | -1.41% | -0.53% | 102.5% | 107.5%
Class D | -0.11% | 1.13% | -1.35% | 102.2% | 99.1%
Class F | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
TEST 1
TEST 2
 | Low delay B Main 10 |  |  |  | 
 | Over ECM 9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.10% | 0.18% | 0.19% | 89.9% | 96.6%
Class C | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class E | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Overall | 0.04% | 0.08% | 0.08% | 95.7% | 98.6%
Class D | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class F | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay P Main 10 |  |  |  | 
 | Over ECM 9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.11% | 0.29% | 0.24% | 92.0% | 106.0%
Class C | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class E | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Overall | 0.04% | 0.12% | 0.10% | 96.6% | 102.5%
Class D | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class F | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 6: Impact on LDB worst cases in Test 1 and Test 2
TEST 1
TEST 2
 | ECM-9.0, low-delay B, QP=22 (Test 1) |  |  |  |  | 
 | Reference |  | Test |  |  | 
Sequence | Enc T [h] | Enc T [d] | Enc T [h] | Enc T [d] | ΔEnc T [d] | EncR
MarketPlace | 323,84 | 13,49 | 231.16 | 9,63 | -3,86 | 0,71
RitualDance | 227,99 | 9,50 | 151.63 | 6,32 | -3,18 | 0,67
Cactus | 276,95 | 11,54 | 181.29 | 7,55 | -3,99 | 0,65
BasketballDrive | 354,87 | 14,79 | 240.03 | 10,00 | -4,78 | 0,68
BQTerrace | 418,83 | 17,45 | 285.71 | 11,90 | -5,55 | 0,68
 | ECM-9.0, low-delay B, QP=22 (Test 2) |  |  |  |  | 
 | Reference |  | Test |  |  | 
Sequence | Enc T [h] | Enc T [d] | Enc T [h] | Enc T [d] | ΔEnc T [d] | EncR
MarketPlace | 323,84 | 13,49 | 223,31 | 9,30 | -4,19 | 0,69
RitualDance | 227,99 | 9,50 | 160,59 | 6,69 | -2,81 | 0,70
Cactus | 276,95 | 11,54 | 188,22 | 7,84 | -3,70 | 0,68
BasketballDrive | 354,87 | 14,79 | 235,71 | 9,82 | -4,97 | 0,66
BQTerrace | 418,83 | 17,45 | 270,99 | 11,29 | -6,16 | 0,65

## Slide 7: Applying proposed changes to VTM11-ECM9 anchor
Test 1 VTM11-ECM9 encoder configuration:
  MaxBTLumaISlice=128
  MaxBTChromaISlice=64
  MaxTTLumaISlice=64
  MaxTTChromaISlice=64
  MaxMTTHierarchyDepthISliceL=4
  MaxMTTHierarchyDepthISliceC=4
  MaxMTTHierarchyDepthByTidOverrideByQP: 22 332222 (class B only)
Test 2 VTM11-ECM9 encoder configuration:
  MaxMTTHierarchyDepthByTidOverrideByQP: 22 332222 (class B only)

## Slide 8: Applying proposed changes to VTM11-ECM9 anchor
TEST 1
TEST 2
 | Low delay B Main 10 |  |  |  | 
 | Over VTM11ecm9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.09% | 0.69% | -0.38% | 89.4% | 99.6%
Class C | -0.10% | -0.05% | -0.12% | 99.5% | 101.1%
Class E | -0.17% | -1.46% | -0.31% | 113.4% | 111.9%
Overall | -0.04% | -0.10% | -0.28% | 98.3% | 103.1%
Class D | -0.04% | 0.28% | -0.09% | 112.7% | 113.4%
Class F | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay P Main 10 |  |  |  | 
 | Over VTM11ecm9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.07% | 0.98% | 0.47% | 88.7% | 108.4%
Class C | -0.10% | -0.03% | -0.32% | 104.0% | 101.6%
Class E | -0.19% | -0.20% | -0.70% | 104.2% | 103.7%
Overall | -0.05% | 0.35% | -0.09% | 97.4% | 104.9%
Class D | -0.04% | 0.21% | -0.63% | 102.9% | 112.6%
Class F | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay B Main 10 |  |  |  | 
 | Over VTM11ecm9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.13% | 0.31% | 0.32% | 86.3% | 98.2%
Class C | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class E | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Overall | 0.06% | 0.13% | 0.13% | 94.0% | 99.2%
Class D | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class F | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
 | Low delay P Main 10 |  |  |  | 
 | Over VTM11ecm9.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.11% | 0.34% | 0.43% | 84.9% | 103.7%
Class C | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class E | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Overall | 0.05% | 0.14% | 0.18% | 93.4% | 101.5%
Class D | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class F | 0.00% | 0.00% | 0.00% | 100.0% | 100.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 9: Conclusion
Modification to CTCs is proposed to significantly reduce worst-case encoding time of ECM for both LDB and LDP.
Worst-case encoder runtime (BQTerrace QP 22) is reduced by more than 6 days, hence more convenient to use in practice
Performance impact of the proposed modifications on ECM-9.0 compared to its anchor is negligible
Propose to adopt Test 2 CTC modifications for next JVET cycle
Thanks to Qualcomm for cross-checking.