## Slide 1: JVET-AF0104: Non-EE2: Direct Decoder-side Intra Mode Derivation for IntraTMP blocks
Junyan Huo, Nengfu Qiu, Yanzhuo Ma,
Fuzheng Yang(Xidian Univ.), Ming Li(OPPO)
October. 2023

## Slide 2: Introduction
IntraTMP in ECM10.0
  Use the template to determine the BV and generate initial predictions
  Use the final predictions to derive intraTmpDimdMode for the transform procedure

## Slide 3: Proposed method
Intra TMP in ECM 10.0

## Slide 4: Proposed method
Use the initial predictions to derive intraTmpDimdMode.
The dependency of generating the final predictions and deriving intraTmpDimdMode can be eliminated, which can be processed in parallel
Intra TMP in proposed method

## Slide 5: Experimental results and conclusion
IntraTMP with Direct DIMD
 | All Intra Main 10 |  |  |  |  | 
 | Over anchor |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 | 0.01% | 0.06% | -0.11% | 100.1% | 100.5% | 99.9%
Class A2 | 0.00% | -0.04% | -0.02% | 99.8% | 100.3% | 100.0%
Class B | 0.01% | -0.06% | -0.07% | 99.9% | 99.6% | 100.0%
Class C | -0.01% | 0.01% | 0.06% | 100.8% | 100.7% | 100.0%
Class E | 0.01% | 0.02% | -0.20% | 99.7% | 99.8% | 100.0%
Overall | 0.00% | -0.01% | -0.06% | 100.1% | 100.2% | 100.0%
Class D | 0.04% | -0.04% | -0.02% | 98.3% | 100.9% | 100.0%
Class F | -0.02% | -0.02% | 0.04% | 98.9% | 99.6% | 100.0%
Class TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0!

## Slide 6: Conclusion
This contribution is proposed that using the initial predictions to derive intraTmpDimdMode
Friendly parallelism
On top of ECM-10.0
  AI: -0.00%, -0.01%, -0.06%, 100.1%,100.2%
  No coding loss
  No EncT or DecT increase
Recommend to investigate in EE2
Thanks to Alibaba for crosscheck

## Slide 7
Thank you