## Slide 1: JVET-AF0106 EE2-related: non-adjacent spatial candidates for DIMD merge
Junyan Huo, Jiawei Fan, Zhenyao Zhang, Yanzhuo Ma,
Fuzheng Yang(Xidian Univ.), Ming Li(OPPO)
Oct. 2023

## Slide 2: Introduction
DIMD HoG
DIMD in ECM10.0
EE2-2.1: DIMD merge
  1. Construct DIMD blocks list
    Neighbouring blocks are checked
    Reorder these blocks based on spatial distances
  2. Derive a merged HoG with maximum 5 DIMD blocks
  3. Determine intra-prediction modes
Current CU
DIMD Merge HoG
Notes:   To investigate whether it is coded with DIMD-related modes or not

## Slide 3: Proposed method
Add non-adjacent spatial candidates after the current candidates
Similar to that in the MPM list construction

## Slide 4: Experimental results
  On the top of ECM10.0
  On the top of EE2-2.1
  Test 2.1a：DIMD merge
  Test 2.1b：DIMD merge with reduced storage
test2.1a+proposed | All Intra Main10 |  |  |  | 
 | Over ECM-10.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.13% | 0.02% | -0.09% | #DIV/0! | #DIV/0!
Class A2 | -0.16% | -0.03% | -0.09% | #DIV/0! | #DIV/0!
Class B | -0.12% | 0.06% | -0.06% | #DIV/0! | #DIV/0!
Class C | -0.11% | 0.08% | 0.12% | #DIV/0! | #DIV/0!
Class E | -0.05% | 0.05% | -0.17% | #DIV/0! | #DIV/0!
Overall | -0.12% | 0.04% | -0.05% | #DIV/0! | #DIV/0!
Class D | -0.04% | -0.02% | -0.12% | #DIV/0! | #DIV/0!
Class F | -0.11% | -0.03% | -0.06% | #DIV/0! | #DIV/0!
TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
test2.1b+proposed | All Intra Main10 |  |  |  | 
test2.1b+proposed | Over ECM-10.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.13% | 0.05% | -0.06% | #DIV/0! | #DIV/0!
Class A2 | -0.15% | -0.10% | -0.02% | #DIV/0! | #DIV/0!
Class B | -0.12% | 0.02% | -0.02% | #DIV/0! | #DIV/0!
Class C | -0.11% | 0.06% | 0.16% | #DIV/0! | #DIV/0!
Class E | -0.06% | 0.03% | -0.08% | #DIV/0! | #DIV/0!
Overall | -0.11% | 0.02% | 0.00% | #DIV/0! | #DIV/0!
Class D | -0.03% | 0.21% | 0.14% | #DIV/0! | #DIV/0!
Class F | -0.10% | 0.09% | 0.12% | #DIV/0! | #DIV/0!
TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
test2.1a+proposed | All Intra Main10 |  |  |  | 
 | Over EE2.1a |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | -0.19% | 0.00% | #DIV/0! | #DIV/0!
Class A2 | -0.06% | 0.00% | -0.04% | #DIV/0! | #DIV/0!
Class B | -0.06% | 0.00% | 0.04% | #DIV/0! | #DIV/0!
Class C | -0.05% | 0.05% | 0.04% | #DIV/0! | #DIV/0!
Class E | -0.01% | 0.04% | -0.13% | #DIV/0! | #DIV/0!
Overall | -0.05% | -0.01% | -0.01% | #DIV/0! | #DIV/0!
Class D | -0.02% | -0.13% | -0.02% | #DIV/0! | #DIV/0!
Class F | -0.04% | -0.05% | -0.12% | #DIV/0! | #DIV/0!
TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!
test2.1b+proposed | All Intra Main10 |  |  |  | 
test2.1b+proposed | Over EE2.1b |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.04% | 0.04% | -0.01% | #DIV/0! | #DIV/0!
Class A2 | -0.04% | -0.06% | 0.04% | #DIV/0! | #DIV/0!
Class B | -0.04% | -0.04% | 0.02% | #DIV/0! | #DIV/0!
Class C | -0.05% | 0.04% | 0.03% | #DIV/0! | #DIV/0!
Class E | -0.02% | -0.09% | 0.00% | #DIV/0! | #DIV/0!
Overall | -0.04% | -0.02% | 0.02% | #DIV/0! | #DIV/0!
Class D | 0.00% | 0.22% | 0.14% | #DIV/0! | #DIV/0!
Class F | -0.04% | 0.05% | 0.10% | #DIV/0! | #DIV/0!
TGM | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0!

## Slide 5: Conclusion
Add non-adjacent spatial candidates after the current candidates in DIMD merge.
It is expected that no large encoding time and decoding time increase.
On top of ECM-10.0
  test a AI: -0.12% 0.04% -0.05%
  test b AI: -0.11% 0.02% -0.00%
On top of EE2-2.1a
  test a AI: -0.05% -0.01% -0.01%
On top of EE2-2.1b
  test b AI: -0.04% -0.02% 0.02%
Recommend to investigate in EE.
Thanks to Alibaba for crosscheck.

## Slide 6
Thank you