## Slide 1: JVET-AF0111 AHG10 MTT split modes early termination
Waqas Ahmad, Per Wennersten, Kenneth Andersson
Ericsson

## Slide 2: Background
In the last JVET meeting, the proposal JVET-AE0057 was adopted for VTM and ECM softwares.
The contribution was enabled for ECM CTC, and to enable it in VTM CTC, it was suggested to further investigate the proposal for low QP values and for different input bit depths.
In this contribution, we also tested high QP values and suggested to update the threshold to obtain better trade-off between coding gain and encoding time reduction for high QP values.

## Slide 3
In JVET-AE0057, a condition is applied on the no-split cost of 64x64 luma CUs.
If the no-split cost is greater than a threshold, MTT splitting will not be investigated.
The threshold in JVET-AE0057 is set based on QP value as follows:
  (1)
We present following tests in this contribution,
  Test 1.1 (VTM SDR, Proposed condition is applied to CTC QPs, i.e., 22, 27, 32, 37)
  Test 1.2 (VTM SDR, Proposed condition is applied to low QP values, i.e., 12, 17, 19, 22)
  Test 1.3 (VTM SDR, Proposed condition is applied to high QP values, i.e., 37,42,47,52)
  Test 2 (VTM HDR, Proposed condition is applied to HDR CTC QPs, i.e., 22, 27, 32, 37)
  Test 3 (VTM HBD, Proposed condition is applied to high bit depth normal QP range, i.e., 22, 27, 32, 37)
Proposal

## Slide 4: Test 1.1: VTM SDR CTC normal QP values QP 22, 27, 32, 37
 | Random access |  |  |  | 
 | BD-rate Over VTM-20.2 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | -0.03% | -0.03% | 0.02% | 98.0% | 100.0%
Class A2 | 0.06% | 0.08% | 0.07% | 95.7% | 100.1%
Class B | 0.03% | 0.05% | 0.06% | 96.0% | 100.0%
Class C | 0.01% | 0.04% | 0.05% | 94.0% | 100.1%
Class E |  |  |  |  | 
Overall | 0.02% | 0.04% | 0.05% | 95.8% | 100.1%
Class D | 0.03% | -0.22% | 0.06% | 96.2% | 99.2%
Class F | 0.18% | 0.21% | 0.22% | 95.0% | 99.9%
 | Low delay B Main 10 |  |  |  | 
 | BD-rate Over VTM-20.2 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
Class B | 0.06% | 0.71% | 0.51% | 95.6% | 99.9%
Class C | 0.05% | 0.31% | -0.10% | 93.9% | 99.8%
Class E | 0.03% | 0.41% | 0.04% | 97.5% | 99.6%
Overall | 0.05% | 0.50% | 0.19% | 95.5% | 99.8%
Class D | 0.03% | 0.62% | -0.45% | 95.9% | 99.7%
Class F | 0.27% | 0.29% | -0.48% | 95.7% | 99.9%
Results
 | Low Delay B |  |  |  | 
 | BD-rate Over ECM9.0 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Overall | 0.05% | -0.06% | -0.20% | 96.8% | 100.0%
 | Random access |  |  |  | 
 | BD-rate Over ECM9.0 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Overall | 0.03% | 0.06% | 0.11% | 97.0% | 99.9%
ECM Results presented in JVET-AE0057

## Slide 5: Test 1.2: VTM SDR CTC Low QP values QP 12, 17, 19, 22
Results
 | Random access |  |  |  | 
 | BD-rate Over VTM-20.2 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.09% | 0.27% | 0.15% | 92.7% | 100.1%
Class A2 | 0.10% | 0.12% | 0.14% | 87.1% | 99.9%
Class B | 0.04% | 0.12% | 0.21% | 91.7% | 100.2%
Class C | 0.03% | 0.10% | 0.05% | 93.1% | 99.6%
Overall | 0.06% | 0.14% | 0.14% | 91.3% | 99.9%
Class D | 0.01% | -0.01% | 0.02% | 96.1% | 99.7%
Class F | 0.29% | 0.19% | 0.18% | 93.3% | 99.9%

## Slide 6
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM 20.2 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.01% | 0.00% | 0.02% | -0.02% | 0.09% | 0.02% | -0.04% | 0.08% | 97.7% | 100.1%
Class H2 |  |  |  |  |  | 0.02% | -0.03% | -0.02% | 98.9% | 99.7%
Overall | 0.01% | 0.00% | 0.02% | -0.02% | 0.09% | 0.02% | -0.04% | 0.04% | 98.1% | 100.0%
Test 2: VTM HDR CTC normal QP values QP 22, 27, 32, 37
Results
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM 20.2 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.07% | 0.03% | 0.01% | -0.02% | 0.11% | 0.01% | -0.03% | 0.10% | 97.4% | 99.6%
Class H2 |  |  |  |  |  | 0.04% | 0.20% | 0.17% | 96.9% | 99.9%
Overall | 0.07% | 0.03% | 0.01% | -0.02% | 0.11% | 0.03% | 0.09% | 0.14% | 97.2% | 99.7%
Test 3: VTM HBD CTC normal QP values QP 22, 27, 32, 37

## Slide 7
 | Random access |  |  |  | 
 | BD-rate Over VTM-20.2 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.00% | 0.02% | 0.00% | 100.5% | 99.4%
Class A2 | 0.00% | 0.04% | 0.02% | 99.6% | 100.3%
Class B | 0.02% | 0.06% | -0.05% | 99.8% | 100.0%
Class C | -0.02% | -0.22% | -0.21% | 98.9% | 99.1%
Overall | 0.00% | -0.03% | -0.07% | 99.7% | 99.7%
Class D | -0.09% | -0.21% | -0.02% | 99.0% | 99.6%
Class F | 0.03% | 0.07% | 0.05% | 99.1% | 100.1%
Test 1.3: VTM SDR CTC High QP values
QP 37, 42, 47, 52
Results
 | Random access |  |  |  | 
 | BD-rate Over VTM-20.2 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.09% | 0.36% | 0.21% | 98.4% | 100.3%
Class A2 | 0.27% | 0.48% | 0.50% | 96.2% | 99.8%
Class B | 0.23% | 0.41% | 0.36% | 97.4% | 99.9%
Class C | 0.35% | 0.45% | 0.45% | 94.6% | 99.6%
Overall | 0.24% | 0.43% | 0.38% | 96.6% | 99.9%
Class D | 0.15% | 0.25% | 0.31% | 94.7% | 99.2%
Class F | 0.37% | 0.67% | 0.53% | 96.1% | 99.6%
New Threshold
Old Threshold
Additional study on high QP values
The threshold in JVET-AF0111 is set based on QP value as follows:
  (2)
Notes: 12 17 19 22 27 32 37 42 47 52 57 62
160 140 132 120 100 80 60 40 20 0 -20 -40
150 135 129 120 105 90 75 60 45 30 15 0

## Slide 8: Test 4.1: ECM SDR CTC normal QP values QP 22, 27, 32, 37
 | Random access |  |  |  | 
 | BD-rate Over ECM-10 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | -0.01% | -0.27% | 0.12% | 100.4% | 99.9%
Class A2 | -0.39% | -0.27% | -0.23% | 103.1% | 99.2%
Class B | -0.49% | -0.21% | -0.57% | 103.6% | 100.2%
Class C | -0.62% | -0.45% | -0.72% | 103.8% | 99.8%
Overall | -0.41% | -0.30% | -0.40% | 102.9% | 99.8%
Class D | -0.25% | -0.38% | -0.51% | 103.3% | 100.9%
Class F | -0.08% | -0.16% | -0.19% | 101.9% | 100.0%
Class TGM | -0.37% | -0.46% | -0.59% | 103.6% | 100.5%
Test 4.2: ECM SDR CTC High QP values
QP 37, 42, 47, 52
 | Random access |  |  |  | 
 | BD-rate Over ECM-10 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.01% | -0.10% | 0.04% | 100.1% | 100.3%
Class A2 | -0.01% | -0.22% | -0.01% | 101.4% | 99.1%
Class B | -0.02% | 0.22% | 0.01% | 100.5% | 99.0%
Class C | -0.01% | -0.05% | -0.08% | 100.6% | 99.6%
Overall | -0.01% | 0.00% | -0.01% | 100.6% | 99.4%
Class D | -0.01% | 0.10% | 0.02% | 100.8% | 99.7%
Class F | 0.03% | 0.00% | 0.03% | 100.4% | 99.5%
Class TGM | -0.05% | 0.01% | -0.03% | 100.6% | 99.6%
Results
Additional study on High QP values

## Slide 9: Test 1.2: VTM SDR CTC Low QP values QP 12, 17, 19, 22
 | Random access |  |  |  | 
 | BD-rate Over VTM-20.2 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.10% | 0.32% | 0.16% | 92.1% | 100.0%
Class A2 | 0.10% | 0.11% | 0.15% | 85.8% | 100.1%
Class B | 0.05% | 0.13% | 0.21% | 91.2% | 100.0%
Class C | 0.02% | 0.12% | 0.10% | 92.7% | 100.3%
Overall | 0.06% | 0.16% | 0.16% | 90.7% | 100.1%
Class D | 0.01% | -0.01% | 0.02% | 96.1% | 99.3%
Class F | 0.29% | 0.20% | 0.17% | 93.5% | 99.3%
Results
 | Random access |  |  |  | 
 | BD-rate Over VTM-20.2 |  |  |  | 
 | Y-PSNR | U-PSNR | V-PSNR | EncT | DecT
Class A1 | 0.09% | 0.27% | 0.15% | 92.7% | 100.1%
Class A2 | 0.10% | 0.12% | 0.14% | 87.1% | 99.9%
Class B | 0.04% | 0.12% | 0.21% | 91.7% | 100.2%
Class C | 0.03% | 0.10% | 0.05% | 93.1% | 99.6%
Overall | 0.06% | 0.14% | 0.14% | 91.3% | 99.9%
Class D | 0.01% | -0.01% | 0.02% | 96.1% | 99.7%
Class F | 0.29% | 0.19% | 0.18% | 93.3% | 99.9%
New Threshold
Old Threshold

## Slide 10: Test 2: VTM HDR CTC normal QP values (New Threshold ) QP 22, 27, 32, 37
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM 20.2 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.05% | 0.02% | 0.02% | 0.12% | 0.08% | 0.02% | 0.13% | 0.09% | 97.9% | 99.8%
Class H2 |  |  |  |  |  | 0.00% | -0.03% | 0.09% | 99.0% | 99.6%
Overall | 0.05% | 0.02% | 0.02% | 0.12% | 0.08% | 0.01% | 0.08% | 0.09% | 98.3% | 99.7%
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM 20.2 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.01% | 0.00% | 0.02% | -0.02% | 0.09% | 0.02% | -0.04% | 0.08% | 97.7% | 100.1%
Class H2 |  |  |  |  |  | 0.02% | -0.03% | -0.02% | 98.9% | 99.7%
Overall | 0.01% | 0.00% | 0.02% | -0.02% | 0.09% | 0.02% | -0.04% | 0.04% | 98.1% | 100.0%
Test 2: VTM HDR CTC normal QP values (Old Threshold) QP 22, 27, 32, 37
Results

## Slide 11: Test 2: VTM HBD CTC normal QP values (New Threshold ) QP 22, 27, 32, 37
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM 20.2 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.12% | 0.02% | 0.01% | 0.06% | 0.12% | 0.00% | 0.03% | 0.08% | 98.0% | 100.0%
Class H2 |  |  |  |  |  | 0.05% | 0.15% | 0.08% | 97.7% | 100.1%
Overall | 0.12% | 0.02% | 0.01% | 0.06% | 0.12% | 0.03% | 0.09% | 0.08% | 97.8% | 100.1%
 | Random Access |  |  |  |  |  |  |  |  | 
 | Over VTM 20.2 |  |  |  |  |  |  |  |  | 
 |  |  | wPSNR |  |  | PSNR |  |  |  | 
 | DE100 | PSNR-L100 | Y | U | V | Y | U | V | EncT | DecT
Class H1 | 0.07% | 0.03% | 0.01% | -0.02% | 0.11% | 0.01% | -0.03% | 0.10% | 97.4% | 99.6%
Class H2 |  |  |  |  |  | 0.04% | 0.20% | 0.17% | 96.9% | 99.9%
Overall | 0.07% | 0.03% | 0.01% | -0.02% | 0.11% | 0.03% | 0.09% | 0.14% | 97.2% | 99.7%
Test 3: VTM HBD CTC normal QP values (Old Threshold) QP 22, 27, 32, 37
Results

## Slide 12: Summary
This contribution present further study of JVET-AE0057.
Test 1.1 & 1.2 shows on average encoding time reduction for VTM SDR contents with limited degradation in the overall coding gain.
Test 2 & 3 shows on average encoding time reduction for HDR and HBD contents with limited degradation in the overall coding gain.
The threshold calculation is modified compared to JVET-AE0057 to improve the trade-off between encoding time reduction and coding loss for high QP values (shown in Test 1.3 & 4.2).
Thanks to InterDigital for cross-checking.

## Slide 13
Thank you