## Slide 1: JVET-AF0176: Non-EE2: Decoder Derived Cross-Component Prediction
Yao-Jen Chang, Po-Han Lin, Vadim Seregin, Jian-Liang Lin, Marta Karczewicz

## Slide 2: Current ECM
Different types of CCP modes are applied to ECM-10
  Cross-component linear model (CCLM)
    Slope adjustment of CCLM
    Gradient LM (GLM)
  Convolutional cross-component intra prediction mode (CCCM)
    No-subsampled CCCM
    CCCM with multiple downsampling filters (CCCMwMDF)
    Gradient and location based CCCM (GLCCCM)
    Block-vector guided CCCM (BVG-CCCM)
  Local-boosting CCP (LB-CCP)
  CCP merge (CCPmerge, also called non-local CCP)
Issue: The current CCP design causes an inefficient signaling while the best CCP mode for a chroma CU in a specific case is the one using longest bits

## Slide 3: Proposed method
A decoder derived cross-component prediction (DDCCP) is proposed with a DDCCP flag signaled
  When this DDCCP flag is true, a CCP mode list is constructed, and the best CCP mode is derived by comparing the template costs between the CCP modes in the list
A decoder-derived CCP fusion mode is also introduced to derive CCP modes for fusion selected based on the template costs
Template
Template

## Slide 4: Test results
Test 1: CCP list constructed by {CCCM, CCCMwMDF, GLCCCM} with the constraint of (CU_Width * CU_Height > 64).
Test 2: CCP list constructed by {CCCM, CCCMwMDF, GLCCCM} with the constraint of (CU_Width * CU_Height > 8).
Test 3: CCP list constructed by {CCLM, CCCM, CCCMwMDF, GLCCCM, LBCCP} with the constraint of (CU_Width * CU_Height > 8).
 | All Intra Main 10 |  | 
 | Over ECM-10.0 |  | 
 | Y | U | V
Class A1 | -0.10% | -0.64% | -0.64%
Class A2 | -0.19% | -0.53% | -0.59%
Class B | -0.11% | -0.03% | -0.12%
Class C | -0.14% | 0.28% | 0.36%
Class E | -0.18% | -0.14% | -0.03%
Overall | -0.14% | -0.16% | -0.16%
Class D | -0.10% | 0.42% | 0.22%
Class F | -0.11% | 0.13% | 0.36%
 | All Intra Main 10 |  |  |  | 
 | Over ECM-10.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07% | -0.75% | -0.79% | 101.3% | 107.1%
Class A2 | -0.15% | -0.64% | -0.74% | 103.2% | 106.0%
Class B | -0.09% | -0.24% | -0.34% | 101.7% | 106.0%
Class C | -0.10% | -0.01% | 0.11% | 104.0% | 103.5%
Class E | -0.10% | -0.25% | -0.08% | 101.2% | 105.2%
Overall | -0.10% | -0.34% | -0.34% | 102.3% | 105.5%
Class D | -0.06% | -0.04% | 0.12% | 100.0% | 105.6%
Class F | -0.09% | 0.00% | 0.02% |  | 
 | All Intra Main 10 |  |  |  | 
 | Over ECM-10.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.08% | -0.74% | -0.84% | 101.0% | 105.9%
Class A2 | -0.14% | -0.64% | -0.78% | 102.0% | 103.9%
Class B | -0.08% | -0.18% | -0.30% | 101.3% | 104.4%
Class C | -0.05% | -0.06% | -0.05% | 102.2% | 98.4%
Class E | -0.10% | -0.32% | -0.35% | 102.0% | 105.7%
Overall | -0.08% | -0.34% | -0.42% | 101.6% | 103.4%
Class D | -0.01% | 0.01% | 0.00% | 101.8% | 102.5%
Class F | -0.01% | -0.01% | 0.03% | 103.5% | 105.3%
Test 1
Test 2
Test 3

## Slide 5: RA results
Test 2: CCP list constructed by {CCCM, CCCMwMDF, GLCCCM} with the constraint of (CU_Width * CU_Height > 8)
 | All Intra Main 10 |  |  |  | 
 | Over ECM-10.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.07% | -0.75% | -0.79% | 101.3% | 107.1%
Class A2 | -0.15% | -0.64% | -0.74% | 103.2% | 106.0%
Class B | -0.09% | -0.24% | -0.34% | 101.7% | 106.0%
Class C | -0.10% | -0.01% | 0.11% | 104.0% | 103.5%
Class E | -0.10% | -0.25% | -0.08% | 101.2% | 105.2%
Overall | -0.10% | -0.34% | -0.34% | 102.3% | 105.5%
Class D | -0.06% | -0.04% | 0.12% | 100.0% | 105.6%
Class F | -0.09% | 0.00% | 0.02% |  | 
 | Random Access Main 10 |  |  |  | 
 | Over ECM-10.0 |  |  |  | 
 | Y | U | V | EncT | DecT
Class A1 |  |  |  |  | 
Class A2 |  |  |  |  | 
*Class B | -0.09% | 0.33% | 0.13% |  | 
Class C | -0.04% | -0.03% | -0.01% |  | 
Class E |  |  |  |  | 
Overall |  |  |  |  | 
Class D | -0.05% | 0.03% | 0.05% |  | 
**Class F | -0.03% | -0.29% | -0.03% |  | 
* 7 rate points copied from anchor
** 3 rate points copied from anchor