## Slide 1: Non-EE2: Adaptive coefficient precision for CCALF JVET-AG0065
Nan Song, Yue Yu, Haoping Yu, Dong Wang

## Slide 2: Introduction – fixed precision value in current ECM for CCALF
The CCALF training process
  Calculate float-type coefficients from Weiner-Hopf equation
  Calculate the temp coefficients
  Get the final coefficients by mapping each element of to
The CCALF filtering process
The precision value for both Cb and Cr is set to 7-bit in the current ECM.

## Slide 3: Proposed – adaptive coefficient precision for CCALF
The CCALF training process
  Precision candidate list is set to be {7, 8, 9, 10}
  Select the best precision value and corresponding coefficients

## Slide 4: Simulation results
Proposed method vs ECM-11.0
 | All Intra Main10 |  |  |  | 
 |  |  | Over ECM-11.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | 0.00% | -0.09% | -0.09% | 100.3% | 100.7%
Class A2 | 0.00% | -0.17% | -0.10% | 100.3% | 100.4%
Class B | 0.00% | -0.24% | -0.41% | 100.2% | 101.0%
Class C | 0.01% | -0.17% | -0.25% | 100.1% | 99.8%
Class E | 0.01% | -0.30% | -0.32% | 100.1% | 100.4%
Overall | 0.00% | -0.20% | -0.25% | 100.2% | 100.5%
Class D | 0.02% | -0.26% | -0.47% | 100.3% | 99.7%
Class F | 0.01% | -0.42% | -0.47% | 100.3% | 100.3%
 | Random access Main10 |  |  |  | 
 |  |  | Over ECM-11.0 |  | 
 | Y | U | V | EncT | DecT
Class A1 | -0.02% | -0.22% | -0.23% | 99.7% | 100.0%
Class A2 | 0.02% | -0.10% | -0.22% | 99.6% | 99.8%
Class B | 0.00% | -0.39% | -0.62% | 100.0% | 99.9%
Class C | 0.01% | -0.25% | -0.35% | 100.0% | 100.1%
Class E |  |  |  |  | 
Overall | 0.00% | -0.26% | -0.39% | 99.9% | 100.0%
Class D | 0.02% | -0.43% | -0.81% | 100.2% | 100.1%
Class F | 0.01% | -0.35% | -0.52% | 100.1% | 99.6%

## Slide 5: Conclusions
This contribution proposes an adaptive coefficient precision instead of a fixed precision for CCALF. The results show that the proposed method can improve the coding efficiency of ECM with negligible complexity change. It is suggested to further study this method in EE2.
Thanks to Qualcomm and ByteDance for cross-checking!