## Slide 1: JVET-AG108 AhG12: Entropy coding extension
Franck Galpin, Federico Lo Bianco, Charles Salmon-Legagneur

## Slide 2: Current coding mode
binarization
Syntax element
decodeBin
Context number
decodeBinEP
bitstream
CABAC
EP

## Slide 3: Proposed coding mode
binarization
Syntax element
decodeBin
decodeBinEP
bitstream
CABAC
EP
decodeBinNEP
Context number
NEP
Context number
NEP: same as CABAC for initial probability setting, then no update.

## Slide 4: Proposed coding mode – during development
binarization
Syntax element
decodeBin
decodeBinEP
bitstream
CABAC
EP
decodeBinNEP
Context number
NEP
Context number
Context number
Systematic context: no normative change, just use during development to improve training opportunities.

## Slide 5: Simulations
Replaced a set of EP coded (flags, unary coded values).
Original CABAC contexts are not touched.
366 new contexts are added.
After training,
- 64 contexts are still using EP coding
- 302 uses the NEP coding
Note:
An additional training test shows that 43 original CABAC contexts can be transformed in EP or NEP.

## Slide 6: Results
runtimes are not reliable
 | All Intra Main 10 |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 | 0.00% | -0.16% | -0.27% | 103.4% | 99.9% | 102.0%
Class A2 | 0.01% | -0.19% | -0.11% | 101.8% | 96.5% | 101.4%
Class B | 0.00% | -0.06% | -0.22% | 102.0% | 98.4% | 96.1%
Class C | 0.00% | -0.18% | -0.12% | 110.3% | 94.1% | 101.7%
Class E | -0.02% | 0.02% | 0.03% | 101.6% | 100.0% | 101.6%
Overall | 0.00% | -0.11% | -0.15% | 103.9% | 97.6% | 100.1%
Class D | -0.02% | -0.21% | -0.13% | 102.3% | 99.6% | 99.6%
Class F | 0.06% | -0.08% | 0.13% | 103.8% | 101.3% | 97.2%
Class TGM | 0.13% | 0.12% | 0.05% | 103.4% | 100.1% | 99.8%
 | Random Access Main 10 |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 | -0.07% | -0.32% | -0.10% | 92.2% | 85.1% | 101.5%
Class A2 | -0.04% | -0.22% | -0.21% | 93.4% | 92.6% | 102.2%
Class B | -0.10% | -0.17% | -0.35% | 94.6% | 91.2% | 100.1%
Class C | -0.10% | -0.20% | -0.19% | 100.5% | 96.3% | 100.0%
Class E |  |  |  |  |  | 
Overall | -0.08% | -0.22% | -0.23% | 95.4% | 91.5% | 100.8%
Class D | -0.06% | -0.33% | -0.59% | 99.5% | 97.0% | 99.2%
Class F | -0.03% | -0.11% | -0.08% | 99.0% | 97.1% | 100.5%
Class TGM | -0.07% | -0.21% | -0.07% | 97.7% | 95.3% | 101.7%
 | Low delay B Main 10 |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  | 
 | Y | U | V | EncT | DecT | VmPeak
Class A1 |  |  |  |  |  | 
Class A2 |  |  |  |  |  | 
Class B | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM!
Class C | 0.09% | -0.12% | -0.64% | 98.5% | 97.4% | #NUM!
Class E | -0.03% | 0.69% | -0.31% | 95.6% | 94.1% | #NUM!
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM!
Class D | -0.05% | -0.93% | -1.34% | 98.9% | 94.7% | #NUM!
Class F | -0.12% | 0.28% | -0.01% | 99.2% | 97.7% | #NUM!
Class TGM | -0.23% | -0.05% | -0.22% | 99.0% | 94.3% | #NUM!

## Slide 7: Conclusion
It is proposed to study these changes in next EE round:
- systematic context during development phase (ratio of CABAC, non CABAC can be choose later)
- study the new NEP mode