## Slide 1
JVET-AG0138 Non-EE2: Chroma intra prediction mode reordering
Xinwei Li, Ru-Ling Liao, Jie Chen, Yan Ye
Alibaba group
BBAAD9C20180234D78A0072836F0B99042B9B20B1A023BA0AAD98430B1382B056B46B738D1636B0C22092308C84662EB99F921AA31D02B511BBFC2F17AAE2DD524FCC1ADE02C8657A4982AF760424ABFE727E5B875AD4FD64887119CFF410CE8DCD624979E3

## Slide 2
BBAAD9C20180234D78A0072836F0B99042B9B20B1A023BA0AAD98430B1382B056B46B738D1636B0C22092308C84662EB99F921AA31D02B511BBFC2F17AAE2DD524FCC1ADE02C8657A4982AF760424ABFE727E5B875AD4FD64887119CFF410CE8DCD624979E3
Introduction
There are 7 non-CCP chroma intra prediction modes in ECM: chroma DBV mode, DM mode, chroma DIMD mode, and four default modes (i.e. planar mode, vertical mode, horizontal mode and DC mode)
A fixed order is used to parse the non-CCP modes:

## Slide 3
Proposed methods
It is proposed to reorder the non-CCP chroma intra prediction modes：
a non-CCP chroma intra prediction mode list is constructed in the following order：
  the 7 non-CCP modes in the current ECM
  the collocated luma modes
  the adjacent chroma modes
  the collocated luma BVs
the list is reordered based on the SAD cost of the collocated luma block
the first N modes in the list can be allowed for the current chroma block (N = 6 or 7 based on the allowance of the chroma DBV mode)
Notes: {4, 8, 12, 16}-pel or {64, 128, 192, 256}-pel

## Slide 4
Proposed methods
It is proposed to reorder the non-CCP chroma intra prediction modes：
the syntax elements to parse the non-CCP chroma intra prediction modes are kept unchanged:
Notes: {4, 8, 12, 16}-pel or {64, 128, 192, 256}-pel

## Slide 5
Simulation results
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.02% | 0.01% | -0.08% | 99.9% | 102.1% | 100.4% | 100.2%
Class A2 | -0.04% | -0.01% | -0.08% | 100.3% | 100.5% | 100.3% | 100.3%
Class B | -0.04% | 0.00% | -0.11% | 100.4% | 101.4% | 101.4% | 100.5%
Class C | -0.07% | -0.08% | -0.07% | 100.5% | 101.5% | 100.4% | 100.2%
Class E | -0.10% | 0.02% | 0.13% | 100.2% | 102.2% | 99.0% | 100.2%
Overall | -0.05% | -0.01% | -0.05% | 100.3% | 101.5% | 100.4% | 100.3%
Class D | -0.07% | -0.15% | 0.02% | 100.4% | 101.3% | 100.4% | 100.1%
Class F | -0.19% | -0.04% | 0.16% | 100.0% | 101.6% | 97.8% | 100.3%
Class TGM | -0.22% | -0.22% | -0.25% | 100.1% | 102.8% | 100.6% | 100.5%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-11.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class B | 0.01% | 0.10% | 0.03% | 99.0% | 98.9% | 99.5% | 100.3%
Class C | -0.01% | -0.08% | 0.04% | 99.0% | 99.0% | 100.3% | 100.2%
Class E |  |  |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #NUM! | #NUM! | #NUM! | #NUM!
Class D | 0.00% | -0.06% | -0.11% | 99.2% | 99.6% | 100.2% | 100.1%
Class F | -0.13% | -0.05% | 0.22% | 99.5% | 99.1% | 100.2% | 100.3%
Class TGM | -0.06% | -0.09% | -0.06% | 99.7% | 99.6% | 99.5% | 100.5%

## Slide 6
Conclusion
non-CCP chroma intra prediction modes reordering was proposed
  -0.05% luma gain for camera-captured contents
  -0.18% luma gain for class F
  -0.22% luma gain for class TGM
It is recommend to further study this proposal in EE2
Thanks to Bytedance for cross-checking

## Slide 7
Thanks
BBAAD9C20180234D78A0072836F0B99042B9B20B1A023BA0AAD98430B1382B056B46B738D1636B0C22092308C84662EB99F921AA31D02B511BBFC2F17AAE2DD524FCC1ADE02C8657A4982AF760424ABFE727E5B875AD4FD64887119CFF410CE8DCD624979E3