## Slide 1
JVET-AH0109 AHG16: Removal of the analysis model on the decoder side and lightweight design
Renjie Zou, Ru-Ling Liao, Bolin Chen, Yan Ye, Jie Chen
Alibaba group
BBAAD9C20180234D78A0072836F0B99042B9B20B1A023BA0AAD98430B1382B056B46B738D1636B0C22092308C84662EB99F921AA31D02B511BBFC2F17AAE2DD524FCC1ADE02C8657A4982AF760424ABFE727E5B875AD4FD64887119CFF410CE8DCD624979E3

## Slide 2
Introduction
Four GFVC methods are supported in AHG16 software including FOMM, FV2V, CFTE, lightweight CFTE
To reduce complexity, we propose to
  remove the analysis model from the decoder for all 4 methods
  replace 3x3 convolution layers with depthwise separable convolution in generative model of lightweight CFTE method

## Slide 3
Removal of the analysis model from the decoder
Directly encode the feature of the base pictures into the bitstream
Allow a more flexible design of the analysis model to be used by the encoder
Does not require any changes to the GFV SEI message under development
Apply to all four GFVC methods

## Slide 4
Complexity reduction of lightweight CFTE method
Generative model has the highest kMACs per pixel among all three models
      Reduce the complexity of generative model by
  halving the channel count
  Replacing 3x3 convolutions with depthwise separable convolutions in the down-sample block
Model | Analysis model | Dense motion model | Generative model
Parameters | 14.1M | 12.3M | 7.9M
kMACs/pixel | 15.1 | 47.9 | 756.1
current design
proposed design

## Slide 5
Simulation results of proposed CFTE
Removal of Analysis model is applied
Small loss is observed over the current design
Number of parameters and kMACs/pixel decrease by 24% and 2%, respectively
 | Proposed CFTE |  |  |  |  |  |  |  |  |  |  | 
 | Over current CFTE |  |  |  |  |  | Over VTM-22.2 |  |  |  |  | 
 | DISTS | LPIPS | RGB444_PSNR | RGB444_SSIM | YUV420_PSNR | YUV420_SSIM | DISTS | LPIPS | RGB444_PSNR | RGB444_SSIM | YUV420_PSNR | YUV420_SSIM
Class A | 1.00% | 1.04% | 0.97% | 0.3% | 1.1% | #VALUE! | -64.40% | -63.28% | -4.73% | -33.0% | -2.1% | -27.2%
Class B | 1.63% | 1.75% | 3.36% | -0.5% | 18.8% | #VALUE! | -54.92% | -51.66% | -1.36% | -21.9% | -6.4% | #VALUE!
Overall | 1.32% | 1.39% | 2.16% | -0.1% | 9.9% | #VALUE! | -59.66% | -57.47% | -3.05% | -27.4% | -4.3% | #VALUE!
 | Parameters | kMACs/pixel
Current CFTE | 58.0M | 851.7
Proposed CFTE | 43.9M | 836.6
* “#VALUE!” means the RD curves cross over each other for some sequences

## Slide 6
Simulation results of proposed FOMM
Removal of Analysis model is applied
Similar observations as those in proposed CFTE over current CFTE
 | Parameters | kMACs/pixel
Current FOMM | 59.8M | 838.0
Proposed FOMM | 45.6M | 818.5
* “#VALUE!” means the RD curves cross over each other for some sequences
 | Proposed FOMM |  |  |  |  |  |  |  |  |  |  | 
 | Over current FOMM |  |  |  |  |  | Over VTM-22.2 |  |  |  |  | 
 | DISTS | LPIPS | RGB444_PSNR | RGB444_SSIM | YUV420_PSNR | YUV420_SSIM | DISTS | LPIPS | RGB444_PSNR | RGB444_SSIM | YUV420_PSNR | YUV420_SSIM
Class A | 1.60% | 1.70% | 4.07% | 2.5% | 24.7% | #VALUE! | -34.49% | -29.84% | 0.00% | 1.3% | 0.0% | #VALUE!
Class B | 3.14% | 3.31% | 12.42% | 3.0% | 11.8% | 3.6% | -30.25% | -27.12% | 5.96% | 1.3% | 2.8% | 10.2%
Overall | 2.37% | 2.50% | 8.24% | 2.7% | 18.3% | #VALUE! | -32.37% | -28.48% | 2.98% | 1.3% | 1.4% | #VALUE!

## Slide 7
Simulation results of proposed FV2V
Removal of Analysis model is applied
Similar observations as those in proposed CFTE over current CFTE
 | Parameters | kMACs/pixel
Current FV2V | 125.1M | 7562.3
Proposed FV2V | 95.0M | 7443.2
 | Proposed FV2V |  |  |  |  |  |  |  |  |  |  | 
 | Over current FV2V |  |  |  |  |  | Over VTM-22.2 |  |  |  |  | 
 | DISTS | LPIPS | RGB444_PSNR | RGB444_SSIM | YUV420_PSNR | YUV420_SSIM | DISTS | LPIPS | RGB444_PSNR | RGB444_SSIM | YUV420_PSNR | YUV420_SSIM
Class A | 1.02% | 1.02% | 0.30% | 0.7% | -3.2% | 0.8% | -51.36% | -50.23% | 0.11% | -20.4% | -0.8% | -19.5%
Class B | 1.89% | 2.06% | 2.78% | 3.9% | 1.7% | 3.2% | -42.03% | -38.85% | 10.63% | -7.6% | 9.4% | -6.1%
Overall | 1.45% | 1.54% | 1.54% | 2.3% | -0.8% | 2.0% | -46.69% | -44.54% | 5.37% | -14.0% | 4.3% | -12.8%

## Slide 8
Simulation results of proposed lightweight CFTE
Removal of Analysis model & Lightweight design are applied
Introduce minor coding loss over the current lightweight CFTE
Significantly reduce the number of parameters and kMACs/pixel
 | Proposed lightweight CFTE |  |  |  |  |  |  |  |  |  |  | 
 | Over current lightweight CFTE |  |  |  |  |  | Over VTM-22.2 |  |  |  |  | 
 | DISTS | LPIPS | RGB444_PSNR | RGB444_SSIM | YUV420_PSNR | YUV420_SSIM | DISTS | LPIPS | RGB444_PSNR | RGB444_SSIM | YUV420_PSNR | YUV420_SSIM
Class A | 1.04% | 2.01% | -2.51% | 2.8% | 0.8% | 1.4% | -67.02% | -65.46% | -3.12% | -34.6% | 0.0% | -29.7%
Class B | -0.28% | 3.97% | 3.41% | 16.9% | 8.0% | 524818.2% | -57.94% | -53.63% | -6.71% | -19.2% | -4.0% | -25.0%
Overall | 0.38% | 2.99% | 0.45% | 9.9% | 4.4% | 262409.8% | -62.48% | -59.54% | -4.91% | -26.9% | -2.0% | -27.3%
 | Parameters | kMACs/pixel
Current lightweight CFTE | 34.3M | 819.1
Proposed lightweight CFTE | 14.2M | 194.2
Reduce by 59%
Reduce by 76%

## Slide 9
Analysis of abnormal number in YUV420_SSIM
Cause by a specific sequence CFVQA_Seq009
Nonmonotone in higher bitrate is observed in this sequence

## Slide 10
Conclusion
Two changes to the AHG16 GFVC software aimed at reducing the complexity:
  removing the analysis model from the decoder of all 4 GFVC methods
  adopting depthwise separable convolutions and halving channel counts in the generative model of the lightweight CFTE method
We recommend to adopt both proposed modifications to the AHG16 GFVC software

## Slide 11
Thanks
BBAAD9C20180234D78A0072836F0B99042B9B20B1A023BA0AAD98430B1382B056B46B738D1636B0C22092308C84662EB99F921AA31D02B511BBFC2F17AAE2DD524FCC1ADE02C8657A4982AF760424ABFE727E5B875AD4FD64887119CFF410CE8DCD624979E3