## Slide 1: [AHG9]: Neural-network post-filter for recovering images from energy-aware images
AH0126, Claire-Hélène DEMARTY, Franck AUMONT, Olivier LE MEUR

## Slide 2: Context (1/2)
The neural-network post-filter characteristics (NNPFC) SEI message includes different purposes for defining and triggering one or more neural-network post-filters.
Use case energy-aware [1]: An energy-aware video, i.e., a video that consumes less at display, is transmitted and rendered at the display side.
Transmission
Input video
Encoding
Decoding
Video coding / Transmission / Video decoding
Pre
-
processing to
reduce the energy
consumption at
the display side
Energy Ratio R
Energy
-
aware video
Energy-aware rendering:
Consumes less energy
Potentially reduced QoE
[1] Sampaio et al. "How to make images less power-hungry: An objective benchmark study." Proceedings of the Second International ACM Green Multimedia Systems Workshop. 2024.

## Slide 3: Context (2/2)
The neural-network post-filter characteristics (NNPFC) SEI message includes different purposes for defining and triggering one or more neural-network post-filters.
Use case energy-aware: An attenuated video, i.e., a video that consumes less at display, is transmitted and rendered at the display side
Transmission
Input video
Encoding
Decoding
Video coding / Transmission / Video decoding
Pre
-
processing to
reduce the energy
consumption at
the display side
Energy Ratio R
Energy
-
aware video
Energy-aware rendering
Consumes less energy
Potentially reduced QoE
Original rendering
?

## Slide 4: Proposal (1/4)
It is proposed to enable recovering an image with a quality close to that of the original at the rendering side through the use of an additional NNPF purpose

## Slide 5: Proposal (2/4)
A new value is added to the nnpfc_purpose field to indicate the activation of the process to recover an image with a quality close to that of the input content, at the expense of more energy consumption.
nnpfc_purpose indicates the purpose of the NNPF as specified in Table 1, where (nnpfc_purpose & bitmask) not equal to 0 indicates that the NNPF has the purpose associated with the BitMask value in Table 1.
The value of nnpfc_purpose shall be in the range of 0 to 127255, inclusive, in bitstreams conforming to this edition of this document. Values of 128256 to 65 535, inclusive, for nnpfc_purpose are reserved for future use by ITU-T | ISO/IEC and shall not be present in bitstreams conforming to this edition of this document. Decoders conforming to this edition of this document shall ignore NNPFC SEI messages with nnpfc_purpose in the range of 128256 to 65 535, inclusive
bitMask | Interpretation
0x01 | General visual quality improvement
0x02 | Chroma upsampling (from the 4:2:0 chroma format to the 4:2:2 or 4:4:4 chroma format, or from the 4:2:2 chroma format to the 4:4:4 chroma format)
0x04 | Resolution resampling (increasing or decreasing the width or height)
0x08 | Picture rate upsampling
0x10 | Bit depth upsampling (increasing the luma bit depth or the chroma bit depth)
0x20 | Colourization
0x40 | Temporal extrapolation (i.e., generating one or more future pictures)
0x80 | Reverse energy aware reconstruction (i.e., reconstructing an image with a quality close to that of the original image while increasing the energy consumption)

## Slide 6: Proposal (3/4)
The SEI message syntax is therefore modified as followed (modifications are highlighted in yellow).

## Slide 7: Proposal (4/4)
Semantic:
The variables ChromaUpsamplingFlag, ResolutionResamplingFlag, PictureRateUpsamplingFlag, BitDepthUpsamplingFlag, ColourizationFlag, TemporalExtrapolatingFlag, and ReverseEnergyAwareFlag, specifying whether nnpfc_purpose indicates the purpose of the NNPF to include chroma upsampling, resolution resampling, picture rate upsampling, bit depth upsampling, colourization, temporal extrapolation, and reverse the energy-aware reconstruction respectively, are derived as follows:
ChromaUpsamplingFlag = ( ( nnpfc_purpose & 0x02 ) > 0 ) ? 1 : 0 ResolutionResamplingFlag = ( ( nnpfc_purpose & 0x04 ) > 0 ) ? 1 : 0 PictureRateUpsamplingFlag = ( ( nnpfc_purpose & 0x08 ) > 0 ) ? 1 : 0 BitDepthUpsamplingFlag = ( ( nnpfc_purpose & 0x10 ) > 0 ) ? 1 : 0 ColourizationFlag = ( ( nnpfc_purpose & 0x20 ) > 0 ) ? 1 : 0 TemporalExtrapolationFlag = ( ( nnpfc_purpose & 0x40 ) > 0 ) ? 1 : 0
ReverseEnergyAwareFlag = ( ( nnpfc_purpose & 0x80 ) > 0 ) ? 1 : 0
nnpfc_energy_recovering_ratio, when ReverseEnergyAwareFlag is equal to 1, specifies the amount of energy recovery the post-filter should achieve. Its value is between 0 and 100, coded over 7 bits.

## Slide 8: Conclusion
This contribution offers new service opportunities and is timely, as the EU Energy Efficiency Directive [1] identifies the Information & Communication Technology (ICT) sector as an energy hungry sector (responsible for 5 to 9 % of the world’s total electricity use and more than 2 % of global emissions).
It is suggested to include this new purpose in the VSEI specification.
[1] https://energy.ec.europa.eu/topics/energy-efficiency/energy-efficiency-targets-directive-and-rules/energy-efficiency-directive_en