## Slide 1: JVET – AH0147/ AH0149
Weilan Chen, Zehui Lin, Yuxin Zhao, Kangying Cai
Elena Alshina, Johannes Sauer, Zhao Yin
Huawei Technologies

## Slide 2: JVET – AH0147
Auxiliary Information along with gaming sequences:
  Depth (32-bits float, encoded)
  Motion Vector (two channels, 32-bits float)
  Camera Information (multiple 4x4 float array)

## Slide 3: JVET – AH0147 & AH0149
Propose 6 sequences from 3 games
Each game: HDR – 1080P – 60fps – 300frame & HDR – 4K – 60fps – 300frames
Test:
4K: VTM-11ecm12 and ECM-12.0, for AI, RA
HD: VTM-11ecm12 and ECM-12.0, for AI, RA, LDB, LDP
Pipeline
Deferred Shading Renderer
RGBAFloat16
Unreal Engine
*.bin
*.yuv
RGBAFloat16
YUV420P10le
ACES 1000-nit ST-2084 (PQ)
*.MP4
MP4
ffmpeg
ffmpeg
Customized
Shader code
Color Primaries: BT.2020
Transfer Characteristics: ACES 1000-nit ST-2084 (PQ)
Matrix Coefficients: BT.2020 non constant
Color Range: limited
Customized
Shader code
Depth: float32, 0.0~1.0
MV: two-channel float32
Camera Information: 4x4 float32 arrays

## Slide 4: JVET – AH0147
Encoded depth
, , c = 0
*From Unreal Engine Implementation
Z – linear depth in the world coordinate; - encoded depth in the normalized device coordinate (-1.0, 1.0)
is the far plane, is the near plane
Target: to accommodate more game engines.

## Slide 5: JVET – AH0147

## Slide 6: JVET – AH0147
Why use encoded depth?
stored in GBuffer is naturally available in the rendering process of game engines.
The reciprocal of Z is already available once hardware finish the perspective division in perspective projection process.
1/z is linear in screen space which is beneficial for the interpolation of across a triangle in rasterization process.
Z might overfloats float32.
Depth Precision Visualized | NVIDIA Developer

## Slide 7: JVET – AH0147
Motion Vector
  Two channels, 32-bits float, (X, Y) – A pixel in current frame, (X’, Y’) – The corresponding position of (X, Y) in the previous frame.
Camera Information
4x4 float32 array