## Slide 1: JVET-AH0179 AhG15: On auxiliary information for the Unity Gaming sequences
S. Thiebaud, S. Puri, T. Poirier, F. Galpin

## Slide 2: Proposal to add auxiliary information to Unity sequences
DarkTree screenshot
Level-1 screenshot
2 Unity sequences have been proposed as gaming sequences (JVET-AF0253)
It is proposed to add auxiliary information to these sequences

## Slide 3: Auxiliary information for the Unity Gaming sequences
[WorldToCam]
Pw(Xw,Yw,Zw)
Image
Pi(xi,yi,ziNDC)
Depth Z
Camera
coordinate system
[Projection]
Pc(Xc,Yc,Zc)
3D world
coordinate system
Znear, Zfar,
FocalLength…
« Camera parameters » as auxiliary information
  « WorldToCamera » matrix
  « Projection » matrix
  Unity camera parameters such as :
    Znear, Zfar, FocalLength, …
  Stored in a text file, a Json object per frame
Maps as auxiliary information
  Non linear ZBufUnity Depth map coding the Depth Z:
  Motion vectors in floating point, one MV per pixel
  Stored in EXR files, one file per frame
    R = Depth, G = MV.hor, B = MV.ver
NDC : Normalized Device Coordinate
ZNDC = 2ZBuf - 1

## Slide 4: Annex 1 : exemple of camera parameters file
Version 0.0 - projectionMatrix, worldToCameraMatrix, farClipPlane, nearClipPlane, focalLength
{"frame":0,
"projectionMatrix":{ "e00":1.080,"e01":0.0,"e02":0.0,"e03":0.0,
"e10":0.0,"e11":1.920,"e12":0.0,"e13":0.0,
"e20":0.0,"e21":0.0,"e22":-1.000,"e23":0.600,
"e30":0.0,"e31":0.0,"e32":1.0,"e33":0.0},
"worldToCameraMatrix":{ "e00":0.991,"e01":0.085,"e02":0.101,"e03":11.727,
"e10":-0.101,"e11":0.981,"e12":0.164,"e13":-42.399,
"e20":0.085,"e21":0.173,"e22":-0.981,"e23":10.997,
"e30":0.0,"e31":0.0,"e32":0.0,"e33":1.0},
"farClipPlane":1500.0, "nearClipPlane":0.300, "focalLength":23.051
}
…
{"frame":n,
"projectionMatrix":{ "e00":1.080,"e01":0.0,"e02":0.0,"e03":0.0,
"e10":0.0,"e11":1.92,"e12":0.0,"e13":0.0,
…

## Slide 5: Annex 2 : example of Depth and Motion vectors
YUV texture
Depth & Motion vectors in EXR files
Depth in red channel
MV.hor in green channel
MV.ver in blue channel

## Slide 6: Annex 3 : Game engine camera
Xcam
Ycam
Zcam
Camera
coordinate system
3D world
coordinate system
Far plane
Near plane
ZF
ZN
Viewing volume
Viewing volume in Normalized Device Coordinates NDC
(-1,-1,-1)
(1,1,1)
NDC mapping