## Slide 1: Non-EE2: Disabling the combination of TIMD-ISP and TIMD-MRL
Sharp Corporation
Zheming Fan
Takeshi Chujoh Tomohiro Ikai
JVET-AI0080

## Slide 2: Proposal (test1)
This proposal suggests disabling the combination of TIMD and ISP (TIMD-ISP), and the combination of TIMD and MRL (TIMD-MRL) in the current ECM.
0.03% luma loss for 3% EncT reduction.
Come from reducing RDO tests in encoder.
When timd_flag is true, no further encoding or decoding operations will be performed on the corresponding flags for ISP and MRL.
Copyright © All rights reserved, SHARP CORPORATION
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | 0.01% | 0.04% | 0.15% | 97.5% | 100.3% | 99.0% | 100.1%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class B | 0.03% | -0.06% | -0.13% | 97.3% | 100.0% | 104.7% | 100.0%
Class C | 0.05% | -0.02% | 0.08% | 97.3% | 100.3% | 98.5% | 100.0%
Class E | 0.03% | 0.03% | 0.00% | 97.4% | 99.7% | 99.8% | 100.0%
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class D | 0.06% | -0.03% | -0.26% | 97.7% | 99.4% | 100.0% | 100.0%
Class F | -0.01% | 0.08% | 0.16% | 98.0% | 99.8% | 99.6% | 99.9%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class B | 0.02% | 0.02% | -0.09% | 99.8% | 100.3% | 100.0% | 100.9%
Class C | 0.01% | 0.06% | 0.07% | 99.8% | 100.4% | 100.4% | 100.9%
Class E |  |  |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class D | 0.02% | 0.10% | -0.11% | 99.7% | 100.2% | 99.9% | 100.9%
Class F | 0.03% | 0.06% | -0.45% | 99.8% | 100.1% | 100.1% | 100.9%

## Slide 3: Proposal (test2)
In test1, the number of RDO required in the encoder is reduced. Based on test1, test2 suggests using other intra modes to replace TIMD-ISP and TIMD-MREF in the RDO list.
0.07% luma gain without change EncT and DecT.
Gain come from using good candidates to replace bad candidates in rdo_list.
Averagely the number of rdo tests remain same.
Copyright © All rights reserved, SHARP CORPORATION
 | All Intra Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | -0.03% | -0.03% | 0.00% | 100.3% | 100.2% | 99.7% | 100.0%
Class A2 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class B | -0.06% | -0.04% | -0.04% | 100.4% | 100.2% | 99.2% | 100.0%
Class C | -0.09% | 0.02% | 0.07% | 100.6% | 100.0% | 98.5% | 100.0%
Class E | -0.09% | -0.08% | -0.13% | 100.4% | 100.3% | 100.7% | 100.0%
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class D | -0.11% | 0.02% | -0.10% | 101.4% | 99.1% | 100.0% | 100.0%
Class F | -0.06% | -0.10% | -0.06% | 100.5% | 100.7% | 102.0% | 100.0%
 | Random Access Main 10 |  |  |  |  |  | 
 | Over ECM-13.0 |  |  |  |  |  | 
 | Y | U | V | EncT | DecT | EncVmPeak | DecVmPeak
Class A1 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class A2 | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class B | -0.03% | -0.06% | -0.06% | 100.3% | 100.5% | 99.9% | 101.5%
Class C | -0.01% | 0.10% | 0.20% | 99.7% | 99.8% | 100.0% | 101.5%
Class E |  |  |  |  |  |  | 
Overall | #VALUE! | #VALUE! | #VALUE! | #DIV/0! | #DIV/0! | #DIV/0! | #DIV/0!
Class D | 0.03% | -0.24% | 0.00% | 99.9% | 100.4% | 100.0% | 101.5%
Class F | -0.02% | 0.09% | -0.05% | 99.7% | 100.0% | 100.1% | 101.5%

## Slide 4: Proposal (test2: rdo list generation)
 | ECM13 |  |  | Proposal (test2) | 
Adding method | rdoListNum | intraTools |  | rdoListNum | intraTools
update() | 3 + n (n is determined by mip) |  |  | 3 + k + n (n is determined by mip) | 
 |  | Angular mode, planar(Hor,Ver), Angular mode+-1, TMRL, intraTMP, MIP, |  |  | Angular mode, planar(Hor,Ver), Angular mode+-1, TMRL, intraTMP, MIP,
 | u (derives by reduceHadCandList) |  |  | u + k (derives by reduceHadCandList) | 
 |  | SGPM, EIP |  |  | SGPM, EIP
Push_back() | u+2 | mpm |  | u + k +2 | mpm
 | u+2+1+1 | DIMD, OBIC |  | u + k +2+1+1 | DIMD, OBIC
 | u+2+1+1+1 | TIMD |  | u + k +2+1+1+1 | TIMD
 | u+2+1+1+1+k | Combinations (timd and isp, timd and mrl) |  | u+2+1+1+1+k | Combinations (timd and isp, timd and mrl)
 | u+2+1+1+1+k+I (u+5+k+I) | ISP |  | u+ k +2+1+1+1+I (u+k+5+I) | ISP
Reducing k
candidates
in rdo list
Adding k
candidates
in rdo list
Remain same
Rdo tests
Copyright © All rights reserved, SHARP CORPORATION

## Slide 5: Conclusion
This proposal includes two tests:
Test 1:
XX XX XX XX XX in AI , XX XX XX XX XX in RA.
By disabling two TIMD-related combinations to achieve a reduction in encoding time, the average result is a 0.03% luma loss for a 3% EncT reduction.
Test 2:
XX XX XX XX XX in AI , XX XX XX XX XX in RA.
Based on Test 1, using other intra modes to replace TIMD-ISP and TIMD-MREF in the RDO list, the result is a 0.07% luma gain without changing EncT and DecT.
Thanks oppo for crosschecking.
Copyright © All rights reserved, SHARP CORPORATION

## Slide 6
Copyright © All rights reserved, SHARP CORPORATION